## Slide 1: 3.10: Attacks on the link layer
김효곤

## Slide 2: Early Ethernet
In Ethernet, interfaces can be placed in promiscuous mode, which allows them to receive traffic even if it is not destined for them
  Early Ethernet was a shared cable, which allowed anyone to “sniff” anybody else’s frames and inspect their contents
  For many higher-layer protocols, it was trivial to intercept a person’s password by merely looking at the ASCII decode of a packet trace
Two factors have affected this approach substantially
  Switches
  Encryption in higher-layer protocols
With switches, the only traffic that is visible is traffic destined for the station itself (or others for which it is bridging) and multicast (broadcast) traffic
  This type of traffic rarely contains information such as passwords, the attack is largely thwarted
Encryption at higher layers is now common and more effective
  Sniffing packets leads to little benefit as the contents are essentially impossible to read

## Slide 3: Switches
Switches hold tables of stations on a per-port basis
If the attacker fill the tables quickly, the switch might be forced into discarding legitimate entries, leading to service interruption for legitimate stations
  E.g. by quickly masquerading as a large number of stations
A related but probably worse attack can be mounted using the STP
  An attacker can masquerade as a switch with a low-cost path to the root bridge and cause traffic to be directed toward it

## Slide 4: Wi-Fi
Eavesdropping and masquerading issues present in wired Ethernet networks are exacerbated, as any station can enter a monitoring mode and sniff packets from the air
  Although placing an 802.11 interface into monitoring mode tends to be more challenging than placing an Ethernet interface into promiscuous mode, as doing so depends on an appropriate device driver
Some of the earliest “attacks” involved simply roaming about while scanning, looking for access points providing Internet connectivity (i.e., war driving)
Although many access points use encryption to limit access to authorized users, others are either open or use so-called capturing portals that direct a would-be user to a registration Web page and then filter access based on MAC address
  Capturing portal systems have been subverted by observing a station as it registers and “hijacking” the connection as it is formed by impersonating the legitimate registering user

## Slide 5: Wi-Fi
A more sophisticated set of attacks on Wi-Fi involves attacking the cryptographic protection, especially the WEP encryption used on many early access points
Attacks on WEP were sufficiently devastating so as to prod the IEEE into revising the standard
The more recent WPA2 encryption framework (and WPA, to a lesser extent) is known to be significantly stronger, and WEP is no longer recommended for use

## Slide 6: PPP
PPP links can be attacked in a number of ways if the attacker can gain access to the channel between the two peers
For very simple authentication mechanisms (e.g., PAP), sniffing can be used to capture the password in order to facilitate illegitimate subsequent use
Depending on the type of higher-layer traffic being carried over the PPP link (e.g., routing traffic), additional unwanted behaviors can be induced

## Slide 7: Tunneling
Tunneling can be both target and tool
  In terms of a target, tunnels pass through a network (often the Internet) and thus are subject to being intercepted and analyzed
  The configured tunnel endpoints can also be attacked, either by attempting to establish more tunnels than the endpoint can support (a DoS attack) or by attacking the configuration itself
If the configuration is compromised, it may be possible to open an unauthorized tunnel to an endpoint
  At this point the tunnel becomes a tool rather than a target, and protocols such as L2TP can provide a convenient protocol independent method of gaining access to private internal networks at the link layer
  E.g. in GRE, traffic can simply be inserted in a non-encrypted tunnel, where it appears at the tunnel endpoint and is injected to the attached “private” network as though it were sent locally