## Slide 1: TCP
13강

## Slide 2: Transmission Control Protocol
Most frequently used transport layer protocol
  The most complex Internet protocol
Service model and characteristics
  Connection-oriented
  Reliable
  In-order delivery
  Full-duplex

## Slide 3: TCP service model
Connection-oriented: data exchange possible only after “connection” is set up
Reliable: retransmission will be done if data packet is not acknowledged
In-order delivery: in the order the user process provided
Full-duplex: two data channels are open in one connection

## Slide 4: TCP
TCP sees user data as a stream of bytes
  No predetermined boundaries
  Segmentation is performed by TCP
    Each packet is called “segment”
Segment size can be adjusted by PMTU discovery
  ICMP notifies TCP if ICMP error (packet too big but DF set) arrives
Maximum segment size (MSS) = MTU - 40

## Slide 5: TCP
TCP header format = 20 bytes + options (max 40 bytes)
  Source port, dest port
  Sequence number
  Ack number
  Header length (In units of 4 bytes)
  8 flags
  Window size
  Checksum
  Urgent pointer
  Options

## Slide 6: Sequence number
Each byte has one 32-bit number
SYN and FIN segments consume a sequence number
“Randomly chosen”
  So that no one can guess
  Security reason
    Hijacking possible if the choice is guessed
The first byte in each segment

## Slide 7: Acknowledgement number
If x is ACK number, it means
  The receiver has up to (x-1) bytes, so expects x next
  X-1 is the sequence number of the last consecutive bytes the receiver has got
TCP sender can flush up to (x-1) in the sending socket buffer upon ACK(x)

## Slide 8: Header length
Like in IP
Basic TCP header is 20 bytes
  “5”
  Options can come after this
  TCP options are very useful

## Slide 9: Flags
CWR, ECE: congestion control use
URG: urgent pointer, means there are urgent bytes came into the byte stream
ACK: always on except in the first SYN segment
PSH: “push”, today it only means that there is no data byte in the sending socket buffer after this segment (i.e. not functional)

## Slide 10: Flags
RST: “reset”, kills the TCP connection
  Not really a reset (going back to the initial state)
SYN: “synchronize” 3 pieces of information to establish the connection
  Later in connection set up
FIN: “finish”
  Hangs up the connection in a graceful manner

## Slide 11: Window size
Actually it is the available receive socket buffer space
  For flow control
Must be interpreted with respect to the ACK number
  E.g. 3500 bytes from ACK number 12780

## Slide 12: TCP checksum
The Internet checksum
Covers the entire TCP segment
  Header
  Body
As in UDP, uses “pseudo-header”
Mandatory in TCP

## Slide 13: Urgent pointer
Points at the last byte of the urgent data in the byte stream
  Offset to the position
In TCP, urgent data cannot preempt preceding normal data
  They should be served in the same way as other normal bytes
TCP does not know what kind of urgent data it is; it just knows it’s urgent

## Slide 14: TCP connection management
Connection is an abstract notion
Connection established means that the two TCP endpoints agreed on:
  Maximum Segment Size (MSS) to use
  Initial Sequence Number (ISN)
  Window Size
The agreement should be made for each data channel

## Slide 15: 3-way handshake
To set up the connection, 3 segments are exchanged
  1. SYN()
  2. ACK() + SYN()
  3. ACK()
After step 2, data channel in  direction becomes usable
After step 3, two data channels are usable

## Slide 16: SYN
The SYN segment carries all 3 pieces of information that should be agreed on
  ISN: in “sequence number” field of the SYN
  MSS: in the option field
  Window size: in the “window size” field
The ISN is NOT taken by the first data byte; it is used by the SYN segment itself

## Slide 17: ACK
The ACK(x) acknowledges the reception into the receive socket buffer up to (x-1)
Once in the receive socket buffer, the receiver side application can use it
Cumulative ACK
  Acknowledges only consecutive last byte
  E.g. For 0~1459, 1460~2919, (missing), 4380~5839, the ACK number is 1460, 2920, 2920
  Robust against ACK losses

## Slide 18: FIN
When tearing down a TCP connection, FIN segment can be used
This time, it is 4-way handshake
  1. FIN()
  2. ACK()
  3. FIN()
  4. ACK()
After step 2, data channel () is torn down
After step 4, data channel () is torn down

## Slide 19: Half-close
One of the two data channels is gone
TCP can keep working in one direction; it is called “half close”
Note that half close is not “half open”
  Half open is an abnormal state where only one end of TCP thinks the connection is still on; the other has been killed (e.g. by power off of the computer)

## Slide 20: Sequence number
Wireshark shows the relative seq. no.
  “0”= ISN, “x”=ISN+x

## Slide 21: Timeout of connection establishment
Your computer can be configured to give up the connection set up after k tries of sending SYN
  No ACK for the SYN
If your browser takes too long for connecting to the web site, sometimes it’s the retries
  Exponential: e.g. gaps between tries: 3s, 6s, 12s  3s, 9s, 21s of elapsed time
  Just hit reload if you experience this

## Slide 22: MSS
The same MSS gets to be used by the two data channels
  The minimum of two: e.g. if () is 576 bytes and () is 1460, it should be 576
  This is to avoid fragmentation

## Slide 23: Selective ACK (SACK) option
When the connection is set up, your computer can want to use SACK
  In addition to the cumulative ACK using the “acknowledgement number” field
  The SACK option can tell the sender what non-consecutive blocks it received
    This information is not available in the TCP header unless SACK is used
  TCP sender does not have to retransmit them
Most modern computers use SACK

## Slide 24: Window scale option
Originally a 16 bit field in the basic TCP header
What if you have more than 65535 bytes of receive socket buffer?
  Specify it using the WSCALE option
  It gives you the left-shift count
  E.g. “4” = 16x, “3” = 8x
  E.g. window size = 1K, shift count = 8  actual window size = 1K * 2^8 = 256K

## Slide 25: Timestamp option
TCP measures RTT once every RTT
Can increase the frequency of measurement
  Every RTT  every packet
Measurement is in the units of 500ms
  It does not make the measurement more precise than this; but it makes the average more solid

## Slide 26: Path MTU discovery
When ICMP tells TCP that the current MSS size caused fragmentation, it uses one smaller segment size
  There is an ordered list of sizes to try

## Slide 27: TCP state machine
Fig. 13-8
Normally, follow the thick sold arrows
Data exchange happens in ESTABLISHED
TIME_WAIT is special
  It’s because the last ACK is not acknowledged in TCP connection tear down
  Has to wait lest there should be a retransmission of FIN from the other side because my ACK has been lost

## Slide 28: Use of Reset
If there is no process at the destination port number, send RST
  C.f. In UDP, ICMP port unreachable is sent
If one wants to finish the connection without the costly TIME_WAIT state, send RST
  Some servers do this
  TIME_WAIT can be long, e.g. 2 minutes