## Slide 1: Dynamic Host Configuration Protocol (DHCP)
6강

## Slide 2: Lineage
Reverse ARP  BOOTP  DHCP
RARP for obtaining IP address only, for diskless workstations
Then use IP networking to contact servers for booting
Remaining bootstrap process required other protocols
  To fetch OS image, etc.

## Slide 3: RARP
Use hard-wired MAC address + PROM program to bootstrap
Broadcast (ff-ff-ff-ff-ff-ff) RARP request : “what’s my IP?”
RARP server responds to the request

## Slide 4: RARP message format
Looks very familiar, doesn’t it?
  It’s a member of the *ARP family
  Ethertype = 80-35 (cf. ARP  08-06)
  OP: 3=request, 4=reply

## Slide 5: Limitations of RARP
Not nearly enough for a full-fledged “auto-configuration” protocol
  Needed other protocols to finish bootstrapping
  Needed 1 RARP server per each subnet
  Implemented as a “hack”: device driver  application (skipping network/transport layers)

## Slide 6: BOOTP
More complete protocol for the entire bootstrapping process (not only IP!)
Overcomes limitations of RARP: 1, 2, 3
Very similar to DHCP
  So we will go directly to DHCP
  Some differences: we will discuss them, too

## Slide 7: What to configure?
Many things --- DHCP can configure close to 200 different things on a host
  http://www.iana.org/assignments/bootp-dhcp-parameters/bootp-dhcp-parameters.xml
IP address, router address, domain name server address, subnet mask, service gateways, ARP cache timeou, location of the bootstrapping files, etc, etc, etc.

## Slide 8: DHCP relay
Enables “remote configuration”
Modern configuration typically uses relays
  Between clients and the remote DHCP server(s)
  Routers are typically configured as relays: they have the IP address of the DHCP server

## Slide 9: DHCP relay
Doesn’t need so many servers anymore
DHCP server can be anywhere, to which the request is forwarded in unicast
  No limitations of broadcast

## Slide 10: “Normal” protocol
Uses UDP (server=67, client=68)
No kernel hacking
Link layer
IP
UDP
DHCP
Auto-configuration

## Slide 11: DHCP
The most frequently used application layer protocol along with DNS (most users don’t know)
Client/server protocol
Evolved from BOOTP
  Which in turn evolved from RARP
Most noticeable change: “lease”

## Slide 12: Why UDP for transport?
Maybe it’s because DHCP exchanges a small number of messages between client and server
But more fundamentally it’s because DHCP requests are IP broadcast (and some replies as well) to 255.255.255.255

## Slide 13: Message format
Fig. 6-1
  Smells of ARP? It should.
Use “bootp” filter in Wireshark

## Slide 15: Message format
OP code: 1=request, 0=reply
Htype, hlen: same as in ARP/RARP
Hops: # of times relay agents have relayed the message
  If > 16, kill it, it’s probably a loop
Transaction ID: to match requests and replies
  Out-of-order delivery in IP network
  All application layer protocols using UDP transport uses similar mechanism

## Slide 16: Message format
B=1 bit in flags field means that the client doesn’t have (know) its IP address
  Server broadcasts the reply
CIAddr: 0.0.0.0 when the client doesn’t know
YIAddr: IP address the server is assigning the client
SIAddr: address of the server that the client should use next in the bootstrap process != DHCP server address
  DHCP server address is in the options part

## Slide 17: Message format
GIAddr: relay agent address
CHAddr: client’s MAC address, used as key
Sname: server can optionally tell the client its name
Boot filename: optionally used by a client to request a particular type of a boot file in a DHCPDISCOVER message
  Used by server in DHCPOFFER to fully specify file name

## Slide 18: Message format
Options in TLV format
  Magic cookie: originally “OREO” but J. Postel changed it to the current value

## Slide 19: Options
Essential in DHCP
IP host parameters, IP interface parameters, link layer parameters, TCP parameters, app/service parameters, DHCP extensions

## Slide 20: Options – DHCP extensions
50 – requested IP address
51 – ip address lease time
53 – DHCP message type* (not really optional)
54 – server identifier
55 – parameter request list
58 – renewal time
59 – rebinding time
61 – client identifier

## Slide 21: DHCP options
Message type option is important
  DISCOVER, REQUEST, ACK, NACK, INFORM

## Slide 22: DHCP FSM

## Slide 23: Lease
Address assignment with contracted duration
Duration depends on how much addresses are in need
Renew (T1) vs. Rebind (T2)
Try renew it by ‘ipconfig /renew’
Try release IP by ‘ipconfig /release’

## Slide 24: Lease

## Slide 25: Lease

## Slide 26: Lease

## Slide 27: DAD by client

## Slide 28: DHCP server conflict detection
Multiple servers, overlapping IP address pools
Before DHCPOFFER, ping the address to assign

## Slide 29: Autoconfiguration
Plug and play
Two kinds of autoconfiguration in IPv4
  Stateful  DHCP
  Stateless  Automatic Private IP Addressing (APIPA; by Microsoft) uses 169.254.0.0/16 when DHCP fails

## Slide 30: APIPA