## Slide 1: UDP
10강

## Slide 2: User Datagram Protocol
Transport layer protocol with low overhead
UDP has the datagram model
  No stream
3 Uses of UDP
  Non-unicast
  Real-time
  Short transactions

## Slide 3: UDP
Does little more than what IP does
  Delivery between interface and process
  Port number is the “address” it uses
UDP format (Fig. 10-2)
  Simple: 2 port numbers, length (header+payload), checksum (usual Internet checksum)

## Slide 4: UDP header
Port number
  Associated with a process (running program)
    If no association is found, ICMP Port Unreachable is returned to the source by UDP
    In TCP, it is Reset flag that is returned, not the ICMP error
  Required to find the process
    Remember ICMP error carries the starting part of the dead IP datagram? Now you know why.

## Slide 5: UDP header
Length field is not really unique
  Can infer the UDP length from the two lengths in the IP header
    Total length – 4*header length
  Both layer headers are accessible because up to transport layer the kernel implements

## Slide 6: UDP checksum
Covers entire UDP datagram including the header
  Optional in IPv4, mandatory in IPv6
    If not used, 0x0000
    If used but computed to be 0x0000, change to 0xffff
    Both are zeros in 1’s complement notation
  Either both ends use it or both don’t use it
  Currently on by default

## Slide 7: UDP checksum
Uses “pseudo-header” in checksum computation
  Also checks if delivered to the right IP address etc.

## Slide 8: UDP and IP fragmentation
UDP simply attaches the 8B header to whatever comes down from the user
  And make it into a “datagram”
  Doesn’t perform any segmentation
So IP sometimes gets to fragment the datagram that contains UDP
  Fig. 10-9