## Slide 1: TCP timeout and retransmission TCP interactive flow algorithms
14강

## Slide 2: TCP timeout
One of the two means of detecting a packet loss
  ACK not arriving until retransmission timeout (RTO)
RTO = avg(RTT)+4*std(RTT)
  Cf. Chevyshef inequality
  Avg RTT is a low-pass filter output of RTT graph
  Standard deviation is not used; actually mean deviation is used

## Slide 3: TCP timeout
RFC 2988 stipulates that max(1s, RTO) should be used
RTO vs. RTT: see Fig. 14-3

## Slide 4: Fast Retransmit
The second means of detecting packet loss
  3 consecutive duplicate ACKs
  E.g. 4320, 4320, 4320, 4320  trigger FR
It’s faster than timeout method

## Slide 5: Delayed ACK algorithm
TCP suppresses ACKs by default
  Uses 200ms timer to suppress
  Waits until a packet in the opposite direction starts
  It’s because the placeholders for the two pieces of ACK information (ACK number + window size) are in the opposite direction data packet anyway

## Slide 6: Delayed ACK algorithm
If 200ms timer expires while suppressing ACK, the ACK segment should go
  Such ACK segment has only header (no body carrying data in the opposite direction)
If window size (i.e. available receive socket buffer space) is newly made larger than 2MSS, suppression should end
  Let the TCP sender know that we can receive more! Let it send!

## Slide 7: Delayed ACK algorithm
Delayed ACK is on by default
If you turn it off (e.g. by editing registry on Windows), all TCP connections will have Delayed ACK off
Delayed ACK is to eliminate unnecessary ACK transmissions on the receiver side of a data channel
  It runs on either side

## Slide 8: Nagle’s algorithm
This is sender side story
We do not want to generate “small” segments
  Small = less than MSS: e.g. 1B, 1459B, etc.
If a small segment has to be sent, check if there is any outstanding small segment unacknowledged yet
  If so, wait until the ACK comes back

## Slide 9: Nagle’s algorithm
Gather bytes in the send socket buffer in the mean time
When the ACK for the prior small segment comes back, carry all the gathered bytes in one segment
  If more than MSS bytes are gathered in the send socket buffer, you can always send a full segment irrespective of Nagle

## Slide 10: Zero window ACK and persist timer
If the receive socket buffer is full, window size=0 is sent in the ACK
  This is a special condition, and the TCP sender notes it; run so called the “persist” timer
The only way to break the sender free is sending an ACK with window size != 0
  Then sender sends some data, gets an ACK, etc. etc.

## Slide 11: Zero window ACK
But what if the window advertisement ACK is lost?
  All packets are equal in the Internet; it can die
The sender is frozen
  As it thinks window size is still 0 as no ACK with WS!=0 arrives
The receiver has nothing to send more
  It already sent an ACK; no retransmission of ACK in TCP

## Slide 12: Zero window ACK
That’s why the sender runs the persist timer
If the timer expires, send a “probe” packet
  Carries at least 1 byte taken from the head of the send socket buffer (normal data)
  TCP always allows such 1 byte packet to be send beyond the window

## Slide 13: Zero window ACK
If there is some space in the receive socket buffer, the probe data will be received and ACKed
  Then the window opening ACK must have been lost indeed
  This will break the livelock and set the TCP running again
If the situation is the same, the receiver will send another zero window ACK

## Slide 14: Silly Window Syndrome
It doesn’t mean that SWS is actually happening in today’s Internet
SWS means the sender transmits “small” packets
Both the sender and the receiver have a preventive mechanism
  Sender: Nagle

## Slide 15: SWS avoidance
What does receiver do?
  It lies
  It lies about the available receive socket buffer size
  If it is less than 2MSS, it just says “0”
    Otherwise the sender will get a small opening, and to fill the opening, it will have to send a small packet
Note that the receiver mechanism is unnecessary if the Nagle is working fine at the sender or vice versa
  We do not trust the other guy…that’s our philosophy; do you?

## Slide 16: Keepalive timer
Not in the TCP spec
The server can check if the client is still there (“half-open” or not?)
  Because half-open only wastes server’s resource
Sends a “probe”, but this is different from the probe used in the persist timer
  Probe is an empty packet with an old sequence number (older than the client is expecting)
  Receiver immediately sends an ACK with a correct ACK number if it is alive!