## Slide 1: Section 2.5 : Special-Use Addresses
김우일
2015011157

## Slide 2: Special-Use Addresses
Both the IPv4 and IPv6 address spaces include a few address ranges that are used for special purposes.

## Slide 3: IPv4 special-use addresses
0.0.0.0/8
  Hosts on the local network.
10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16
  Address for private networks(intranets).
127.0.0.0/8
  Internet host loopback addresses(same computer).
169.254.0.0/16
  “Link Local” addresses
192.0.0.0/24
  IETF protocol assignments
192.0.2.0/24, 198.51.100.0/24, 203.0.113.0/24
  TEST-NET-1, 2, 3

## Slide 4: IPv4 special-use addresses
198.18.0.0/15
  Used for benchmarks and performance testing.
224.0.0.0/4
  IPv4 multicast addresses(formerly class D)
240.0.0.0/4
  Reserved space (formerly class E), except 255.255.255.255.
255.255.255.255/32
  Local network(limited) broadcast address.

## Slide 5: IPv6 special-use addresses
::/0
  Default route entry. Not used for addressing.
::/128
  The unspecified address; may be used as a source IP address.
::1/128
  The IPv6 host loopback address.
::ffff:0:0/96
  IPv4-mapped addresses.
::{ipv4-address}/96
  IPv4-compatible addresses.
2001::/32
  Teredo addresses.

## Slide 6: IPv6 special-use addresses
2001:10::/28
  Overlay Routable Cryptographic Hash Identifiers.
2001:db8::/32
  Address range used for documentation and for examples.
2002::/16
  6to4 addresses of 6to4 tunnel relays.
fc00::/7
  Unique, local unicast addresses.
fe80::/10
  Link-local unicast addresses.
ff00::/8
  IPv6 multicast addresses.

## Slide 7: 2.5.1 Addressing IPv4/IPv6 Translators
Use format called an IPv4-embedded IPv6 address
Contains an IPv4 address inside an IPv6 address.
Encoded using one of 6 formats, based on the length of the IPv6 prefix : 32, 40, 48, 56, 64, 96

## Slide 8: 2.5.2 Multicast Addresses
Multicast addressing is supported by IPv4 and IPv6.
IP multicast address(group address) identifies a group of host interfaces, rather than a single one.
Portion of the network a single group covers is known as the group’s scope.
ASM(any-source multicast)
  Any sender may send to any group. A receiver joins the group by specifying only the group address.
SSM(source-specific multicast)
  Uses only a single sender per group. To join a group, a host specifies the address of a channel, which comprises both a group address and a source IP address.

## Slide 9: 2.5.3 IPv4 Multicast Addresses
The class D space(224.0.0.0-239.255.255.255) has been reserved for multicast.
With 28 bits, this provides 228 host groups.
This address space is divided into major sections based on the allocating way and handling way in routing.
The blocks of addresses up to 224.255.255.255 are allocated for the exclusive use of certain application protocols or organizations.

## Slide 10: 2.5.3 IPv4 Multicast Addresses
224.0.0.0 – 224.0.0.255
  Local network control; not forwarded
224.0.1.0 – 224.0.1.255
  Internetwork control; forwarded normally
224.0.2.0 – 224.0.255.255
  Ad hoc block I
224.1.0.0 – 224.1.255.255
  Reserved
224.2.0.0 – 224.2.255.255
  SDP(Session Description Protocol) / SAP(Announcement)
224.3.0.0 – 224.4.255.255
  Ad hoc block II

## Slide 11: 2.5.3 IPv4 Multicast Addresses
224.5.0.0–231.255.255.255, 235.0.0.0–238.255.255.255
  Reserved
232.0.0.0. – 232.255.255.255
  Source-specific multicast (SSM)
233.0.0.0 – 233.251.255.255
  GLOP
233.252.0.0 – 233.255.255.255
  Ad hoc block III
234.0.0.0 – 234.255.255.255
  Unicast-prefix-based IPv4 multicast addresses
239.0.0.0 – 239.255.255.255
  Administrative scope

## Slide 12: 2.5.3 IPv4 Multicast Addresses
The most recent of the IPv4 multicast address allocation mechanisms associates a number of multicast addresses with an IPv4 unicast address prefix. This is called unicast-prefix-based multicast addressing(UBM).
To determine the set of UBM addresses associated with a unicast allocation, the allocated prefix is simply prepended with the 234/8 prefix.
Ex) Unicast IPv4 prefix 192.0.2.0/24 -> 234.192.0.2 Multicast 234.128.32.0/24 -> IPv4 128.32.0.0/16
234
(8 bit)
Unicast Prefix
(up to 24 bits)
Group ID
(up to 16 bits)
78
0
N
31
IPv4 UBM address format

## Slide 13: 2.5.4 IPv6 Multicast Addresses
The prefix ff00::/8 has been reserved for multicast addresses, and 112 bits are available for holding the group number. 2112 groups are possible.
The scope field is used to indicate a limit on the distribution of datagrams addressed to certain multicast addresses.
Flag bits
  0 : reserved
  R : contains rendezvous point
  P : uses unicast prefix
  T : transient
11111111
0 | R | P | T | | | | |
Group ID
(112 bits)
0
16
Base IPv6 multicast address format
Flag(4bit) + Scope(4bit)

## Slide 14: 2.5.4 IPv6 Multicast Addresses
Multicast address format is used when the P and R bit fields are set to 0.
Rendezvous point(RP): is the IP address of a router set up to handle multicast routing for one or more multicast groups.
11111111
0 | R | P | T | | | | |
Group ID
(112 bits)
0
16
Base IPv6 multicast address format
Flag(4bit) + Scope(4bit)

## Slide 15: 2.5.5 Anycast Addresses
A unicast IPv4 or IPv6 address that identifies a different host depending on where in the network it is used.
Anycast address refers not o a single host in the Internet, but to the ‘most appropriate’ or ‘closest’ single host.
ex) DNS server, 6to4 gateway encapsulating IPv6 traffic in IPv4 tunnels.