## Slide 1: The Design Philosophy of the DARPA Internet Protocols
D. Clark
ACM SIGCOMM Computer Communication Review Volume 18, Issue 4, 1988

## Slide 2: Introduction
After 15 years (in 1988)… it is sometimes difficult to determine the motivation and reasoning which led to the design of Internet protocol suite
In fact, the design philosophy has evolved considerably from the first proposal to the current standards, e.g.
  Idea of the datagram, or connectionless service
  Layering of the architecture into the IP and TCP layers
This paper discusses the original objectives of the Internet architecture, and the relation between these goals and the important features of the protocols

## Slide 3: Fundamental goal for Internet architecture
Multiplexed utilization of existing interconnected networks
  Connect together the original ARPANET with the ARPA packet radio network
  Local area network had not yet emerged
An alternative to interconnecting existing networks would have been to design a unified system
  Higher degree of integration, and thus better performance
  However, administrative boundaries of control
  Abandoned
The technique selected for multiplexing was packet switching
  Connected together using packet communications processors

## Slide 4: Second level goals (in order of importance/priority): defines architecture!
Internet communication must continue despite loss of networks or gateways (survivability – military context!)
The Internet must support multiple types of communications service
The Internet architecture must accommodate a variety of networks
The Internet architecture must permit distributed management of its resources
The Internet architecture must be cost effective
The Internet architecture must permit host attachment with a low level of effort
The resources used in the internet architecture must be accountable

## Slide 5: Survivability in face of failure
Continue without having to reestablish or reset the high level state of their conversation
  Only one failure, and it is total partition
Take state information and gather it at the endpoint of the net, at the entity which is utilizing the service of the network
  Stored in the intermediate packet switching nodes  should be replicated  distributed algorithms difficult to build: abandoned!
  Call this approach to reliability "fate-sharing”
  It is acceptable to lose the state information associated with an entity if, at the same time, the entity itself is lost

## Slide 6: Survivability in face of failure
Consequences of fate sharing approach to survivability
  Stateless packet switches  "datagram" network
  More trust is placed in the host machine
Survivability still second to the top level goal of interconnection of existing networks
  A more survivable technology might have resulted from a single multi media network design

## Slide 7: Types of service
Speed, latency and reliability
Bi-directional reliable delivery of data was the first service provided in the Internet architecture, using the Transmission Control Protocol (TCP)
Services that TCP could not support well
  Debugging
  Real-time delivery (e.g. in teleconferencing)
    Most serious source of delay in networks is the mechanism to provide reliable delivery
    Very easy to cope with an occasional missing packet
More than one transport service would be required!

## Slide 8: Types of service
This goal caused TCP and IP, which originally had been a single protocol in the architecture, to be separated into two layers
User Datagram Protocol (UDP) was created to provide a application level interface to the basic datagram service of Internet

## Slide 9: Varieties of networks
Incorporate and utilize ARPANET itself, X.25 networks, local area nets (e.g. Ethernet), broadcast satellite nets, packet radio networks, serial links (1200bps ~ 1.5Mbps), inter-computer buses, etc.
Internet architecture achieves this flexibility by making a minimum set of assumptions about the function which the net will provide
  Network can transport a packet or datagram
  Packet must be of reasonable size, perhaps 100 bytes minimum
  Delivered with reasonable but not perfect reliability
  Network must have some suitable form of addressing if it is more than a point to point link

## Slide 10: Varieties of networks
Services which are explicitly not assumed from the network
  Reliable or sequenced delivery
  Network level broadcast or multicast
  Priority ranking of transmitted packet
  Support for multiple types of service, and internal knowledge of failures, speeds, or delays
Undesirable approach, because these services would have to be re-engineered and reimplemented for every single network and every single host interface to every network
  Instead, engineer these services at the transport

## Slide 11: Other goals
The remaining goals, because they were lower in importance, were perhaps less effectively met, or not so completely engineered
  e.g. does not produce as cost effective a utilization of expensive communication resources as a more tailored architecture would
    Headers of Internet packets are fairly long (a typical header is 40 bytes)
    Since lost packets are not recovered at the network level, it may be necessary to retransmit a lost packet from one end of the Internet to the other

## Slide 12: Datagrams
Datagrams as the entity which is transported across the underlying networks
  Eliminate the need for connection state within the intermediate switching nodes
    Internet can be reconstituted after a failure without concern about state
  Provides a basic building block out of which a variety of types of service can be implemented
    Provides a more elemental service which the endpoints can combine as appropriate to build the type of service needed
  Represents the minimum network service assumption
    Permits a wide variety of networks to be incorporated into various Internet realizations
The decision to use the datagram was an extremely successful one, which allowed the Internet to meet its most important goals very successfully

## Slide 13: TCP
Bytes not packets for flow control
  Original ARPAnet had both bytes and packets: abandoned
    To allow control in sequence space (later dropped as well)
  To permit TCP packet to be broken up into smaller packets to fit through a net with a small packet size
  To permit small packets to be gathered into one larger packet for retransmission
    Turned out to be critical
    Single character interactions that slow hosts could not process
Lost “message” (or “record”) semantics
  Records = separate packets
  Replaced by PUSH flag