## Slide 1: Section 2.2: Expressing IP Addresses
유재정
2015010642

## Slide 2: IPv4 – Dotted-Quad notation
Dotted-Quad notation
  A simple way of representing the whole IPv4 address
  Consists of four decimal numbers separated by ‘.’ (dot)
    Ex) 163.152.161.122
  Each number is nonnegative integer in the range (0~255)
    Ex) 0.0.0.0 ~ 255.255.255.255
Dotted-Quad Representation | Binary Representation
0.0.0.0 | 00000000 00000000 00000000 00000000
1.2.3.4 | 00000001 00000010 00000011 00000100
10.0.0.255 | 00001010 00000000 00000000 11111111
163.152.161.122 | 10100011 10011000 10100001 01111010
255.255.255.255 | 11111111 11111111 11111111 11111111

## Slide 3: IPv6 – Hexadecimal notation
Hexadecimal notation
  A series of four hexadecimal numbers separated by ‘:’ (colon)
  IPv6 address containing eight blocks
    Ex) 5f05:2000:80ad:5800:0058:0800:2023:1d71
  Not familiar to users, need standardized simplifications
Agreed-upon simplifications
  Leading zeros of a block need not be written
    Ex) 5f05:2000:80ad:5800:58:800:2023:1d71
  Block of all zeros can be omitted and replaced by ‘::’
    Ex) 0:0:0:0:0:0:0:1 -> ::1
    Ex) 2001:0db8:0:0:0:0:0:2 -> 2001:db8::2

## Slide 4: IPv6 – Hexadecimal notation
Agreed-upon simplifications
  Embedded IPv4 addresses represented in the IPv6 format can use a form of hybrid notation called an ‘IPv4-mapped IPv6 address’
    The block which consists of ‘ffff’ can be placed at left block of the IPv4
    Ex) 163.152.161.122 (IPv4) -> ::ffff:163.152.161.122 (IPv6)
  Low-order 32bits of the IPv6 address can be written using dotted-quad notation called an ‘IPv4-compatible IPv6 address’
    Ex) ::0102:f001 -> ::1.2.240.1
    Note that IPv4-compatible address is not the same as IPv4 mapped address

## Slide 5: IPv6 – URL containing an address
URL containing an address
  When expressing a URL, the ‘:’(colon) delimiter in an IPv6 address may be confused with another separator
    Ex) http://2001:0db8:85a3:08d3:1319:8a2e:0370:7344:443
    Which one is IPv6 address and port number?
  In above case, when expressing URL, ‘[‘,’]’ (bracket characters) are used to surround the IPv6 addresss
    Ex) http://[2001:0db8:85a3:08d3:1319:8a2e:0370:7344]:443