## Slide 1
Chapter 10 addendum
Cyclic Codes: The Proofs
Why the codeword divides, why x + 1 catches odd errors, how bursts slip through
Addendum to Forouzan, Data Communications and Networking, 5th ed., 10.3.3 and 10.3.4
1. c(x) = xr d(x) + r(x) is a multiple of g(x)
2. A factor x + 1 in g(x) catches every odd number of errors
3. Bursts: L ≤ r always caught, L = r + 1 missed with probability (1/2)r−1, longer with (1/2)r
Every number checked by computation: factorizations and exhaustive burst counts

## Slide 2
10.3.3
Proof: the codeword is a multiple of g(x)
Given: d(x), generator g(x) of degree r, coefficients in GF(2)
Step 1, division algorithm: xr d(x) = q(x) g(x) + r(x), deg r(x) < r
Step 2, add r(x) to both sides: xr d(x) + r(x) = q(x) g(x) + r(x) + r(x)
Step 3, GF(2): r(x) + r(x) = 0, since 1 + 1 = 0
Result: c(x) = xr d(x) + r(x) = q(x) g(x), remainder 0. QED
Book 10.3.4: "by definition of codeword": a theorem, not a definition
dataword, k = 4
r = 3 zeros
x3 d(x)
1
0
0
1
0
0
0
+ r(x)
1
1
0
= c(x)
1
0
0
1
1
1
0
1001 followed by 3 empty bits
remainder of 1001000 ÷ 1011
= (x3 + x)(x3 + x + 1)
deg r(x) < r: r(x) lands in the zeros, no carries, data bits untouched
adding = subtracting in GF(2): the remainder is removed, so g(x) divides c(x)
New Appending the remainder, dataword 1001, g(x) = 1011
2

## Slide 3
10.3.4
Worked check, and why it matters
d(x) = x3 + 1, g(x) = x3 + x + 1
x3 d(x) = x6 + x3 → 1001000
q(x) = x3 + x, r(x) = x2 + x (110)
c(x) = 1001110 = g(x) q(x), two x4 terms cancel
Receiver: 1001110 ÷ 1011 → remainder 000
Remainder is linear: rem(a + b) = rem(a) + rem(b)
Undetected error: exactly when g(x) divides e(x), whatever the data
c(x) = q(x) g(x)
÷ g(x)
remainder 0
e(x), the error
÷ g(x)
rem[e(x) / g(x)]
c(x) + e(x), received
÷ g(x)
0 + rem[e(x) / g(x)] = s(x)
remainders add in GF(2): the data part contributes 0 to s(x)
New The syndrome ignores the data
3

## Slide 4
Lemma
Evaluating a polynomial at x = 1
f(1) = number of terms mod 2
x5 + x2 + 1 → 1 + 1 + 1 = 1
x3 + x → 1 + 1 = 0
Evaluation respects products: (f h)(1) = f(1) h(1)
Factor theorem: (x + 1) | f(x) iff f(1) = 0
Divide: f(x) = (x + 1) q(x) + c, c a constant
x = 1: f(1) = 0 · q(1) + c = c
So every multiple of x + 1 has an even number of 1s
Multiples of x + 1 always have an even number of 1s
(x + 1) · 1
1
1
2 ones
(x + 1)(x2 + 1)
1
1
1
1
4 ones
(x + 1)(x3 + x + 1)
1
1
1
0
1
4 ones
odd error x5 + x2 + 1
1
0
0
1
0
1
3 ones: e(1) = 1
not a multiple of x + 1
New Why x + 1 sees odd errors
4

## Slide 5
10.3.4
Theorem: x + 1 catches every odd number of errors
Claim: (x + 1) | g(x), e(x) with an odd number of terms → g(x) does not divide e(x)
Proof: if g | e, then (x + 1) | e and e(1) = 0, but odd count gives e(1) = 1. QED
Corollary: every codeword has an even number of 1s, a built-in parity bit
x + 1 alone (parity): misses two adjacent errors xi (x + 1)
CRC-16 = (x + 1)(x15 + x14 + x13 + x12 + x4 + x3 + x2 + x + 1)
Quick test: x + 1 is a factor iff g has an even number of terms, CRC-32 has 15
Generator | Terms | x + 1 factor
CRC-8: x8 + x2 + x + 1 (ATM header) | 4 | Yes
CRC-10: x10 + x9 + x5 + x4 + x2 + 1 (ATM AAL) | 6 | Yes
CRC-16: x16 + x12 + x5 + 1 (HDLC) | 4 | Yes
CRC-32 (LANs) | 15 | No
New Standard generators and the x + 1 factor
5

## Slide 6
10.3.4
Burst of length L
Burst: first and last corrupted bits L positions apart, anything between
e(x) = xi b(x): b(x) = xL−1 + … + 1, both ends 1
Generator: degree r = number of check bits, g(0) = 1
Model: the L − 2 inner bits of b independent, each 1 with probability 1/2
Missed: exactly when g(x) divides e(x)
burst length L = 6
i = 6 positions: factor xi
sent c(x)
1
1
0
1
0
0
1
1
1
0
0
1
0
1
1
0
error e(x)
0
0
0
0
1
0
1
1
0
1
0
0
0
0
0
0
received
1
1
0
1
1
0
0
0
1
1
0
1
0
1
1
0
XOR
x15
x0
b(x) = 101101: both ends 1, the 4 inside bits could be
any of 2L−2 = 16 patterns, each with probability 1/16
only bits where e(x) has a 1 flip
e(x) = x6 b(x), missed iff g(x) divides e(x)
New Anatomy of a burst: e(x) = xi b(x)
6

## Slide 7
10.3.4
Position lemma, Cases 1 and 2
Lemma: g(0) = 1 → g | xi b iff g | b, since g and xi share no factor
Case 1, L ≤ r: always detected
deg b = L − 1 < r = deg g
Nonzero multiples of g have degree ≥ r, so g does not divide b. QED
Case 2, L = r + 1: missed with probability (1/2)r−1
g | b iff b = 1 · g: one quotient
Ends agree, all r − 1 inner bits must match g. QED
g(x)
1
g
g
g
g
1
r + 1 = 6 bits (r = 5), fixed
L = 4 ≤ r
1
?
?
1
shorter than g: no nonzero multiple
of g is that short, always caught
L = 6 = r + 1
1
?
?
?
?
1
same length as g: missed only if b = g,
all r − 1 inner bits match: (1/2)r−1
L = 8 ≥ r + 2
1
?
?
?
?
?
?
1
longer than g: missed iff b = q(x) g(x),
count quotients q = 1 ? 1: 2 of 64, (1/2)r
New The three cases: b(x) against a fixed g(x), r = 5
7

## Slide 8
10.3.4
Case 3, L ≥ r + 2: count the quotients
Missed iff b = q(x) g(x): count the possible quotients q
deg q = L − 1 − r ≥ 1
b has both ends 1, so q must too
Free bits of q: L − r − 2 → 2L−r−2 quotients
Distinct q → distinct b: one missed burst per quotient
All bursts of length L: 2L−2
P(missed) = 2L−r−2 / 2L−2 = (1/2)r. QED
g = 1011, L = 6: q = 101 or 111, 2 of 16 bursts missed = (1/2)3
Case 2 is the same count: L = r + 1 leaves only q = 1
L
quotient q
missed b = q g
count
L = 4
1
× g =
1
0
1
1
1 of 4
L = 5
1
1
× g =
1
1
1
0
1
1 of 8
L = 6
1
0
1
× g =
1
0
0
1
1
1
2 of 16
1
1
1
× g =
1
1
0
0
0
1
L = 7
1
?
?
1
× g =
4 quotients → 4 bursts
4 of 32
q = 1 ? … ? 1: L − r bits, ends fixed, L − r − 2 free
→ 2L−r−2 quotients = 2L−r−2 missed bursts of 2L−2
New Missed bursts = possible quotients q, g(x) = 1011
8

## Slide 9
Example
Every burst checked for g(x) = 1011
L = 3: 0 of 2 missed, shorter than g
L = 4: 1 of 4, only g itself, (1/2)2
L = 5: 1 of 8, only (x + 1) g, (1/2)3
Each extra check bit: halves the miss rate of long bursts
L = r + 1: worst case, twice the rate of longer bursts
Model caveat: real bursts are not uniform, but L ≤ r holds for every pattern
g(x) = x3 + x + 1:
1
0
1
1
r = 3
L = 3 ≤ r
1
0
1
1
1
1
0 of 2 missed
L = 4 = r + 1
1
0
0
1
1
0
1
1
= g
1
1
0
1
1
1
1
1
1 of 4 missed = (1/2)2
L = 5 = r + 2
1
0
0
0
1
1
0
0
1
1
1
0
1
0
1
1
0
1
1
1
1
1
0
0
1
1
1
0
1
1
1
1
1
0
1
= (x + 1) g
1
1
1
1
1
1 of 8 missed = (1/2)3
New Every burst up to L = 5 for g(x) = 1011, missed ones in red
9

## Slide 10
Example 10.10
What the formulas give
CRC-32, r = 32: bursts up to 32 bits always caught, L = 33 missed 1 in 2.1 billion, longer 1 in 4.3 billion
Exhaustive count, x14 + x3 + 1: 1 of 8192 at L = 15, 1 of 16,384 at L = 16
x6 + 1 count matches: L = 7 gives 1/32 = (1/2)5, L ≥ 8 gives 1/64 = (1/2)6
Choosing r: cover the longest expected burst, anything longer slips through at most (1/2)r−1
L | Bursts | Missed | Fraction
2 to 6 | 1 to 16 | 0 | 0
7 | 32 | 1 | 1/32
8 | 64 | 1 | 1/64
9 | 128 | 2 | 1/64
10 | 256 | 4 | 1/64
11 | 512 | 8 | 1/64
New Exhaustive count, g(x) = x6 + 1, r = 6
Generator | r | L = r + 1 | L ≥ r + 2
x6 + 1 | 6 | 1/32 ≈ 3.1% | 1/64 ≈ 1.6%
x14 + x3 + 1 | 14 | 1 in 8192 | 1 in 16,384
x18 + x7 + x + 1 | 18 | 7.6 per million | 3.8 per million
x32 + x23 + x7 + 1 | 32 | 4.7 in 1010 | 2.3 in 1010
New Missed fraction by generator, L ≤ r always caught
10

## Slide 11
Summary
What a generator catches, and why
Proof tools
Division algorithm, deg r(x) < deg g(x)
GF(2): 1 + 1 = 0, add = subtract = XOR
Evaluation at x = 1: parity of the terms
Unique factorization: removes the shift xi
Counting: quotients over all bursts
Try it
x3 + x + 1 misses two errors 7 bits apart: x7 + 1 = (x + 1)(x3 + x + 1)(x3 + x2 + 1)
List the bursts of length 6 missed by x3 + x + 1: count the quotients
Codeword 0001011 of the C(7, 4) code: why does that 3-bit error go undetected?
Error pattern | Condition on g(x) | Reason
Single bit, xi | 2 or more terms, g(0) = 1 | xi has no factor of g
Two bits, xi (xt + 1) | g does not divide xt + 1, t up to n − 1 | xi drops out
Odd number of bits | x + 1 is a factor of g | e(1) = 1, multiples of g vanish at 1
Burst, L ≤ r | g(0) = 1 | b(x) too short
Burst, L = r + 1 | g(0) = 1 | one quotient: (1/2)r−1
Burst, L ≥ r + 2 | g(0) = 1 | 2L−r−2 quotients: (1/2)r
New What a generator catches
11