## Slide 1: 4.4: ARP Frame Format
Seung-Woo Han
2015021525

## Slide 2: 4.4 ARP Frame Format
ARP frame format as used when mapping IPv4 addresses to 48-bit MAC (Ethernet) addresses
ARP is general enough to be used with addresses other than IPv4 addresses, although this is very rare.
The first 14 bytes constitute the standard Ethernet header, assuming no 802.1p/q or other tags, and the remaining portion is defined by the ARP protocol.

## Slide 3: 4.4 ARP Frame Format
The first 8 bytes of the ARP frame are generic
The remaining portion applies specifically when mapping IPv4 addresses to 48-bit Ethernet-style addresses.
The first two fields contain the destination and source Ethernet addresses.
The special Ethernet destination address of ff:ff:ff:ff:ff:ff (all 1 bits) means the broadcast address—all Ethernet interfaces in the same broadcast domain receive these frames.

## Slide 4: 4.4 ARP Frame Format
The 2-byte Ethernet frame Length or Type field is required to be 0x0806 for ARP (requests or replies).
The first four fields following the Length/Type field specify the types and sizes of the final four fields and are maintained by the IANA [RFC5494]
The adjectives hardware and protocol are used to describe the fields in the ARP packets.
  For example, an ARP request asks for the hardware address (an Ethernet address in this case) corresponding to a protocol address (an IPv4 address in this case).

## Slide 5: 4.4 ARP Frame Format
The common terminology for the hardware address is MAC, physical, or link-layer address.
  Ethernet address when the network in use is based on the IEEE 802.3/Ethernet series of specifications.
The Hard Type field specifies the type of hardware address.
  Value = 1 for Ethernet.
The Prot Type field specifies the type of protocol address being mapped.
  Value = 0x0800 for IPv4 addresses.
  Purposely the same value as the Type field of an Ethernet frame containing an IPv4 datagram.

## Slide 6: 4.4 ARP Frame Format
The next two 1-byte fields, Hard Size and Prot Size represent the hardware addresses and the protocol addresses in bytes.
  Values: Hard = 6, Prot = 4
The Op field specifies whether the operation is an ARP request (a value of 1), ARP reply (2), RARP request (3), or RARP reply (4).
  Required because the Length/Type field is the same for an ARP request and an ARP reply.

## Slide 7: 4.4 ARP Frame Format
The next four fields:
  The Sender’s Hardware Address (an Ethernet MAC address in the figure at 1st slide)
  The Sender’s Protocol Address (an IPv4 address)
  The Target Hardware (MAC/Ethernet) Address
  The Target Protocol (IPv4) Address.
Duplication of information: The sender’s hardware address is available both in the Ethernet header and in the ARP message.

## Slide 8: 4.4 ARP Frame Format
For an ARP request, all the fields are filled in except the Target Hardware Address (which is set to 0).
When a system receives an ARP request directed to it
  It fills in its hardware address.
  Swaps the two sender addresses with the two target addresses.
  Sets the Op field to 2, and sends the reply.