## Slide 1: Internet address architecture
Lecture 3

## Slide 2: Introduction
Every interface connected to Internet has at least 1 IP address
IPv4 addr
  32 bits  dotted decimal notation
IPv6 addr
  128 bits  colon hexadecimal notation
  Block = 4 hexadecimals

## Slide 3: Dotted decimal notation
Only for human convenience
Computer program still needs 32-bit representation – will be translated

## Slide 4: Introduction
Three types of IPv4 addresses
Unicast – most applications use this
Multicast – IPTV uses this
Broadcast
IPv6: broadcast addresses are called multicast

## Slide 5: Classful addressing
Class (A, B, C, D, E) determines allocation size
  A, B, C unicast
  D multicast
  E reserved
How many blocks are in A, B, C?
Now  classless addressing

## Slide 6: Classful addressing

## Slide 7: IPv4 unicast address structure
Originally two-tier structure – reflects Internet structure

## Slide 8: Problems of classful IP addressing
Lack of internal address flexibility  subnetting
Inefficient use of address space  classless addressing
Proliferation of router table entries  CIDR

## Slide 9: Inefficient use of addresses

## Slide 10: Classless addressing
Names still remain (e.g. Class A space)
Now you can salami or aggregate blocks
No fixed boundary between network and host
Classless InterDomain Routing (CIDR)

## Slide 11: Classless addressing
Aggregation example
These 16 entries in the routing table can be merged to a single entry

## Slide 12: Classless addressing
Example

## Slide 13: Subnetting
IPv4 address = network + host
Subnetting splits host  subnet + host
“Subnet mask” tells |subnet|

## Slide 14: Subnetting
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 15: Subnetting
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 16: Subnetting

## Slide 17: Sub-sub-subnet?
As long as routing table is correctly set up!

## Slide 18: Subnetting – what’s good
Better match to physical network structure
Flexibility – subnet size can be customized
Invisibility to public Internet
No routing table entry proliferation

## Slide 19: Subnetting
In Korea University …

## Slide 20: Broadcast addresses
Broadcast target is marked by all 1’s
Limited
Directed
  Policy dictates if directed broadcast is forwarded

## Slide 21: CIDR & aggregation
CIDR notation
Routing table size reduction
  Fig. 2-8

## Slide 22: Special-use addresses
IPv4  Tab. 2-7
  Private  one in each class
  Loopback
  Test
  Reserved
  Multicast
  Broadcast
  Unspecified

## Slide 23: Special-use addresses

## Slide 24: Special-use addresses

## Slide 25: Special-use addresses
IPv6  Tab. 2-8
  Default route
  Unspecified
  Loopback
  V4v6 transition related
  Test and documentation
  Link local
  multicast

## Slide 26: Multicast addresses
Tab. 2-9
  SSM vs. ASM
  GLOP (233)  16 b ASN
  UBM (234)
  Administrative scope  analogous to private unicast addr

## Slide 27: Multicast addresses

## Slide 28: IPv6 multicast addresses
No “broadcast” in IPv6
Reserved block  ff00::/8
  ff02  link local multicast
  ff0e  global multicast
P=1 (ff3)
  UBM (IPv6) or
  Link scoped  IID used
    T=1
R=1 (ff7)

## Slide 29: Anycast
Closest
DNS, RP, 6to4 servers

## Slide 30: Allocation
IANA, top of the hierarchy
RIR
Provider aggregatable vs. provider independent (PI)

## Slide 31: Allocation

## Slide 32: Allocation of IPv4 – end in sight
IANA was depleted on 3 Feb. 2011
RIRs are distributing last /8
IoT aggravates IP address shortage
Time to migrate to IPv6? – may or may not be

## Slide 33: IPv6 addresses
Unicast
Multicast – includes broadcast!
Anycast – not explicitly, but through assigning the same IP address to more than one device

## Slide 34: IPv6 address space
2128 addresses – 1.6 inch vs. solar system

## Slide 35: IPv6 address notation
Colon-hexadecimal, also for human convenience

## Slide 36: IPv6 addresses
Leading zeros can be omitted in a block
All 0’s in a block  ::
  Can be used only once in an IPv6 addr
IPv4-mapped IPv6 addr  ::ffff:a.b.c.d

## Slide 37: IPv6 address space allocations

## Slide 38: IPv6 address structure
Scope
  Node local, link local, global
Link-local
  Prefix (64b) + interface ID (64b)
IID  usually modified EUI-64

## Slide 39: IPv6 global unicast address
You can split the subnet ID part any way you want – e.g. no subnet, single-level subnet, sub-sub-sub net, etc.

## Slide 40: Modified EUI-64
EUI-48
  First 24b  Organizationally unique identifier (OUI)
  Last 2 bits of the first byte of OUI
    U : 1=locally administered
    G : 1=multicast
Modified EUI-64 = OUI + 0xFFFE + 3B
  “modified”  u bit inverted

## Slide 41: Modified EUI-64

## Slide 42: IPv6 multicast addresses
Starts with FF

## Slide 43: IPv6 multicast: solicited-node multicast address
There is no ARP protocol in IPv6… instead,

## Slide 44: IPv6 adoption
Google: 8% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  20 years and counting!
  think of application-level changes in last 20 years: WWW, Facebook, streaming media, Skype, …
  Why? “NAT is IPv4ever.”

## Slide 45: Tunneling
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4