## Slide 1: 4.6 ARP cache timeout
Dynamic entries
  Cf. static entries never time out
Most implementations have a timeout of 20 minutes for a completed entry
  For an incomplete entry? implementation dependent
These implementations normally restart the 20-minute timeout for an entry each time the entry is used
  [RFC1122], the Host Requirements RFC, says that this timeout should occur even if the entry is in use, but many implementations do not do this

## Slide 2: 4.7 Proxy ARP
Proxy ARP lets a system (generally a specially configured router) answer ARP requests for a different host
  This fools the sender of the ARP request into thinking that the responding system is the destination host when in fact the destination host may be elsewhere (or may not exist)
  Proxy ARP is not commonly used and is generally to be avoided if possible
Proxy ARP has also been called promiscuous ARP or the ARP hack
  A router in the middle is configured as a proxy ARP agent to respond to ARP requests on one network for a host on the other network
  This technique can be used to “hide” one group of hosts from another

## Slide 3: 4.8 Gratuitous ARP & Address Conflict Detection (ACD)
It occurs when a host sends an ARP request looking for its own address
  This is usually done when the interface is configured “up” at bootstrap time
It lets a host determine if another host is already configured with the same IPv4 address
  The host sending the gratuitous ARP is not expecting a reply to its request
  If a reply is received, however, the error message “Duplicate IP address sent from Ethernet address . . .” is usually displayed
If the host sending the gratuitous ARP has just changed its hardware address
  Causes any other host receiving the broadcast that has an entry in its cache for the old hardware address to update its ARP cache entry accordingly

## Slide 4: 4.8 Gratuitous ARP & Address Conflict Detection (ACD)
Address Conflict Detection (ACD) defines ARP probe and ARP announcement packets
  An ARP probe is an ARP request packet where Sender’s Protocol Address = 0
    Used to see if a candidate IPv4 address is being used by any other systems in the broadcast domain
    Setting the Sender’s Protocol Address field to 0 avoids cache pollution should the candidate IPv4 address already be in use by another host, a difference from the way gratuitous ARP works
  An ARP announcement is identical to an ARP probe, except Sender’s Protocol Address = Target Protocol Address = candidate IPv4 address
    It is used to announce the sender’s intention to use the candidate IPv4 address as its own

## Slide 5: 4.8 Gratuitous ARP & Address Conflict Detection (ACD)
To perform ACD, a host sends an ARP probe when an interface is brought up or out of sleep, or when a new link is established
It first waits a random amount of time (in the range 0–1s, distributed uniformly) before sending up to three probe packets
  The delay is used to avoid power-on congestion when multiple systems powered on simultaneously would otherwise attempt to perform ACD at once, leading to a network traffic spike
Probes are spaced randomly, with between 1 and 2s of delay (distributed uniformly) placed between

## Slide 6: 4.8 Gratuitous ARP & Address Conflict Detection (ACD)
While sending its probes, a requesting station may receive ARP requests or replies
  A reply to its probe indicates that a different station is already using the candidate IP address
  A request containing the same candidate IPv4 address in the Target Protocol Address field sent from a different system indicates that the other system is simultaneously attempting to acquire the candidate IPv4 address
  In either case, the system should indicate an address conflict message and pursue some alternative address
[RFC5227] places a limit of ten conflicts when trying to acquire an address before the requesting host enters a rate-limiting phase when it is permitted to perform ACD only once every 60s until successful

## Slide 7: 4.8 Gratuitous ARP & Address Conflict Detection (ACD)
If a requesting host does not discover a conflict according to the procedure just described, it sends two ARP announcements spaced 2s apart to indicate to systems in the broadcast domain the IPv4 address it is now using
In the announcements, both the Sender’s Protocol Address and the Target Protocol Address fields are set to the address being claimed
The purpose of sending these announcements is to ensure that any preexisting cached address mappings are updated to reflect the sender’s current use of the address

## Slide 8: 4.8 Gratuitous ARP & Address Conflict Detection (ACD)
ACD is considered to be an ongoing process, and in this way it differs from gratuitous ARP
  Once a host has announced an address, it continues inspecting incoming ARP traffic (requests and replies) to see if its address appears in the Sender’s Protocol Address field
  If so, some other system believes it is rightfully using the same address; In this case, [RFC5227] provides three possible resolution mechanisms:
    Cease using the address
    Keep the address but send a “defensive” ARP announcement and cease using it if the conflict continues
    Continue to use the address despite the conflict
  The last option is recommended only for systems that truly require a fixed, stable address (e.g., an embedded device such as a printer or router)

## Slide 9: 4.8 Gratuitous ARP & Address Conflict Detection (ACD)
[RFC5227] also suggests the potential benefit of having some ARP replies be sent using link-layer broadcast
  This has not traditionally been the way ARP works
  At the expense of requiring all stations on the same segment to process all ARP traffic
Broadcast replies allow ACD to occur more quickly because all stations will notice the reply and invalidate their caches during a conflict

## Slide 10: Arp commands
arp –a
arp –d
arp -s

## Slide 11: 4.11 Attacks involving ARP
Use the proxy ARP facility to masquerade as some host, responding to ARP requests for it
  If the victim host is not present, this is straightforward and may not be detected
  It is considerably more difficult if the host is still running, as more than one response may be generated per ARP request, which is easily detected
When a machine is attached to more than one network, and ARP entries from one interface “leak” over into the ARP table of the other, because of a bug in the ARP software
  This can be exploited to improperly direct traffic onto the wrong network segment

## Slide 12: 4.11 Attacks involving ARP
Static entries may be used to avoid the ARP request/reply when seeking the Ethernet (MAC) address corresponding to a particular IP address
Unfortunately, most implementations of ARP have traditionally replaced even static cache entries with entries provided by ARP replies
The consequence of this is that a machine receiving an ARP reply (even if did not send an ARP request) would be coaxed into replacing its static entries with those provided by an attacker