## Slide 1: 6.6 Attacks involving system configuration
Problems are widespread
  Deploying unauthorized clients or unauthorized servers that interfere with DHCP
  DoS attacks that involve resource exhaustion, such as requesting all possible IP addresses a server may have to give out
Why?
  Older IPv4-based protocols used for address configuration were designed for networks where trust was assumed, and the newer ones have seen little deployment to date
  None of these attacks are directly addressed by typical DHCP deployments
    Link-layer authentication (e.g., WPA2 as used with Wi-Fi networks) helps to limit the number of unauthorized clients that are able to attach to a particular network
IPv6 Neighbor Discovery would directly impact the security of operating networks using SLAAC
  Secure Neighbor Discovery (SEND) protocol is defined in [RFC3971]
  SEND applies IPsec (see Chapter 18) to Neighbor Discovery packets
  Cryptographically generated addresses (CGAs) [RFC3972]
    Addresses are derived from a keyed hash function, so they can be generated only by a system holding the appropriate key material