## Slide 1: PPP Implementation & Serial Communication
Term project #2

## Slide 2: Serial Communication
Open serial device
#include <stdio.h> #include <stdlib.h>
#include <fcntl.h> #include <string.h>
#include <termios.h>
#define BAUDRATE B38400
#define SERIALDEVICE /dev/ttyS0
int main(void) {
int fd;
struct termios tio;
fd = open(SERIALDEVICE, O_RDWR | O_NOCTTY | O_NONBLOCK);
if (fd < 0) { perror(SERIALDEVICE); exit(-1); }
…
}

## Slide 3: Serial Communication
Device control and file description
  Given a pathname for a file(or a device), open() returns a file descriptor
  The file descriptor is used in device control functions (system calls such as read(), write() )
The termios structure
  data structure containing terminal configuration
  c_cflag/c_iflag :control mode/input mode flags

## Slide 4: Serial Communication
Serial device settings
  tcflush(): discards data in the fd
    TCIFLUSH : flushes data received but not read
  tcsetattr(): sets the parameters associated with the terminal
bzero(&tio, sizeof(tio));
tio.c_cflag = BAUDRATE | CRTSCTS | CS8 | CLOCAL | CREAD;
tio.c_iflag = IGNPAR | ICRNL;
tcflush (fd, TCIFLUSH);
tcsetattr (fd, TCSANOW, &tio);

## Slide 5: Serial Communication
Read/write serial device
  read(int fd, void *buf, size_t count)
    reads up to count bytes from a fd into the buf, returns the number of bytes successfully read
  write(int fd, const void *buf, size_t count)
int res, snd, buf_size;
unsigned char buf[255];
res = read(fd, buf, 255);
snd = write(fd, buf, buf_size);

## Slide 6: PPP Implementation
AHDLC frame Receiving procedure
  Some byte streams are arrived
  Assemble sequential bytes into a AHDLC PPP frame (between flag/delimiter 7Es)
  Check the CRC using CRC-16 mechanism
  Remove escape codes
  Check protocol field
    LCP : LCP negotiation process
    IPCP : IPCP negotiation process

## Slide 7: Example of AHDLC frame receiving procedure
RCVD: 7e ff 7d 23 c0 21 7d 21 7d 21 7d 20 7d 2e
RCVD: 7d 22 7d 26 7d 20 7d 20 7d 20 7d 20 7d 27
RCVD: 7d 22 7d 28 7d 22 70 34 7e ff 7d 23 c0 21
7e ff 7d 23 c0 21 7d 21 7d 21 7d 20 7d 2e 7d 22 7d 26 7d 20 7d 20 7d 20 7d 20 7d 27 7d 22 7d 28 7d 22 70 34 7e
CRC check : 70 34 is good crc
7e ff 03 c0 21 01 01 00 0e 02 06 00 00 00 00 07 02 08 02 70 34 7e
Protocol field : c0 21 -> LCP procedure

## Slide 8: PPP Implementation
AHDLC frame sending procedure
  Get original data from upper protocols (LCP, IPCP)
  Convert original data to escape code if ACCM is on
  Append a CRC code
    Convert to escape code if ACCM is on
  Add flag/delimiter 7E to the frame

## Slide 9: PPP Implementation
LCP implementation
  Must implement a PPP state machine
    connection/termination transition must be covered
  LCP negotiation procedure follows transition of the PPP state machine
  LCP should be able to handle ACCM, pcomp, accomp options

## Slide 10: PPP state machine

## Slide 11: PPP state machine

## Slide 12: Connection Establishment

## Slide 13: Homework #2
Implement PPP
  Implement a basic PPP protocol included LCP, IPCP and connect to the pppd program to complete PPP connection establishment and termination.
  Implementation components
    AHDLC PPP framing with CRC-16 and character escaping process
    LCP negotiations with PPP state machine (connection establishment/termination)
    IPCP negotiations
    Print hex codes of send/recv frame and analyze messages like debug of pppd

## Slide 14: Homework #2
Test & Result
  Connect your developed program to a pppd of virtual machine
  The program should be able to negotiate accomp, pcomp options.
submission
  Result screenshot
    Execution results : both of pppd and your program results
    Show hex codes, message exchanges, analysis of messages
  Report
    Explain your program : what components is implemented, especial points(functions, algorithms, codes, and so on)

## Slide 15: References
RFC 1661, RFC 1662, RFC 1332
James Carlson, “PPP Design, Implementation, and Debugging 2nd edition,” Addison-Wesley, July 2000.
http://www.tldp.org/HOWTO/Serial-Programming-HOWTO/