## Slide 1: Kyun Queue: A Sensor Network System to Monitor Road Traffic Queues
SENSYS 2012
Indian Institute of Technology,
Bombay

## Slide 2: Contents
Introduction
Traffic sensing with wireless across road
Design of the Kyun Queue system
Hardware prototypes
Deployment based evaluation
Self localization
Discussion and future work
Conclusions

## Slide 3: Introduction
The Problem of road congestion is currently plaguing most cities in the world
  Unpredictable travel times
  Fuel inefficiency
Automated traffic management solutions
  Developed for western traffic
  Characteristics of traffic in developing country
    non-lane based, highly heterogeneous

## Slide 4: Introduction
Ideal traffic sensing system’s requirements
  Sense road occupancy even if traffic is chaotic and non-lane based
  Deployable without interrupting traffic flow
  Capable of real time sensing and classification to support applications like traffic signal control
  Low installation and maintenance costs

## Slide 5: Introduction
Kyun Queue
  A sensor network system for real time traffic queue monitoring
  To sense road occupancy, based on how RF link quality suffers in absence of line of sight
    IEEE 802.15.4 transmitter-receiver pair across the road.
Design & Build Embedded platform
  Sensing and computation for binary classification
  Communication to combine the decisions of multiple sensors to know the length of traffic queue
  Communication of the queue length values to a remote server

## Slide 6: Traffic sensing with wireless across road
Design a system for traffic queue length measurement in chaotic road conditions
  Rather than exact vehicle counts
  Queue length is proportional to traffic volume.
Using wireless transmitter-receiver pair to measure road traffic density
Question
  Can traffic states be quantitatively inferred from RF link characteristics?
  Can classifications be done in order of tens of seconds to support applications like traffic light control?
  What wireless features and algorithms can be used for high classification accuracy?

## Slide 7: Does road traffic affect wireless links?
802.15.4 compliant Telosb motes
Tx sends 25 pkt/sec, payload 100bytes at -25dBm power
Measure RSSI, PRR
25m

## Slide 8: Classification Algorithm
Binary traffic state classification
Four machine learning algorithm
  FeatureClassifier (FC) algorithm with K-means
  FeatureClassifier (FC) algorithm with SVM
  SignalClassifier (SC) algorithm with K-means
  SignalClassifier (SC) algorithm with SVM
The accuracy for FeatureClassifier using K-means is above 90%, with 20s time window

## Slide 9: Choice of features
LQI (link quality index), RSSI, PRR
  RSSI percentile-based features yield better accuracies than the others
  Non-intuitive observation : RSSI is much more strongly correlated with line-of-sight than LQI or PRR
Summary
  Use FeatureClassifier(FC) algorithm with K-Means
    Built over 20 seconds
    Feature : RSSI

## Slide 10: Design of the Kyun Queue System
Architecture
  3 pairs of transmitter (Ti) – receiver (Ri)
    Perform sensing and computation to know the traffic condition.
  Central controller unit (C)
    Receive the road occupancy observation values from Tx-Rx pairs
  Server (S)
    Receiving road occupancy information
    Implement other applications like coordinated signal control, bottleneck identification and congestion mapping

## Slide 11: Design of the Kyun Queue System
Which RF technology to use for sensing
  Wi-Fi
    large energy consumption
    Connection oriented protocol, may induce long delay in re-establishing connection following packet losses
  Bluetooth
    Poor range, hard to establish for wide roads of 25m
  802.15.4 seems to be a better choice

## Slide 12: Design of the Kyun Queue System
Two types of wireless links
  sensing links
    across the road from T and R
    should be affected by the traffic flow on the road
  communication links
    along the road, from on R to R
    have to be reliable as well

## Slide 13: Software Protocol
Ensure that all R’s perform sensing and computation
  C centrally controls measurement cycle
  No need of any explicit time synchronization mechanism
MAC protocol
  CSMA-CA
C-RDY: receiver ready mode waiting for a control message
C sends a control message
Compute sensing decision
Decision results send to the next R
1. Write in micro-SD card and Compute the traffic signal schedule from the queue length information in the data message (every 30s)
2. Send to S by GPRS

## Slide 14: Hardware prototypes

## Slide 15: Deployment based evaluation
Evaluation
  Installation
    T : on a divider
    C, R : on a Lamp-posts
  R has a stored K-Means clustering model using nine RSSI percentile, measured over t=20 secs, as features.

## Slide 16: Deployment based evaluation
Deployment
Nov. 17(Thu), 18(Fri), 19(Sat), 2011 6pm – 9pm
  Image based manual verification scheme
    Samsung Google Nexus phone
    to capture image ever 30 seconds
    Can only cover T-R pair 1-3
  Person observes offline and estimates
  the queue length
C R1 R2 R3 R4 R5
1 | 1 | 1 | 0 | 0
3
Queue length can take 6 values
From 0 to 5
0 : all R’s report free flow
5 : all R’s report congestion

## Slide 17
Error of 1 ~ 3 unit
  Difference between queue estimate and the ground truth
  fp : false positive ( queue estimate > ground truth)
  fn : false negative ( queue estimate < ground truth)
Result
  Maximum : 96 % (Nov 18)
  Minimum : 74 % (Nov 17)
Deployment based evaluation

## Slide 18: Self Localization
Without pre-defined order and program R unit
To use RSSI ranging
  It is not a monotonically decreasing function of distance
  Oscillations
    Lower Antenna heights seem to give less oscillations
    Vertical polarization seems to give less oscillations

## Slide 19: Self Localization
Fig. 30: {node 2, node 5, node 4, node 6, node 3}
  31 116 95 144 70
Fig. 31: {node 2, node 5, node 6, node 4, node 3}
  39 113 140 85 64
Alternative
  The R recording the best RSSI is marked as the first node
  Continue iteratively

## Slide 20: Discussion and future work
Interference issues
  802.15.4 has 16 orthogonal channel
  Inter-network interference can still exists (Wi-Fi AP)
  Interference doesn’t affect RSSI of received packets
    Disable CRC
    Disable CCA
  Use only 802.15.4 channel 26
    Outside 802.11 spectrum

## Slide 21: Discussion and future work
Power consumption
  T units: 20 XBEE tx operations per second
  R units: in every measurement cycle spanning 30 seconds,
    Receive at most 400 XBEE packets during sensing
    Perform one classification operation
    Receive and transmit at most 8 CC2520 messages
  C unit:
    Performs 1 GPRS communication
    2 SD card operations
    Receive and transmit at most eight CC2520 messages

## Slide 22: Discussion and future work
Classification schemes and model training
  Identify characteristics like road width and vehicle types
  Extend -> multi-classes
    Empty road
    Fast traffic
    Slow traffic
    Standing traffic
Other design choices
  Different topologies to reduce overhead
  Replace dual radio solution with single radio

## Slide 23: Conclusion
Design and implement a new sensing system to detect road occupancy based on RF link quality degradation
Design and implement a sensor network to distributedly decide traffic queue length in real time
Achieve up to 96% accuracy in queue length estimation

## Slide 24: Q & A