## Slide 1: Dynamic Host Configuration Protocol (DHCP)
6강

## Slide 2: What to configure?
Many things --- DHCP can configure close to 200 different things on a host
  http://www.iana.org/assignments/bootp-dhcp-parameters/bootp-dhcp-parameters.xml
IP address, router address, domain name server address, subnet mask, service gateways…

## Slide 3: Autoconfiguration
Plug and play
Two kinds of autoconfiguration
  Stateful  DHCP
  Stateless

## Slide 4: DHCP
Client/server protocol
  Application layer protocol  Uses UDP/IP
  UPD port 67 (server) & 68 (client)
Evolved from BOOTP
  Which in turn evolved from RARP
Most noticeable change: “lease”

## Slide 5: Lease
Address assignment with contracted duration
Duration depends on how much addresses are in need

## Slide 6: Message format
Fig. 6-1
  Smells of ARP?
Use “bootp” filter in Wireshark

## Slide 7: Message format
Fixed part + Options
Client H/W address is 16 bytes
  Usually the “H/W” address (i.e. link layer address like MAC address) is only 6 bytes
  Padding is used
    Due to fixed length

## Slide 8: Message format
Op
  1 = request, 2 = reply (like in ARP)
HW type
  Link layer (e.g. Ethernet = 1)
HW length
  Address length used by the HW type specified above (e.g. Ethernet = 6 bytes)
Hops
  Number of DHCP (bootp) relays that this message have been through so far

## Slide 9: Message format
Transaction ID
  Like in any other application protocol that uses UDP, this matches a response with the request that triggered the repsonse
Secs
  Number of seconds since the first attempt
Flags
  “B”: broadcast = reply should be broadcast

## Slide 10: Message format
Client IP address
  If nothing is assigned yet, 0.0.0.0
  Otherwise, the assigned IP address
Your IP address
  This is the IP address that the DHCP server offers to the client
Next server address
  The IP address of the “next” server to go to
    E.g. After address assignment, go to the boot image server to download OS

## Slide 11: Message format
Gateway (relay) IP address
  The DHCP (bootp) relay address to use
  Usually the router
  Today’s first-hop routers run DHCP relay
Server name & boot file name
  Boot image server and the location of the bootfile
  When DHCP is used to bootstrap a client computer

## Slide 12: Message format
Options
  Many (close to 200)
  Examine some DHCP trace to know which are most popular and what they do

## Slide 13: DHCP options
Close to 200
TLV format again
Message type option is important
  DISCOVER, REQUEST, ACK, NACK, INFORM

## Slide 14: DHCP protocol operations
Fig. 6-2
State machine (Fig. 6-10)
Try “ipconfig /release” and “ipconfig /renew”

## Slide 15: Rapid commit
Usually there is only one DHCP server
Usually the offered address is accepted
Offer and Request steps can be omitted

## Slide 16: Stateless Address Autoconfiguration
This is about IP address configuration only
  DHCP can configure close to 200 host parameters other than IP address
Using link local IP addresses
  IPv4: 169.254.0.0/16
  IPv6: fe80::/64

## Slide 17: DHCP with relays
Modern configuration typically uses relays
  Between clients and the remote DHCP server(s)
Routers are typically configured as relays
Note: relays only relay broadcast DHCP packets
  Unicast packets to/from the DHCP server after the server is found by the client don’t have to be relayed