## Slide 1: Reconfiguring the Software Radio to Improve Power, Price, and Portability
Ye-sheng Kuo, Patrick Pannuto, Thomas Schmid, and Prabal Dutta
SenSys ‘12 at Toronto

## Slide 2: Recent low-power wireless research
“High-Resolution, Low-Power Time Synchronization an Oxymoron No More”
  IPSN ‘10
“Design and Evaluation of a Versatile and Efficient Receiver-Initiated Link Layer for Low-Power Wireless”
  SenSys ‘10
“Efficient Network Flooding and Time Synchronization with Glossy”
  IPSN ‘11
“Low-Power Wireless Bus”
  SenSys ‘12

## Slide 3: Current SDR platforms
 | USRP2 | USRP E100 | WARP v3 | SORA
Power | ~10 W | ~10 W | ~50 W* | ~100 W
Size | 1760 cm3 | 1760 cm3 | 900 cm3 | 300 cm3*
Cost | $1,700 | $1,300 | $4,900 | $2,000
Low-power wireless research cannot benefit from current SDRs

## Slide 4: If we have a low-power portable SDR
Software radios that you could
  Hold in the palm of your hand
  Deploy at very large scale
  Hand out for student labs
Software radios that would enable
  Mobile networking research
  Large-scale, in situ evaluations

## Slide 5: uSDR is low-power, small and low-cost
Power:
  1.4 W maximum
  0.32 W minimum
  Battery-operated
Size:
  203 cm3
Cost:
  ~$150
  (Core SDR Platform, assembled)

## Slide 6: Outline
Introduction
Challenges
Architecture Overview
Evaluation
Radio enhancement
Limitation
Conclusion

## Slide 7: 1st challenge: Power
SRAM FPGA
  High in-rush current
  High static power
  Re-configuration required
SRAM FPGA is not able to duty-cycle
Images from www.microsemi.com
Notes: Reconfiguration -> Latency, Energy

## Slide 8: 2nd challenge: Size
General purpose
Highly reconfigurable
Modular design
Images from Mango communication
Ettus research
1-250 MHz
TX Board
50-860 MHz
RX Board x2
2.3-2.9 GHz
RX/TX Board
20 MHz TXCO
Clock Board
2.4, 5 GHz
RF Board
WARP v2 Main
Notes: Tradeoff between modularity and area

## Slide 9: 3rd challenge: Cost
Modular design
High performance hardware
  Xilinx Virtex-6, (3rd WARP)
    $2,000
  Xilinx Virtex-5, (SORA)
Not standalone

## Slide 10: Outline
Introduction
Challenges
Architecture Overview
Evaluation
Radio enhancement
Limitation
Conclusion

## Slide 11: Emerging technology
Microsemi’s SmartFusion
  Hard core ARM Cortex-M3
    80MHz std.
    Embedded SRAM and Flash
  500K system gate FPGA
    Flash-based
    Embedded RAM
  Analog Compute Engine
    Low-speed ADCs/DACs
  High speed interconnect
    Memory-mapped IO
    1.4Gb/s (measured)
Images from www.microsemi.com

## Slide 12: Architecture overview

## Slide 13: Highly integrated HW
Baseband processing (PHY, MAC)
  Microsemi SmartFusion
RF Frontend
  Maxim MAX2831
Data converters
  Maxim MAX5189
  Analog Device AD9288
Sacrifice modular design → Size, Cost
Low-power / sleep mode → Power

## Slide 14: Advantages of Flash-based FPGA
Low in-rush current
Low static power
No configuration process
  No current
  No delay
Limitations
  Lifetime
  Speed
  Area
Images from www.microsemi.com

## Slide 15: Outline
Introduction
Challenges
Architecture Overview
Evaluation
Radio enhancement
Limitation
Conclusion

## Slide 16: Flash FPGA is better in duty cycling
uSDR
 | USRP2 | uSDR | 
Latency | 1.96 s | 54 ms | 36X
Energy | 9.56 J | 0.028 J | 341X
USRP loads firmware from SD card
USRP2
Notes: Piece

## Slide 17: Flash FPGA has low static power
Voltage Rail | SmartFusion (uSDR) Static Current | Spartan (USRP2) Static Current
3.3 V (IO) | 26.9 mA | 79 mA
2.5 V (AUX) | n/a | 88 mA
1.5 V (Core) | 8.0 mA | n/a
1.2 V (Core) | n/a | 80 mA
Static Power | 101 mW | 578 mW
6X improvement
SmartFusion 2 supports Flash*Freeze mode, 1 mW
Two switches are used to detach clock signal
Measurement was made “after” firmware has been loaded

## Slide 18: uSDR is portable
Platform | Size (cm3)
SORA | 36000a
WARP v3 | 900b
USRP2 | 1760
uSDR | 203
a: including a desktop PC
b: assume 3 cm thick
uSDR

## Slide 19: uSDR is low-cost
Desc | Part Number | Cost (1K)
FPGA | A2F500M3G | $45
ADC | AD9288 | $4
DAC | MAX5189 | $5
RF | MAX2831 | $4
Memories |  | $9
PoE | AG9205S | $10
Discrete parts |  | $62
PCB | 6 layers | $25
Assembly |  | $50
Total |  | $214
Platform | Cost
SORA | $2,000
WARP v3 | $4,900
USRP2 | $1,700
uSDR kit | $214
(USD)
Notes: Insert USD

## Slide 20: Outline
Introduction
Challenges
Architecture Overview
Evaluation
Radio enhancement
Limitation
Conclusion
Notes: Pause…

## Slide 21: uSDR is better for low-power research
Fully access to low level control/information
Tight control loop
  Automatic Gain Control (AGC)
Flexible Architecture
  Multiple address recognition
Radio extension
  Hard Glossy
  Automatic Transmission

## Slide 22: Beat frequency attenuates amplitude
In the concurrent transmission scenario…
  rB(t): received base band signal
  d(t): signal was been transmitted
  ∆f: carrier frequency mismatch between two transmitters
RSSI
RX Base band
TX1 Base band
TX2 Base band

## Slide 23: Cont. AGC is better for concurrent TX.
 | SFD-Latched AGC | Continuous AGC
Setting | Latch gain when SFD detected | Changing the gain every 4 us
ARR | 97.27 % | 98.20 %
Gain Latched
SFD-Latched AGC is more vulnerable to local minimum
Notes: SFD = Start Frame Delimeter

## Slide 24: Concurrent transmission fails
Beat frequency
  Amplitude below certain threshold (Δf)
  Number of envelopes in a packet (Δf, packet length)
  Slope of envelope (Δf)
Frequency mismatch
Packet length

## Slide 25: Impact of frequency mismatch
60 Bytes per packet
Δf ↓
Beat Freq ↓
Period ↑
Slope ↓

## Slide 26: Impact of packet length
Frequency mismatch < 1KHz

## Slide 27: Architecture of uSDR is flexible
High throughput
Low latency
Flexible SW/HW boundary
Memory mapped radio
Enables
  Multiple address recognition
  Rapid frame filtering
  SW/HW time/area trade-off

## Slide 28: Additional features of uSDR
Hard Glossy
  High speed forwarding
  Precise timing control
  10X faster
Automatic Transmission
  Precise timing control

## Slide 29: Running uSDR as a Testbed
Various Power input
  Power Jack, Headers
  PoE, USB
External Memories
  8 MB flash
  16 MB PSRAM
uClinux
  SSHd, telnetd, httpd
  Network File System (NFS)
  FPGA Live programming
Images from www.uclinux.org

## Slide 30: Outline
Introduction
Challenges
Architecture Overview
Evaluation
Radio enhancement
Limitation
Conclusion
Notes: Pause…

## Slide 31: Limitations
Relatively fewer FPGA gates/LUTs
Higher power than most motes
Lower performance than SRAM-based FPGA
Fixed frontend limits RF flexibility

## Slide 32: Conclusion
uSDR
  A low-power, low-cost and portable SDR platform
  uSDR offers great hardware/software dynamics
  uSDR allows designer to explore wireless protocols
  Better platform for low-power wireless research
Notes: Allows us

## Slide 34: Automatic Frequency Compensation
O-QPSK
  Signal rotates at constant speed
Simulation result
50 KHz apart initially
Freq. step size = 300 Hz