## Slide 1: 5.1 Introduction
IP is the workhorse protocol of the TCP/IP protocol suite
  All TCP, UDP, ICMP, and IGMP data gets transmitted as IP datagrams
IP provides a best-effort, connectionless datagram delivery service
  By “best-effort” we mean there are no guarantees that an IP datagram gets to its destination successfully
  Although IP does not simply drop all traffic unnecessarily, it provides no guarantees as to the fate of the packets it attempts to deliver
Any required reliability must be provided by the upper layers (e.g., TCP)

## Slide 2: 5.1 Introduction
Connectionless means that IP does not maintain any connection state information about related datagrams within the network elements (i.e., within the routers); each datagram is handled independently from all other others
This also means that IP datagrams can be delivered out of order
  Each datagram is routed independently and can take different paths
Datagrams may be duplicated in transit, and they may have their data altered as the result of errors