## Slide 1: 3.1 Introduction
TCP/IP supports many different link layers, depending on the type of networking hardware being used
  Wired LANs such as Ethernet
  Metropolitan area networks (MANs) such as cable TV and DSL connections available through service providers
  Wired voice networks such as telephone lines with modems
  More recent wireless networks such as Wi-Fi (wireless LAN)
  Various wireless data services based on cellular technology such as HSPA, EV-DO, LTE, and WiMAX
In this chapter we shall look at details involved in using
  Ethernet
  Wi-Fi link layers
  Point-to-Point Protocol (PPP)
  Tunneling
    How link-layer protocols can be carried inside other (link- or higher-layer) protocols

## Slide 2: 3.1 Introduction
Most link-layer technologies have an associated protocol format that describes how the corresponding PDUs must be constructed in order to be carried by the network hardware
  Link-layer PDUs is called frame
The upper bound of the frame size is called the maximum transmission unit (MTU), a characteristic of the link layer
  Some network technologies, such as modems and serial lines, do not impose their own maximum frame size, so they can be configured by the user