## Slide 1: S.72-227 Digital Communication Systems
Convolutional Codes

## Slide 2: Targets today
Why to apply convolutional coding?
Defining convolutional codes
Practical encoding circuits
Defining quality of convolutional codes
Decoding principles
Viterbi decoding

## Slide 3: Convolutional encoding
Convolutional codes are applied in applications that require good performance with low implementation cost. They operate on code streams (not in blocks)
Convolution codes have memory that utilizes previous bits to encode or decode following bits (block codes are memoryless)
Convolutional codes achieve good performance by expanding their memory depth
Convolutional codes are denoted by (n,k,L), where L is code (or encoder) Memory depth (number of register stages)
Constraint length C=n(L+1) is defined as the number of encoded bits a message bit can influence to
n(L+1) output bits
input bit
(n,k,L) encoder
k bits
n bits
encoded bits
message bits

## Slide 4
Example: Convolutional encoder, k = 1, n = 2
Convolutional encoder is a finite state machine (FSM) processing information bits in a serial manner
Thus the generated code is a function of input and the state of the FSM
In this (n,k,L) = (2,1,2) encoder each message bit influences a span of C= n(L+1)=6 successive output bits = constraint length C
Thus, for generation of n-bit output, we require n shift registers in k = 1 convolutional encoders
(n,k,L) = (2,1,2) encoder
memory
depth L =number of states

## Slide 5
Example: (3,2,1) Convolutional encoder
Here each message bit influences
a span of C = n(L+1)=3(1+1)=6 successive output bits

## Slide 6: Generator sequences
(n,k,L) Convolutional code can be described by the generator sequences that are the impulse responses for each coder n output branches:
Generator sequences specify convolutional code completely by the associated generator matrix
Encoded convolution code is produced by matrix multiplication of the input and the generator matrix
Note that the generator sequence length
exceeds register depth always by 1
(n,k,L) encoder
k bits
n bits

## Slide 7: Convolution point of view in encoding and generator matrix
Encoder outputs are formed by modulo-2 discrete convolutions: where u is the information sequence:
Therefore, the l:th bit of the j:th output branch is*
Hence, for this circuit the following equations result, (assume: )
encoder output:
j branches
n(L+1) output bits
input bit
*note that u is reversed in time as in the definition of convolution top right

## Slide 9
Example: Using generator matrix
Verify that you can obtain the result shown!

## Slide 10
This tells how one input bit
is transformed into two output bits
(initially register is all zero)
Representing convolutional codes: Code tree
(n,k,L) = (2,1,2) encoder

## Slide 11
Representing convolutional codes compactly: code trellis and state diagram
Shift register states
Input state ‘1’
indicated by dashed line
Code trellis
State diagram

## Slide 12: Inspecting state diagram: Structural properties of convolutional codes
Each new block of k input bits causes a transition into new state
Hence there are 2k branches leaving each state
Assuming encoder zero initial state, encoded word for any input of k bits can thus be obtained. For instance, below for u=(1 1 1 0 1), encoded word v=(1 1, 1 0, 0 1, 0 1, 1 1, 1 0, 1 1, 1 1) is produced:
- encoder state diagram for (n,k,L)=(2,1,2) code
- note that the number of states is 2L+1 = 8
Verify that you can obtain the same result!
Input state

## Slide 13: Code weight, path gain, and generating function
The state diagram can be modified to yield information on code distance properties (= Tells how good the code is)
Rules:
  (1) Split S0 into initial and final state, remove self-loop
  (2) Label each branch by the branch gain Xi. Here i is the weight of the n encoded bits on that branch
  (3) Each path connecting the initial state and the final state represents a nonzero code word that diverges and re-emerges with S0 only once
The path gain is the product of the branch gains along a path, and the weight of the associated code word is the power of X in the path gain
Code weigh distribution is obtained by using a weighted gain formula to compute its generating function (input-output equation) where Ai is the number of encoded words of weight i

## Slide 14
The path representing the state
sequence S0S1S3S7S6S5S2S4S0 has
path gain X2X1X1X1X2X1X2X2=X12
and the corresponding code word
has the weight 12
Where does these terms come from?
weight: 1
weight: 2
branch
gain

## Slide 15: Distance properties of convolutional codes
Code strength is measured by the minimum free distance: where v’ and v’’ are the encoded words corresponding information sequences u’ and u’’. Code can correct up to errors.
The minimum free distance dfree denotes:
    The minimum weight of all the paths in the state diagram that diverge from and remerge with the all-zero state S0
    The lowest power of the code-generating function T(X)
Code gain*:
* for derivation, see Carlson’s, p. 583

## Slide 16: Coding gain for some selected convolutional codes
Here is a table of some selected convolutional codes and their code gains RCdf /2 (df = dfree) often expressed (hard decoding) also by

## Slide 17: Decoding of convolutional codes
Maximum likelihood decoding of convolutional codes means finding the code branch in the code trellis that was most likely transmitted
Therefore maximum likelihood decoding is based on calculating code Hamming distances for each branch forming encoded word
Assume that the information symbols applied into an AWGN channel are equally alike and independent
Let’s denote by x encoded symbols (no errors) and by y received (potentially erroneous) symbols:
Probability to decode the symbols is then
The most likely path through the trellis will maximize this metric. Often ln() is taken from both sides, because probabilities are often small numbers, yielding
Decoder
(=distance
calculation)
received code:
non - erroneous code:
bit
decisions

## Slide 18: Example of exhaustive maximal likelihood detection
Assume a three bit message is transmitted [and encoded by (2,1,2) convolutional encoder]. To clear the decoder, two zero-bits are appended after message. Thus 5 bits are encoded resulting 10 bits of code. Assume channel error probability is p = 0.1. After the channel 10,01,10,11,00 is produced (including some errors). What comes after the decoder, e.g. what was most likely the transmitted code and what were the respective message bits?
a
b
c
d
states
decoder outputs if this path is selected

## Slide 19
errors
correct
weight for prob. to
receive bit in-error

## Slide 20
Note also the Hamming distances!
The largest metric, verify
that you get the same result!

## Slide 21: The Viterbi algorithm
Problem of optimum decoding is to find the minimum distance path from the initial state back to initial state (below from S0 to S0). The minimum distance is the sum of all path metrics that is maximized by the correct path
Exhaustive maximum likelihood method must search all the paths in phase trellis (2k paths emerging/ entering from 2 L+1 states for an (n,k,L) code)
The Viterbi algorithm gets its efficiency via concentrating into survivor paths of the trellis
Received code
sequence
Decoder’s output sequence
for the m:th path

## Slide 22: The survivor path
Assume for simplicity a convolutional code with k=1, and up to 2k = 2 branches can enter each state in trellis diagram
Assume optimal path passes S. Metric comparison is done by adding the metric of S into S1 and S2. At the survivor path the accumulated metric is naturally smaller (otherwise it could not be the optimum path)
For this reason the non-survived path can be discarded -> all path alternatives need not to be considered
Note that in principle whole transmitted sequence must be received before decision. However, in practice storing of states for input length of 5L is quite adequate

## Slide 23: Example of using the Viterbi algorithm
Assume the received sequence is and the (n,k,L)=(2,1,2) encoder shown below. Determine the Viterbi decoded output sequence!
(Note that for this encoder code rate is 1/2 and memory depth L = 2)

## Slide 24: The maximum likelihood path
The decoded ML code sequence is 11 10 10 11 00 00 00 whose Hamming
distance to the received sequence is 4 and the respective decoded
sequence is 1 1 0 0 0 0 0 (why?). Note that this is the minimum distance path.
(Black circles denote the deleted branches, dashed lines: '1' was applied)
1
1
Smaller accumulated
metric selected
First depth with two entries to the node
After register length L+1=3
branch pattern begins to repeat
(Branch Hamming distances
in parenthesis)

## Slide 25: How to end-up decoding?
In the previous example it was assumed that the register was finally filled with zeros thus finding the minimum distance path
In practice with long code words zeroing requires feeding of long sequence of zeros to the end of the message bits: this wastes channel capacity & introduces delay
To avoid this path memory truncation is applied:
  Trace all the surviving paths to the depth where they merge
  Figure right shows a common point at a memory depth J
  J is a random variable whose applicable magnitude shown in the figure (5L) has been experimentally tested for negligible error rate increase
  Note that this also introduces the delay of 5L!

## Slide 26: Lessons learned
You understand the differences between cyclic codes and convolutional codes
You can create state diagram for a convolutional encoder
You know how to construct convolutional encoder circuits based on knowing the generator sequences
You can analyze code strengths based on known code generation circuits / state diagrams or generator sequences
You understand how to realize maximum likelihood convolutional decoding by using exhaustive search
You understand the principle of Viterbi decoding