## Slide 1
Chapter 11
Data Link Control (DLC)
Frames, flow and error control, HDLC and PPP
Forouzan, Data Communications and Networking, 5th ed., Chapter 11
11.1 DLC services, 11.2 data-link protocols, 11.3 HDLC, 11.4 PPP
Today panels: framing, link-layer ARQ, HDLC family and PPP in use now
Figures 11.1 to 11.29 and Tables 11.1 to 11.3 all included, flow diagrams build step by step
Errata: printed slides and textbook

## Slide 2
11.1
DLC services
DLC: node-to-node procedures, dedicated or broadcast link
Functions: framing, flow control, error control, connection handling
Physical layer: bit synchronization, same bit duration and timing
Data-link layer: frame synchronization, where each frame starts and ends
Analogy, envelope: delimiter + sender and receiver addresses
11.1.1
Framing
Destination address: where the frame goes
Source address: lets the receiver acknowledge
Many small frames, not one big one: one bit error → resend only the frame hit
Frame size: fixed (ATM cell) or variable (LANs, HDLC, PPP)
Variable size needs delimiters: character- or bit-oriented
New
Data-link layer = DLC + MAC
Network layer
Part IV: end to end
Data link control (DLC)
Chapter 11: node to node
Media access control (MAC)
Chapter 12: shared links
Physical layer
Part II: bits as signals
11.1.1
Fixed-size frames still need delineation
Fixed size: no flag, frame length known in advance
Book: "size itself is the delimiter": only after the receiver has locked onto a boundary
ATM cell: 53 bytes = 5-byte header + 48-byte payload
5th header byte = HEC, CRC-8 over the first 4
Delineation: HUNT bit by bit, PRESYNC for δ cells, SYNC lost after α failures
Same idea: T-1 frame alignment (Chapter 6), GFP over SDH/OTN today
New
HEC-based cell delineation (ITU-T I.432)
test HEC at
every bit position
check HEC
cell by cell
locked: cell
boundaries known
HUNT
PRESYNC
SYNC
correct HEC
incorrect HEC
δ correct
in a row
α incorrect in a row

## Slide 3
11.1.1
Character-oriented framing
Data: 8-bit characters, e.g. ASCII
Header: addresses, control. Trailer: error-detection bits (Chapter 10)
Flag: one protocol-dependent special byte at start and end
Fine while only text crossed the link
Binary data (images, audio, video): any byte value may appear
Flag pattern inside data → receiver sees a false end of frame
Figure 11.1
A frame in a character-oriented protocol
11.1.1
Byte stuffing
Sender: insert ESC before every data byte equal to Flag or ESC
Receiver: remove ESC, keep the next byte as data
ESC inside data also escaped: ESC ESC, else a data ESC + Flag is misread
Receiver order: find the flags first, then unstuff
Overhead: 0 to 100%, worst case every byte escaped
Book: Unicode breaks byte stuffing? No: stuffing ignores content, any byte stream works
PPP's real rule: ESC 0x7D, then the byte XOR 0x20 (11.4.2)
Figure 11.2
Byte stuffing and unstuffing
Notes: Figure 11.2 builds in 3 clicks: stuffed frame, received frame, unstuffed data.

## Slide 4
11.1.1
Bit-oriented framing
Data: a bit sequence, any content
Flag: 01111110 (0x7E) at both ends
Bit stuffing: 0 then five 1s → insert 0, whatever the next bit
Receiver: 0, five 1s, 0 → drop that 0. 0, six 1s, 0 → flag. Seven or more 1s → abort
Stuffed frame never holds six 1s in a row: flag stays unique
Overhead: at most 1 bit per 5 data bits (20%)
Figure 11.3
A frame in a bit-oriented protocol
11.1.1
Bit stuffing, worked example
Data: 0001111111001111101000
Sent: 000111110110011111001000
Two stuffed 0s, each after a 0 and five 1s
1st: inside a run of seven 1s
2nd: next data bit already 0, stuffed anyway
Flag-like data 01111110 → sent as 011111010
Real flags never stuffed: receiver finds flags, then removes stuffed 0s
Same trick elsewhere: USB (after six 1s), CAN (after five equal bits), for clock recovery
Figure 11.4
Bit stuffing and unstuffing
Notes: Figure 11.4 builds in 3 clicks: stuffed frame, received frame, unstuffed data.

## Slide 5
Today
Where frame boundaries come from now
Link | Frame boundary | Stuffing
HDLC, PPP (serial, SONET/SDH) | Flag 0x7E | Bit or byte stuffing
USB 1.x and 2.0 | SYNC pattern, end-of-packet line state | Bit stuffing after six 1s, keeps NRZI transitions
CAN bus | Start-of-frame bit, fixed field layout | Stuff bit after five equal bits
Ethernet | Preamble + SFD, PHY code groups mark start and end (8b/10b, 64b/66b) | None
GFP over SDH/OTN (G.7041) | 2-byte length + CRC-16 core header, hunted like ATM | None
Wi-Fi A-MPDU | 4-byte delimiter: length, CRC-8, signature 0x4E | None
5G NR MAC | Size known from the grant (DCI), subheaders carry lengths | None
Trend: not bit-oriented, as the book says, but length fields and PHY coding, no stuffing
11.1.2
Flow control
Producer faster than consumer: consumer overwhelmed, frames dropped
Feedback: receiver tells sender to stop or slow down
Buffers at both DLCs: receiver buffer full → "stop", space again → "send more"
Example 11.1: one-slot buffer, slot empty → "send the next frame" = the ACK of Stop-and-Wait
Figure 11.5
Flow control at the data-link layer

## Slide 6
11.1.2
Error control
Physical layer unreliable → error control at DLC
CRC: added by sender in the trailer (FCS), checked by receiver
Book says "header": it is the trailer
Method 1: corrupted → silently discard, intact → deliver (Ethernet)
Method 2: corrupted → discard, intact → deliver + ACK
ACK serves flow and error control
No ACK before timeout → sender assumes loss
NAK: explicit negative acknowledgment (HDLC REJ, SREJ)
11.1.3
Connectionless and connection-oriented
Connectionless: independent, unnumbered frames, no ordering
Not "no physical link": no relation between frames
Most LAN data-link protocols
Connection-oriented: setup → transfer → teardown
Frames numbered, delivered in order
Some point-to-point links (HDLC ABM, PPP), wireless LANs, WANs
11.2
Data-link protocols and FSMs
Classic four: Simple, Stop-and-Wait, Go-Back-N, Selective-Repeat
This chapter: first two, all four in Chapter 23
Book: last two "disappeared" → alive in wireless links (Today)
FSM: event → actions (maybe none) + next state (maybe same)
Figure 11.6: two states
State I, event 1 → actions 1, 2 → State II
State II, event 2 → action 3, stay
State II, event 3 → no action → State I
Book text: "three states", "event 1 → action 3": wrong
Figure 11.6
An example FSM

## Slide 7
11.2.1
Simple protocol
No flow control, no error control
Assumption: receiver handles every frame at once, never overwhelmed
Sender DLC: packet from network layer → frame → send
Receiver DLC: frame → extract packet → deliver
Figure 11.7
Simple protocol
11.2.1
FSMs of the Simple protocol
One state each: Ready
Sender: waits for a packet from its network layer
Packet came → make a frame, send it, stay Ready
Receiver: waits for a frame from the link
Frame arrived → deliver the packet, stay Ready
Figure 11.8
FSMs for the simple protocol

## Slide 8
Example 11.2
Simple protocol in action
Sender: frames back to back, no waiting
Receiver: delivers each packet on arrival
Nothing flows back: no ACK, no feedback
Safe only if the receiver keeps up and the link never errs
Figure 11.9
Flow diagram for Example 11.2
11.2.2
Stop-and-Wait protocol
Flow control + error control
One frame at a time: wait for ACK before the next
CRC on each data frame: corrupted → silently discarded, receiver silence = lost or corrupted
Timer: started at each send
ACK in time → stop timer, send next frame
Timeout → resend the saved copy
Copy kept until its ACK arrives: at most one frame and one ACK on the link
Figure 11.10
Stop-and-Wait protocol
Notes: Figure 11.9 builds in 2 clicks, one frame each.

## Slide 9
11.2.2
Stop-and-Wait FSMs
Sender, Ready
Packet arrives → make frame, save copy, start timer, send → Blocking
Sender, Blocking
Timeout → resend saved frame, restart timer
Corrupted ACK → discard it
Error-free ACK → stop timer, discard copy → Ready
Receiver, always Ready
Error-free frame → deliver packet, send ACK
Corrupted frame → discard
Figure 11.11
FSM for the Stop-and-Wait protocol

## Slide 10
Example 11.3
Lost frame, lost ACK
Frame 1: sent, acknowledged
Frame 2: lost → timeout → resent
Frame 3: delivered, ACK lost → timeout → resent
Packet 3 delivered twice: duplicate
Fix: number the frames and the ACKs
Example 11.4
Sequence and acknowledgment numbers
Seq 0, 1, 0, 1, … ACK 1, 0, 1, 0, …: ACK n = next frame expected
1 bit suffices: one frame outstanding
Frame 1 lost → resent → ACK 0
ACK 1 lost → Frame 0 resent: receiver expects 1, discards it, re-sends ACK 1
In use: Bluetooth LE link layer, 1-bit SN and NESN
Figure 11.12
Flow diagram for Example 11.3
Figure 11.13
Flow diagram for Example 11.4
Notes: Figures 11.12 and 11.13 each build in 5 clicks, one exchange per click. Run 11.12 first, then 11.13.

## Slide 11
11.2.3
Piggybacking and link efficiency
Piggybacking: ACK rides on reverse data, HDLC N(R), TCP
Stop-and-Wait on long links: U = Tf / (Tf + RTT)
1 Gbps, 1500 bytes: Tf = 12 μs
100 m LAN, RTT ≈ 1 μs: U ≈ 92%
1000 km fiber, RTT ≈ 10 ms: U ≈ 0.12%
Fix: many frames in flight
Go-Back-N, Selective Repeat (Chapter 23)
Parallel Stop-and-Wait processes (HARQ)
Today
Link-layer ARQ in use
Link | Scheme | Numbers, window
Bluetooth LE | Stop-and-Wait | 1-bit SN, NESN
Wi-Fi | Stop-and-Wait + Block Ack | Window 64 to 1024
LTE, NR HARQ | Parallel Stop-and-Wait | 8 (LTE), 16 (NR), 32 (NTN)
LTE, NR RLC AM | Selective Repeat | NR: 12- or 18-bit SN
LAPB, LAPD | Go-Back-N with REJ | Modulo 8 or 128
Ethernet, PPP | None, drop bad frames | TCP recovers
11.3
HDLC
High-level Data Link Control: bit-oriented, ISO/IEC 13239
Links: point-to-point, multipoint
Book: "implements Stop-and-Wait" → sliding window
3-bit numbers: 7 outstanding, 7-bit: 127
REJ → Go-Back-N, SREJ → Selective Repeat
Book: "theoretical" → HDLC family still deployed
Not the Ethernet frame: no flags, no stuffing
Today
HDLC family in use
Protocol | Where it runs
LAPB | X.25 (legacy), AX.25 packet radio
LAPD, LAPDm, LAPF | ISDN D channel, GSM radio signaling, Frame Relay
Cisco HDLC | Cisco serial WAN default
PPP framing | RFC 1662, Packet over SONET/SDH
IEEE 802.2 LLC | I, S, U control field on 802 LANs
IEC 62056-46 | Electricity meter reading

## Slide 12
11.3.1
NRM, normal response mode
Unbalanced configuration
One primary: sends commands
Secondaries: only respond
Point-to-point or multipoint (polling)
Figure 11.14
Normal response mode
11.3.1
ABM, asynchronous balanced mode
Balanced, point-to-point only
Combined stations: each primary + secondary, peers
Common mode today (LAPB, LAPD)
Figure 11.15
Asynchronous balanced mode

## Slide 13
11.3.2
HDLC frames
I-frame: user data + piggybacked control
S-frame: flow and error control only, no information field
U-frame: link management
Flag: 01111110, back-to-back frames may share one
Address: secondary station, 1 or more bytes
From primary: "to" address, from secondary: "from" address
Control: 1 or 2 bytes. Information: user or management data
FCS: CRC-16 or CRC-32
Figure 11.16
HDLC frames
11.3.2
Control field
First bits = type: 0 → I, 10 → S, 11 → U
I-frame: N(S) 3 bits, P/F, N(R) 3 bits
N(R): piggybacked ACK, next frame expected
P/F: Poll (primary → secondary), Final (secondary → primary)
S-frame codes, with N(R): RR 00 ACK, RNR 10 ACK but busy, REJ 01 NAK (Go-Back-N), SREJ 11 NAK (Selective Repeat)
U-frame: 2 + 3 code bits → up to 32 types
Extended mode: 2-byte control, 7-bit N(S) and N(R)
Figure 11.17
Control field format for the different frame types

## Slide 14
Example 11.5
Connection setup and release
SABM, A → B: set asynchronous balanced mode
UA, B → A: unnumbered acknowledgment
Data transfer: I-frames and S-frames
DISC, A → B: disconnect, UA from B confirms
Book figure: UA from B carries address A → B, a response carries its sender's address
11.3.2
Common U-frames
Frame | Meaning | Code bits | Byte
SABM | Set asynchronous balanced mode | 11, 100 | 0x2F
SNRM | Set normal response mode | 00, 001 | 0x83
UA | Unnumbered acknowledgment | 00, 110 | 0x63
DISC | Disconnect | 00, 010 | 0x43
DM | Disconnected mode | 11, 000 | 0x0F
FRMR | Frame reject | 10, 001 | 0x87
UI | Unnumbered information, PPP's 0x03 | 00, 000 | 0x03
Code bits: 2 before P/F, 3 after. Byte with P/F = 0, bit 1 sent first
Figure 11.18
Example of connection and disconnection
Notes: Figure 11.18 builds in 5 clicks: SABM, UA, data transfer, DISC, UA.

## Slide 15
Example 11.6
Piggybacking with and without error
a. No error
A → B: I0, I1 with N(R) = 0, nothing from B yet
B → A: I0, I1, I2 with N(R) = 2, A's 0 and 1 received
A has no data: RR 3 acknowledges B's 0, 1, 2
b. Error
B's I1 lost, I2 out of order → discarded
A → B: REJ 1, a NAK: resend from 1 (Go-Back-N)
B resends I1, I2 → A answers RR 3
Book figure: discarded I2 shows N(R) = 2 → 0
Three frames outstanding: HDLC is not Stop-and-Wait
Figure 11.19
Example of piggybacking with and without error
Notes: Figure 11.19 builds in 13 clicks: six frames of case a, then seven frames of case b.

## Slide 16
11.4
PPP services
Point-to-Point Protocol: RFC 1661 (1994)
Book: most users reach the ISP by dial-up modem
Dial-up nearly gone, PPP lives on in PPPoE, L2TP, cellular modems
Provides: frame format, link negotiation (LCP), several network layers (one NCP each)
Optional authentication: PAP, CHAP, later EAP
Address configuration: IPCP gives the user an address
Multilink PPP: an extension (RFC 1990), not a new version
Does not provide: flow control, error recovery, multipoint addressing
CRC detects, bad frame silently dropped
Book: "packets out of order" → a single link keeps order: frames get lost, not reordered
11.4.2
PPP framing
Flag 0x7E, Address 0xFF (all stations), Control 0x03 (HDLC UI)
Protocol: 2 bytes, 1 if compression negotiated
Payload: up to 1500 bytes by default (MRU)
FCS: CRC-16, or CRC-32 if negotiated
Asynchronous links (RFC 1662): send 0x7D, then the byte XOR 0x20
7E → 7D 5E, 7D → 7D 5D
Bytes below 0x20 escaped by default, ACCM option relaxes it
Bit-synchronous links: HDLC bit stuffing instead
Padding optional: flags mark the end (book: "needed")
Figure 11.20
PPP frame format

## Slide 17
11.4.3
Transition phases
Dead: no carrier, line quiet
Establish: carrier detected, LCP negotiates options
Authenticate: only if agreed, PAP or CHAP, failure → Terminate
Network: NCP, e.g. IPCP, configures the network layer
Open: data transfer
Terminate: LCP Terminate-Request and Terminate-Ack, carrier dropped → Dead
RFC 1661 names: Link Dead, Establishment, Authentication, Network-Layer Protocol, Termination
Figure 11.21
Transition phases
11.4.4
LCP packet
Carried with Protocol 0xC021
Code: packet type (Table 11.1)
ID: matches a reply to its request
Length: whole LCP packet
Information: options as type, length, data
Figure 11.23
LCP packet encapsulated in a frame

## Slide 18
Table 11.1
LCP packets
Code | Packet type | Description
0x01 | Configure-request | Contains the list of proposed options and their values
0x02 | Configure-ack | Accepts all options proposed
0x03 | Configure-nak | Announces that some options are not acceptable
0x04 | Configure-reject | Announces that some options are not recognized
0x05 | Terminate-request | Request to shut down the line
0x06 | Terminate-ack | Accept the shutdown request
0x07 | Code-reject | Announces an unknown code
0x08 | Protocol-reject | Announces an unknown protocol
0x09 | Echo-request | A type of hello message to check if the other end is alive
0x0A | Echo-reply | The response to the echo-request message
0x0B | Discard-request | A request to discard the packet
Table 11.2
Common options
Option | Default
Maximum receive unit | 1500
Authentication protocol | None
Protocol field compression | Off
Address and control field compression | Off
11.4.4
Code groups
1 to 4: configuration (Establish)
5, 6: termination
7 to 11: monitoring, debugging
11.4.4
Option negotiation
Configure-Request: lists proposed options
Ack: all accepted, Nak: some values unacceptable, counter-proposal, Reject: some options unknown
Echo-Request and Echo-Reply: keepalive, e.g. PPPoE sessions

## Slide 19
11.4.4
Multiplexing in PPP
One link, several protocols: told apart by the Protocol field
LCP 0xC021: link setup, options, keepalive, teardown
Authentication: PAP 0xC023, CHAP 0xC223
NCPs: IPCP 0x8021, IPv6CP 0x8057, …
Data: IPv4 0x0021, IPv6 0x0057
Pattern: NCP 0x8xxx configures data 0x0xxx
NCP packets configure only: never carry user data
One LCP, two classic APs, one NCP per network layer
Figure 11.22
Multiplexing in PPP

## Slide 20
11.4.4
PAP
Password Authentication Protocol: RFC 1334, Protocol 0xC023
Two steps
User → system: user name + password
System → user: Authenticate-Ack or Authenticate-Nak
Codes: 1 Request, 2 Ack, 3 Nak
Password in clear text: anyone on the link reads it
Book figure: Ack and Nak carry Msg-Length + Message, not a user name
Figure 11.24
PAP packets encapsulated in a PPP frame
Today
PAP and CHAP now
PPPoE logins: PAP or CHAP still carry the subscriber account
MS-CHAPv2: broken in 2012, avoid
PAP: only inside an encrypted tunnel

## Slide 21
11.4.4
CHAP
Challenge Handshake Authentication Protocol: RFC 1994, Protocol 0xC223
Three-way handshake
System → user: Challenge, a fresh random value
User → system: Response = MD5(ID, secret, challenge)
System computes the same → Success or Failure
Password never crosses the link, replayed response useless
Codes: 1 Challenge, 2 Response, 3 Success, 4 Failure
Weakness: both ends store the secret in clear, MD5 dated
Figure 11.25
CHAP packets encapsulated in a PPP frame
Today
EAP, the successor born in PPP
EAP (RFC 2284, 1998, now RFC 3748): one framework, many methods
Now in: 802.1X Wi-Fi and Ethernet (WPA2/WPA3-Enterprise), 5G (EAP-AKA′)

## Slide 22
11.4.4
NCP, IPCP, data, Multilink
One NCP per network layer: IPCP 0x8021, IPv6CP 0x8057, OSI 0x8023, Xerox NS IDP 0x8025
IPCP: LCP codes 1 to 7 (Table 11.3), options: user IP address, DNS servers (RFC 1877)
IPv6CP: only a 64-bit interface identifier, prefix via SLAAC or DHCPv6
User data: Protocol 0x0021 for IPv4 (0x0057 IPv6, 0x0023 OSI)
Multilink PPP (RFC 1990): one logical link over several links, fragments with Protocol 0x003D, sequence number, begin and end bits
Figure 11.26
IPCP packet encapsulated in PPP frame
Table 11.3
Code values for IPCP packets
Code | IPCP packet
0x01 | Configure-request
0x02 | Configure-ack
0x03 | Configure-nak
0x04 | Configure-reject
0x05 | Terminate-request
0x06 | Terminate-ack
0x07 | Code-reject
Figure 11.27
IP datagram encapsulated in a PPP frame
Figure 11.28
Multilink PPP

## Slide 23
Example 11.7
A PPP session
Establish: LCP Configure-Request, Configure-Ack
Options: PAP, address and control field compression
Authenticate: PAP Request, Ack
Network: IPCP Configure-Request, Configure-Ack
Data transfer: IP packets, Protocol 0x0021
Terminate: LCP Terminate-Request, Terminate-Ack
IPCP alone can close: LCP stays up for another NCP
Book figure errors
PAP Ack: code 02, carries a Message, not a Name
LCP frames always keep FF 03, even after compression is agreed
Figure 11.29
An example
Notes: Figure 11.29 builds in 5 clicks: establish, authenticate, network, data transfer, terminate.

## Slide 24
Today
PPP today
Dial-up modem PPP: nearly gone
PPPoE (RFC 2516): PPP sessions over Ethernet, DSL and many fiber ISPs
6-byte PPPoE + 2-byte PPP header → IP MTU 1492, RFC 4638 allows 1500
LCP Echo as keepalive
L2TP (RFC 2661, RFC 3931): PPP tunneled over IP, wholesale broadband, VPNs
Cellular: PPP between host and modem (AT commands), no PPP in the LTE and 5G core
New
PPPoE encapsulation and the 1492-byte MTU
Ethernet payload ≤ 1500 bytes
Ethernet
header
PPPoE
header
PPP
Protocol
IP packet
FCS
14 bytes
6
2
≤ 1492 = 1500 − 6 − 2
4
Today
Framing and error control across today's links
Link | Frame boundary | Error control
HDLC (LAPB) | Flag + bit stuffing | CRC-16, Go-Back-N with REJ
PPP, PPPoE | Flag + byte stuffing, or Ethernet framing (PPPoE) | CRC, discard only
Ethernet | Preamble + SFD, PHY code groups | CRC-32, discard only
Wi-Fi | PHY length field, A-MPDU delimiters | CRC-32, ACK and Block Ack
5G NR | Grant size (DCI), MAC subheaders | CRC-24, HARQ + RLC ARQ
Bluetooth LE | Access address + length field | CRC-24, Stop-and-Wait (SN, NESN)

## Slide 25
Errata
Corrections to the textbook and the original slides (1 of 2)
Where | Printed | Corrected
Book 11.1.1, fixed size | size itself is the delimiter | boundary must be found first (ATM: HEC hunting)
Book 11.1.1, byte stuffing | 16- and 32-bit Unicode characters conflict with it | stuffing ignores content: any byte stream works
Book 11.1.2 | CRC added to the frame header | CRC in the trailer (FCS)
Book Figure 11.6 and text | caption: connectionless and connection-oriented service, text: three states, event 1 → action 3 | generic FSM example: two states, event 2 → action 3
Book 11.2 | Go-Back-N, Selective Repeat gone from the data-link layer | alive: Wi-Fi Block Ack, LTE and NR RLC, LAPB REJ
Book 11.3, deck slide 32 | HDLC implements Stop-and-Wait | sliding window: up to 7 (127) outstanding, REJ, SREJ
Book 11.3, deck objectives | HDLC is the basis of Ethernet | only 802.2 LLC, Ethernet has no flags or stuffing
Book 11.3.2 | U-frame control field paragraph printed twice | printed once
Deck slide 7 | ATM: 53 bytes packet | 53-byte cell
Summary
Chapter 11 in one panel
Framing: flags + byte or bit stuffing, fixed size + HEC hunting, or length fields
Stop-and-Wait: 1-bit numbers stop duplicates, wastes long links
HDLC: I, S, U frames, N(S) and N(R), RR, RNR, REJ, SREJ, sliding window
PPP: byte-stuffed HDLC-like frame, LCP → authentication → NCP → data

## Slide 26
Errata
Corrections to the textbook and the original slides (2 of 2)
Where | Printed | Corrected
Book Figure 11.18 | UA from node B carries address A | B: a response carries its sender's address
Book Figure 11.19b | discarded I-frame 2 with N(R) = 2 | N(R) = 0, as in its resend
Book 11.4, deck slide 43 | most users connect over dial-up modems | PPPoE, L2TP, cellular modems (Today panel)
Book 11.4.1 | Multilink PPP is a new version of PPP | an extension (RFC 1990)
Book 11.4.1 | no sequence numbers → out-of-order packets | single link keeps order: loss, not reordering
Book 11.4.2 | padding needed, no length field | padding optional (RFC 1661), flags mark the end
Book 11.4.2, deck slide 45 | escape = insert 01111101 | insert 0x7D, then send the byte XOR 0x20 (RFC 1662)
Book Figure 11.24 | Ack and Nak carry user name | Msg-Length + Message (RFC 1334)
Book Figure 11.29 | Authenticate-ack code 01 with Name, LCP Terminate without Address and Control | code 02 with Message, LCP always keeps FF 03 (RFC 1661)
EXPLORE
Try it
Try it: bit-stuff 0111111011111100 by hand, then unstuff it
Try it: Stop-and-Wait over a 36,000 km satellite hop at 10 Mbps: utilization?
Try it: capture a PPPoE login in Wireshark: PADI, PADO, LCP, PAP or CHAP, IPCP