## Slide 1: Section 3.8: MTU and Path MTU
서경진
2015010493

## Slide 2: MTU and Path MTU
MTU(maximum transmission unit)
  호스트간에 데이터 패킷이 전송될때 라우터에서 한번에 처리되는 데이터의 사이즈.
  하나의 프레임이나 패킷이 한 번에 전송이 될 때 이더넷을 통과할 수 있는 데이터의 크기를 말한다. 이 값은 아래와 같이 어떤 프로토콜인가에 따라 다르다.
Path MTU(maximum transmission unit)
  상호간의 데이터 전송 경로상 셋팅되있는 MTU값중에 가장 작은 MTU값을 Path MTU라고 정의
  두 호스터간 경로에서 가장 작은 MTU값을 말한다. 이 값은 라우팅 경로가 매번 일정하지 않고 수시로 바뀌므로 이 값도 라우팅 령로에 따라 수시로 변경될 수 있다. 그리고 같은 호스트 사이라 하더라도 두 호스트간의 트래픽 종류에 따라 값이 달라지게 된다.

## Slide 3: MTU
A limit on the size of the frame available for carrying the PDUs of higher-layer protocols in many link-layer networks such as Ethernet.
This usually limits the number of payload bytes to about 1500 for Ethernet and often the same amount for PPP in order to maintain compatibility with Ethernet.
Notes: This characteristic of the link layer is called the maximum transmission unit (MTU).
이러한 링크 레이어의 특성은 최대 전송 단위 (MTU)라고 합니다.

## Slide 4
MTU A
MTU B
MTU C
When two hosts communicate across multiple networks, each link can have a different MTU.
The minimum MTU across the network path comprising all of the links is called the path MTU.
The path MTU between any two hosts need not be constant over time.

## Slide 5
[RFC1191] specifies the path MTU discovery (PMTUD) mechanism for IPv4, and [RFC1981] describes it for IPv6.
A complementary approach that avoids some of the issues with these mechanisms is described in [RFC4821].