## Slide 1: 4.1 Introduction
IP protocol is designed to provide interoperability of packet switching across a large variety of physical network types
Doing so requires, among other things, converting between the addresses used by the network-layer software and those interpreted by the underlying network hardware
  Generally, network interface hardware has one primary hardware address (e.g., a 48-bit value for an Ethernet or 802.11 wireless interface)
  But a conventional IPv4 network works with its own addresses: 32-bit IPv4 addresses
  Knowing a host’s IP address is insufficient for the system to send a frame to that host efficiently on networks where hardware addresses are used
For TCP/IP networks, the Address Resolution Protocol (ARP) provides a dynamic mapping between IPv4 addresses and the hardware addresses used by various network technologies
  ARP is used with IPv4 only; IPv6 uses the Neighbor Discovery Protocol, which is incorporated into ICMPv6

## Slide 2: 4.1 Introduction
Network-layer and link-layer addresses are assigned by different authorities
  For network hardware, the primary address is defined by the manufacturer of the device and is stored in permanent memory within the device
  IP address assigned to a network interface is installed by the user or network administrator, and can be changed
Address resolution is the process of discovering the mapping from one address to another
  For the TCP/IP protocol suite using IPv4, this is accomplished by running the ARP
  ARP is a generic protocol; it is designed to support mapping between a wide variety of address types
  In practice, however, it is almost always used to map between 32-bit IPv4 addresses and Ethernet-style 48-bit MAC addresses

## Slide 3: 4.1 Introduction
ARP provides a dynamic mapping from a network-layer address to a corresponding hardware address
It happens automatically and adapts to changes over time without requiring reconfiguration by a system administrator
  If a host has its network interface card changed, thereby changing its hardware address (but retaining its assigned IP address), ARP would continue to operate properly after some delay
A related protocol that provides the reverse mapping from ARP, called RARP, was used by systems lacking a disk drive (normally diskless workstations or X terminals)
  It is rarely used today and requires manual configuration by the system administrator