## Slide 1: 9.5 Attacks involving IGMP and MLD
IGMP and MLD are signaling protocols --- attacks using these protocols primarily are either DoS attacks or resource utilization attacks
A simple DoS attack can be mounted by sending IGMP or MLD to subscribe to a large number of high bandwidth multicast groups
  Doing so can cause bandwidth exhaustion, leading to a denial of service
A more complex attack can be mounted by generating requests using a relatively low IP address
  The attacker is elected to be the querier for the link and can advertise its own robustness variable, query interval, and maximum response time that will be adopted by the other multicast routers
  If the maximum response time is very small, hosts are induced to send reports rapidly, using CPU resources

## Slide 2: 9.5 Attacks involving IGMP and MLD
Fragmented IGMP packets have been used to induce crashes in certain operating systems
More recently, specially crafted IGMP or MLD packets using SSM information have been used to induce remote code execution bugs
Overall, the impact of IGMP or MLD vulnerabilities tends to be somewhat less than with other protocols, as multicast tends to be supported only in the local area
As a result, remote attackers lacking on-link access to the target LAN are likely to be limited