## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Chapter 6 The Link Layer
and LANs
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2023
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
Updated datacenter slides, day-in-the-life
8.2 (July 2023): changes from 8.0
Minor updates throughout, including removal of master/slave
A few new slides added (transportation analogy, UMass LAN example, extended LANs)
Couple of not-used slides now hidden.

## Slide 2: Link layer and LANs: our goals
understand principles behind link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  local area networks: Ethernet, VLANs
datacenter networks
instantiation, implementation of various link layer technologies

## Slide 3: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 4: Link layer: introduction
terminology:
hosts, routers: nodes
communication channels that connect adjacent nodes along communication path: links
  wired , wireless
  LANs
layer-2 packet: frame, encapsulates datagram
mobile network
enterprise
network
national or global ISP
datacenter
network
link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link

## Slide 5: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., WiFi on first link, Ethernet on next link
each link protocol provides different services
  e.g., may or may not provide reliable data transfer over link

## Slide 6: Transportation analogy
transportation analogy:
trip from Princeton to Lausanne
  limo: Princeton to JFK
  plane: JFK to Geneva
  train: Geneva to Lausanne
tourist = datagram
transport segment = communication link
transportation mode = link-layer protocol
travel agent = routing algorithm
Princeton
JFK
Geneva
Lausanne

## Slide 7: Link layer: services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses in frame headers identify source, destination (different from IP address!)
reliable delivery between adjacent nodes
  we already know how to do this!
  seldom used on low bit-error links
  wireless links: high error rates
    Q: why both link-level and end-end reliability?
…
…
Cable access
cellular
WiFi
Ethernet LANs
Notes: reliable delivery between adjacent nodes
Not always
Rdt likes we studied in transport layer
Reliable is not as important is correctness. How is correctness assured?
Wireless is subjected to noise, interference and has high bit error rate.
Why

## Slide 8: Link layer: services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects errors, signals retransmission, or drops frame
error correction:
  receiver identifies and corrects bit error(s) without retransmission
half-duplex and full-duplex:
  with half duplex, nodes at both ends of link can transmit, but not at same time
…
…
Cable access
cellular
WiFi
Ethernet LANs
Notes: Error detection in the link layer is usually more sophisticated and is implemented in hardware. Error correction is similar to error detection, except that a receiver not only detects when bit errors have occurred in the frame but also deter- mines exactly where in the frame the errors have occurred (and then corrects these errors).

## Slide 9: Host link-layer implementation
in each-and-every host
link layer implemented on-chip or in network interface card (NIC)
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
cpu
memory
host bus
(e.g., PCI)
network interface
application
transport
network
link
link
physical
Notes: The Ethernet capabilities are either integrated into the motherboard chipset or implemented via a low-cost dedicated Ethernet chip. For the most part, the link layer is implemented on a chip called the network adapter, also sometimes known as a network interface controller (NIC). The network adapter implements many link layer services including framing, link access, error detection, and so on. Thus, much of a link-layer controller’s functionality is implemented in hardware. For example, Intel’s 700 series adapters [Intel 2020] implements the Ethernet protocols we’ll study in Section 6.5; the Atheros AR5006 [Atheros 2020] controller implements the 802.11 WiFi protocols we’ll study in Chapter 7.
Figure 6.2 shows that while most of the link layer is implemented in hardware, part of the link layer is implemented in software that runs on the host’s CPU. The software components of the link layer implement higher-level link-layer functionality such as assembling link-layer addressing information and activating the controller hardware. On the receiving side, link-layer software responds to con- troller interrupts (for example, due to the receipt of one or more frames), handling error conditions and passing a datagram up to the network layer. Thus, the link layer is a combination of hardware and software

## Slide 10: Interfaces communicating
controller
physical
memory
CPU
controller
physical
cpu
memory
application
transport
network
link
link
physical
application
transport
network
link
link
physical
sending side:
encapsulates datagram in frame
adds error checking bits, reliable data transfer, flow control, etc.
receiving side:
looks for errors, reliable data transfer, flow control, etc.
extracts datagram, passes to upper layer at receiving side
linkh
linkh
datagram
datagram
datagram

## Slide 11: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 12: Error detection
EDC: error detection and correction bits (e.g., redundancy)
D: data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction
datagram
D
EDC
d data bits
bit-error prone link
D’
EDC’
all
bits in D’
OK
?
N
detected
error
otherwise
datagram

## Slide 13: Parity checking
single bit parity:
detect single bit errors
0111000110101011
1
parity bit
d data bits
Can detect and correct errors (without retransmission!)
two-dimensional parity: detect and correct single bit errors
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
1 0 1 0 1
0 1 1 1 0
1 0 1 0 1
1 1 1 1 0
1
0
1
0
no errors:
parity
error
parity
error
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 0
1 0 1 0 1 0
detected
and
correctable
single-bit
error:
Even/odd parity: set parity bit so there is an even/odd number of 1’s
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
At receiver:
compute parity of d received bits
compare with received parity bit – if different than error detected

## Slide 14: Internet checksum (review, see section 3.3)
sender:
treat contents of UDP segment (including UDP header fields and IP addresses) as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment content
checksum value put into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  not equal - error detected
  equal - no error detected. But maybe errors nonetheless? More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment

## Slide 15: Cyclic Redundancy Check (CRC)
more powerful error-detection coding
D: data bits (given, think of these as a binary number)
G: bit pattern (generator), of r+1 bits (given, specified in CRC standard)
sender: compute r CRC bits, R, such that <D,R> exactly divisible by G (mod 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
  widely used in practice (Ethernet, 802.11 WiFi)
<D,R> = D 2r XOR R
*
formula for these bits
r CRC bits
d data bits
D
R
bits to send

## Slide 16: Cyclic Redundancy Check (CRC): example
Sender wants to compute R such that:
  D . 2r XOR R = nG
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
D.2r
G
R = remainder [ ]
... or equivalently (XOR R both sides):
  D . 2r = nG XOR R
... which says:
if we divide D . 2r by G, we want remainder R to satisfy:
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 0
1 0 1 0
0 1 1
0 1 1
D
R
1 0 0 1
G
0 0 0
1 0 1 1 1 0
2r (here, r=3)
*
1
0
1
algorithm for
computing R

## Slide 17: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 18: Multiple access links, protocols
two types of “links”:
point-to-point
  point-to-point link between Ethernet switch, host
  PPP for dial-up access
broadcast (shared wire or medium)
  old-school Ethernet
  upstream HFC in cable-based access network
  802.11 wireless LAN, 4G/4G. satellite
shared radio: satellite
humans at a cocktail party
(shared air, acoustical)
shared radio: WiFi
shared wire (e.g.,
cabled Ethernet)
shared radio: 4G/5G

## Slide 19: Multiple access protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination
multiple access protocol

## Slide 20: An ideal multiple access protocol
given: multiple access channel (MAC) of rate R bps
desiderata:
  1. when one node wants to transmit, it can send at rate R.
  2. when M nodes want to transmit, each can send at average rate R/M
  3. fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. simple

## Slide 21: MAC protocols: taxonomy
three broad classes:
channel partitioning
  divide channel into smaller “pieces” (time slots, frequency, code)
  allocate piece to node for exclusive use
random access
  channel not divided, allow collisions
  “recover” from collisions
“taking turns”
  nodes take turns, but nodes with more to send can take longer turns

## Slide 22: Channel partitioning MAC protocols: TDMA
TDMA: time division multiple access
access to channel in “rounds”
each station gets fixed length slot (length = packet transmission time) in each round
unused slots go idle
example: 6-station LAN, 1,3,4 have packets to send, slots 2,5,6 idle
1
3
4
1
3
4
6-slot
frame
6-slot
frame

## Slide 23: Channel partitioning MAC protocols: FDMA
FDMA: frequency division multiple access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
unused transmission time in frequency bands go idle
example: 6-station LAN, 1,3,4 have packet to send, frequency bands 2,5,6 idle
frequency bands
time
FDM cable

## Slide 24: Random access protocols
when node has packet to send
  transmit at full channel data rate R
  no a priori coordination among nodes
two or more transmitting nodes: “collision”
random access protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  ALOHA, slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 25: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot
  if collision: node retransmits frame in each subsequent slot with probability p until success
randomization – why?
t0
t0+1

## Slide 26: Slotted ALOHA
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E
C: collision
S: success
E: empty
Notes: Slotted ALOHA would appear to have many advantages. Unlike channel partitioning, slotted ALOHA allows a node to transmit continuously at the full rate, R, when that node is the only active node. (A node is said to be active if it has frames to send.) Slotted ALOHA is also highly decentralized, because each node detects collisions and independently decides when to retransmit. (Slotted ALOHA does, however, require the slots to be synchronized in the nodes; shortly we’ll discuss an unslotted version of the ALOHA protocol, as well as CSMA protocols, none of which require such synchronization.) Slotted ALOHA is also an extremely simple protocol.

## Slide 27: Slotted ALOHA: efficiency
efficiency: long-run fraction of successful slots (many nodes, all with many frames to send)
suppose: N nodes with many frames to send, each transmits in slot with probability p
  prob that given node has success in a slot = p(1-p)N-1
  prob that any node has a success = Np(1-p)N-1
  max efficiency: find p* that maximizes Np(1-p)N-1
  for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives:
max efficiency = 1/e = .37
at best: channel used for useful transmissions 37% of time!
Notes: Suppose there are N nodes. Then the probability that a given slot is a successful slot is the probability that one of the nodes transmits and that the remaining N - 1 nodes do not transmit. The probability that a given node transmits is p; the probability that the remaining nodes do not transmit is (1 - p)N-1. Therefore, the probability a given node has a success is p(1 - p)N-1. Because there are N nodes, the probability that any one of the N nodes has a success is Np(1 - p)N - 1.
only 37 percent of the slots do useful work. Thus, the effective transmission rate of the channel is not R bps but only 0.37 R bps! A similar analysis also shows that 37 percent of the slots go empty and 26 percent of slots have collisions.

## Slide 28: Pure ALOHA
unslotted Aloha: simpler, no synchronization
  when frame first arrives: transmit immediately
collision probability increases with no synchronization:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]
t0 + 1
t0 - 1
t0
will overlap
with end of
i’s frame
will overlap
with start of
i’s frame
pure Aloha efficiency: 18% !

## Slide 29: CSMA (carrier sense multiple access)
simple CSMA: listen before transmit:
  if channel sensed idle: transmit entire frame
  if channel sensed busy: defer transmission
human analogy: don’t interrupt others!
CSMA/CD: CSMA with collision detection
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
  collision detection easy in wired, difficult with wireless
human analogy: the polite conversationalist

## Slide 30: CSMA: collisions
collisions can still occur with carrier sensing:
  propagation delay means two nodes may not hear each other’s just-started transmission
collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability
spatial layout of nodes

## Slide 31: CSMA/CD:
CSMA/CD reduces the amount of time wasted in collisions
  transmission aborted on collision detection
spatial layout of nodes

## Slide 32: Ethernet CSMA/CD algorithm
Ethernet receives datagram from network layer, creates frame
If Ethernet senses channel:
  if idle: start frame transmission.
  if busy: wait until channel idle, then transmit
If entire frame transmitted without collision - done!
If another transmission detected while sending: abort, send jam signal
After aborting, enter binary (exponential) backoff:
  after mth collision, chooses K at random from {0,1,2, …, 2m-1}. Ethernet waits K·512 bit times, returns to Step 2
  more collisions: longer backoff interval
Notes: For Ethernet, the actual amount of time a node waits is K # 512 bit times (i.e., K times the amount of time needed to send 512 bits into the Ethernet) and the maxi- mum value that n can take is capped at 10.

## Slide 33: CSMA/CD efficiency
Tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!
Notes: let dprop denote the maximum time it takes signal energy to propagate between any two adapters. Let dtrans be the time to transmit a maximum-size frame (approximately 1.2 msecs for a 10 Mbps Ethernet).

## Slide 34: “Taking turns” MAC protocols
channel partitioning MAC protocols:
  share channel efficiently and fairly at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“taking turns” protocols
  look for best of both worlds!

## Slide 35: “Taking turns” MAC protocols
polling:
centralized controller “invites” other nodes to transmit in turn
typically used with “dumb” devices
concerns:
  polling overhead
  latency
  single point of failure (master)
Bluetooth uses polling
centralized controller
client devices
poll
data
data
Notes: The first drawback is that the protocol introduces a polling delay—the amount of time required to notify a node that it can transmit. If, for example, only one node is active, then the node will transmit at a rate less than R bps, as the master node must poll each of the inactive nodes in turn each time the active node has sent its maximum number of frames. The second drawback, which is potentially more serious, is that if the master node fails, the entire channel becomes inoperative. The Bluetooth protocol, which we will study in Section 6.3, is an example of a polling protocol.

## Slide 36: “Taking turns” MAC protocols
token passing:
control token message explicitly passed from one node to next, sequentially
  transmit while holding token
concerns:
  token overhead
  latency
  single point of failure (token)
T
data
(nothing
to send)
T
Notes: no master node
But it has its problems as well. For example, the failure of one node can crash the entire channel. Or if a node accidentally neglects to release the token, then some recovery procedure must be invoked to get the token back in circulation.

## Slide 37: Cable access network: FDM, TDM and random access!
cable headend
CMTS
ISP
cable modem
termination system
cable
modem
splitter
…
…
Internet frames, TV channels, control transmitted
downstream at different frequencies
multiple downstream (broadcast) FDM channels: up to 1.6 Gbps/channel
  single CMTS transmits into channels
multiple upstream channels (up to 1 Gbps/channel)
  multiple access: all users contend (random access) for certain upstream channel time slots; others assigned TDM

## Slide 38: Cable access network:
DOCSIS: data over cable service interface specification
FDM over upstream, downstream frequency channels
TDM upstream: some slots assigned, some have contention
  downstream MAP frame: assigns upstream slots
  request for upstream slots (and data) transmitted random access (binary backoff) in selected slots
Residences with cable modems
Downstream channel i
Upstream channel j
MAP frame for
Interval [t1, t2]
t1
t2
Assigned minislots containing cable modem
upstream data frames
Minislots containing
minislots request frames
cable headend
CMTS

## Slide 39: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, FDDI, token ring

## Slide 40: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 41: MAC addresses
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
  e.g.: 128.119.40.136
MAC (or LAN or physical or Ethernet) address:
  function: used “locally” to get frame from one interface to another physically-connected interface (same subnet, in IP-addressing sense)
  48-bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
  e.g.: 1A-2F-BB-76-09-AD

## Slide 42: MAC addresses
each interface on LAN
has unique 48-bit MAC address
has a locally unique 32-bit IP address (as we’ve seen)
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or wireless)
137.196.7/24
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23

## Slide 43: MAC addresses
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address: portability
  can move interface from one LAN to another
  recall IP address not portable: depends on IP subnet to which node is attached

## Slide 44: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
Question: how to determine interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23
ARP
ARP
ARP
ARP
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)

## Slide 45: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A broadcasts ARP query, containing B's IP addr
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
1
Source MAC: 71-65-F7-2B-08-53
Source IP: 137.196.7.23
Target IP address: 137.196.7.14
…
1
Ethernet frame (sent to FF-FF-FF-FF-FF-FF)

## Slide 46: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
B replies to A with ARP response, giving its MAC address
2
Target IP address: 137.196.7.14
Target MAC address:
58-23-D7-FA-20-B0
…
2
ARP message into Ethernet frame (sent to 71-65-F7-2B-08-53)

## Slide 47: ARP protocol in action
58-23-D7-FA-20-B0
137.196.7.14
B
C
D
TTL
71-65-F7-2B-08-53
137.196.7.23
A
ARP table in A
IP addr
MAC addr
TTL
example: A wants to send datagram to B
  B’s MAC address not in A’s ARP table, so A uses ARP to find B’s MAC address
A receives B’s reply, adds B entry into its local ARP table
3
137.196.
7.14
58-23-D7-FA-20-B0
500

## Slide 48: Routing to another subnet: addressing
walkthrough: sending a datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame) levels
R
A
B
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
  assume that:
    A knows B’s IP address
    A knows IP address of first hop router, R (how?)
    A knows R’s MAC address (how?)

## Slide 49: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame containing A-to-B IP datagram
  R's MAC address is frame’s destination
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 50: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 51: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
R determines outgoing interface, passes datagram with IP source A, destination B to link layer
R creates link-layer frame containing A-to-B IP datagram. Frame destination address: B's MAC address
IP
Eth
Phy

## Slide 52: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
transmits link-layer frame
R determines outgoing interface, passes datagram with IP source A, destination B to link layer
R creates link-layer frame containing A-to-B IP datagram. Frame destination address: B's MAC address

## Slide 53: Routing to another subnet: addressing
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP
Eth
Phy
B receives frame, extracts IP datagram destination B
B passes datagram up protocol stack to IP
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 54: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 55: Ethernet
“dominant” wired LAN technology:
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 400 Gbps
single chip, multiple speeds (e.g., Broadcom BCM5761)
Metcalfe’s Ethernet sketch
https://www.uspto.gov/learning-and-resources/journeys-innovation/audio-stories/defying-doubters
Bob Metcalfe: Ethernet co-inventor,
2022 ACM Turing Award recipient

## Slide 56: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
bus: coaxial cable
switched
switched: prevails today
  active link-layer 2 switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)

## Slide 57: Ethernet frame structure
sending interface encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
preamble:
used to synchronize receiver, sender clock rates
7 bytes of 10101010 followed by one byte of 10101011

## Slide 58: Ethernet frame structure (more)
dest.
address
source
address
data (payload)
CRC
preamble
type
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g., ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol
  mostly IP but others possible, e.g., Novell IPX, AppleTalk
  used to demultiplex up at receiver
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped

## Slide 59: Ethernet: unreliable, connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn’t send ACKs or NAKs to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff

## Slide 60: 802.3 Ethernet standards: link & physical layers
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister pair) physical layer
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, ... 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps, 80 Gbps

## Slide 61: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 62: Ethernet switch
Switch is a link-layer device: takes an active role
  store, forward Ethernet (or other type of) frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent: hosts unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 63: Switch: multiple simultaneous transmissions
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, so:
  no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions

## Slide 64: Switch: multiple simultaneous transmissions
switch with six interfaces (1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, so:
  no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
  but A-to-A’ and C to A’ can not happen simultaneously

## Slide 65: Switch forwarding table
A
A’
B
B’
C
C’
1
2
3
4
5
6
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 66: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table

## Slide 67: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving interface */

## Slide 68: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
A’ A
A’
4
60
frame destination, A’, location unknown:
flood
destination A location known:
selectively send
on just one link

## Slide 69: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 70: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 71: UMass Campus Network - Detail
...
Agg2
...
Agg1
building
closets
to off campus
Wireless
Controller
...
Wireless
Controller
border
border
core
Core
...
Agg3
...
Agg4
firewall
data center
WiFi
UMass network:
4 firewalls
10 routers
2000+ network switches
6000 wireless access points
30000 active wired network jacks
55000 active end-user wireless devices
… all built, operated, maintained by ~15 people

## Slide 72: UMass Campus Network - Detail
...
Agg2
...
Agg1
building
closets
to off campus
Wireless
Controller
...
Wireless
Controller
border
border
core
Core
...
Agg3
...
Agg4
firewall
data center
WiFi
eBGP
iBGP
IS-IS
IS-IS
Ethernet
layer-2
switching
intra-domain
routing
inter-domain
routing
Protocols
Link Speeds
10G;
100G pending
40G & 100G
40G
10G & 1G

## Slide 73: Switches vs. routers
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram
6-73
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses

## Slide 74: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 75: Virtual LANs (VLANs): motivation
Computer
Science
EE
Q: what happens as LAN sizes scale, users change point of attachment?
single broadcast domain:
  scaling: all layer-2 broadcast traffic (ARP, DHCP, unknown MAC) must cross entire LAN
  efficiency, security, privacy issues

## Slide 76: Virtual LANs (VLANs): motivation
administrative issues:
CS user moves office to EE - physically attached to EE switch, but wants to remain logically attached to CS switch
Computer
Science
EE
single broadcast domain:
  scaling: all layer-2 broadcast traffic (ARP, DHCP, unknown MAC) must cross entire LAN
  efficiency, security, privacy, efficiency issues
Q: what happens as LAN sizes scale, users change point of attachment?

## Slide 77: Port-based VLANs
1
8
2
7
9
16
10
15
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local Area Network (VLAN)
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
… operates as multiple virtual switches
1
8
2
7
EE (VLAN ports 1-8)
…
9
16
10
15
…
CS (VLAN ports 9-15)

## Slide 78: Port-based VLANs
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 79: VLANS spanning multiple switches
1
8
2
7
9
16
10
15
…
EE (VLAN ports 1-8)
CS (VLAN ports 9-15)
…
5
8
2
7
…
16
1
6
3
4
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports

## Slide 80: 802.1Q VLAN frame format
802.1 Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information
(12 bit VLAN ID field, 3 bit priority field like IP TOS)
Recomputed
CRC
802.1Q frame
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 81: EVPN: Ethernet VPNs (aka VXLANs)
1
8
2
7
9
16
10
15
…
…
Layer-2 Ethernet switches logically connected to each other (e.g., using IP as an underlay)
  Ethernet frames carried within IP datagrams between sites
  “tunneling scheme to overlay Layer 2 networks on top of Layer 3 networks ... runs over the existing networking infrastructure and provides a means to "stretch" a Layer 2 network.” [RFC 7348]
5
8
2
7
…
6
3
4
16
1
Sunnyvale
data center
Bangalore
data center
Ethernet
Ethernet
frame
IP
datagram

## Slide 82: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 83: Multiprotocol label switching (MPLS)
label
Exp
S
TTL
20
3
1
5
goal: high-speed IP forwarding among network of MPLS-capable routers, using fixed length label (instead of shortest prefix matching)
  faster lookup using fixed length identifier
  borrowing ideas from Virtual Circuit (VC) approach
  but IP datagram still keeps IP address!
remainder of Ethernet frame, including IP header with IP source, destination addresses
MPLS header
Ethernet
header
remainder of Ethernet frame, including IP header with IP source, destination addresses

## Slide 84: MPLS capable routers
a.k.a. label-switched router
forward packets to outgoing interface based only on label value (don’t inspect IP address)
  MPLS forwarding table distinct from IP forwarding tables
flexibility: MPLS forwarding decisions can differ from those of IP
  use destination and source addresses to route flows to same destination differently (traffic engineering)
  re-route flows quickly if link fails: pre-computed backup paths

## Slide 85: MPLS versus IP paths
R2
D
R3
R5
A
R6
R4
IP routing: path to destination determined by destination address alone
IP router

## Slide 86: MPLS versus IP paths
R2
D
R3
R5
A
R6
IP router
R4
IP routing: path to destination determined by destination address alone
IP/MPLS router
IP/MPLS entry router (R4) can use different MPLS routes to A based, e.g., on IP source address or other fields
MPLS routing: path to destination can be based on source and destination address
  flavor of generalized forwarding (MPLS 10 years earlier)
  fast reroute: precompute backup routes in case of link failure
R1

## Slide 87: MPLS signaling
modify OSPF, IS-IS link-state flooding protocols to carry info used by MPLS routing:
  e.g., link bandwidth, amount of “reserved” link bandwidth
R2
D
R3
R5
A
R6
R4
modified
link state
flooding
RSVP-TE
entry MPLS router uses RSVP-TE signaling protocol to set up MPLS forwarding at downstream routers
R1

## Slide 88: MPLS forwarding tables
in out out
label label dest interface
6 - A 0
in out out
label label dest interface
10 6 A 1
12 9 D 0
in out out
label label dest interface
8 6 A 0
in out out
label label dest interface
10 A 0
12 D 0
8 A 1
R2
D
R3
R5
A
R6
R4
R1
0
1
0
0
1
0

## Slide 89: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 90: Datacenter networks
10’s to 100’s of thousands of hosts, often closely coupled, in close proximity:
  e-business (e.g. Amazon)
  content-servers (e.g., YouTube, Akamai, Apple, Microsoft)
  search engines, data mining (e.g., Google)
challenges:
  multiple applications, each serving massive numbers of clients
  reliability
  managing/balancing load, avoiding processing, networking, data bottlenecks
Inside a 40-ft Microsoft container, Chicago data center

## Slide 91: Datacenter networks: network elements
Server racks
20- 40 server blades: hosts
Top of Rack (TOR) switch
one per rack
100G-400G Ethernet to blades
Tier-2 switches
connecting to ~16 TORs below
Tier-1 switches
connecting to ~16 T-2s below
Border routers
connections outside datacenter
…
…
…
…
…
…
…
…

## Slide 92: Datacenter networks: network elements
Facebook F16 data center network topology:
https://engineering.fb.com/data-center-engineering/f16-minipack/ (posted 3/2019)

## Slide 93: Datacenter networks: multipath
9
10
11
12
13
14
15
16
two disjoint paths highlighted between racks 1 and 11
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy

## Slide 94: Datacenter networks: application-layer routing
…
…
…
…
…
…
…
…
Load
balancer
Internet
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)

## Slide 95: Datacenter networks: protocol innovations
link layer:
  RoCE: remote DMA (RDMA) over Converged Ethernet
transport layer:
  ECN (explicit congestion notification) used in transport-layer congestion control (DCTCP, DCQCN)
  experimentation with hop-by-hop (backpressure) congestion control
routing, management:
  SDN widely used within/among organizations’ datacenters
  place related services, data as close as possible (e.g., in same rack or nearby rack) to minimize tier-2, tier-1 communication
Google Networking: Infrastructure and Selected Challenges (Slides: https://networkingchannel.eu/google-networking-infrastructure-and-selected-challenges/

## Slide 96: ORION: Google’s new SDN control plane for internal datacenter (Jupiter) + wide area (B4) network
Orion SDN architecture and core apps
routing (intradomain, iBGP), traffic engineering: implemented in applications on top of ORION core
edge-edge flow-based controls (e.g., CoFlow scheduling) to meet contract SLAs
management: pub-sub distributed microservices in Orion core, OpenFlow for switch signaling/monitoring
Note:
no routing protocols, congestion control (partially) also managed by SDN rather than by protocol
are protocols dying?
Notes: Repeat after each reveal: no protocol
Coflows: “a collection of flows between two groups of machines with associated semantics and a collective objective”; [Sigcomm’13, Sigcomm’15, Sigcomm’18]. Not unlike multiprocessor scheduling in the 1980’s

## Slide 97: Link layer, LANs: roadmap
a day in the life of a web request
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
  VLANs
link virtualization: MPLS
data center networking

## Slide 98: Synthesis: a day in the life of a web request
our journey down the protocol stack is now complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 99: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
browser
web page
arriving mobile client attaches to network …
requests web page: www.google.com
scenario:
Sounds
simple!

## Slide 100: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet de-muxed to IP de-muxed, UDP de-muxed to DHCP

## Slide 101: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
DHCP
UDP
IP
Eth
Phy
DHCP
UDP
IP
Eth
Phy
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 102: A day in the life… ARP (before DNS, before HTTP)
router has
ARP server
arriving mobile:
ARP client
DNS
UDP
IP
Eth
Phy
Eth
Phy
ARP
before sending HTTP request, need IP address of www.google.com: DNS
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
ARP
ARP reply

## Slide 103: A day in the life… using DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
Comcast network
68.80.0.0/13
DNS
server
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
de-muxed to DNS
DNS replies to client with IP address of www.google.com
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS

## Slide 104: A day in the life…TCP connection carrying HTTP
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in TCP 3-way handshake) inter-domain routed to web server
TCP connection established!
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in TCP 3-way handshake)

## Slide 105: A day in the life… HTTP request/reply
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed

## Slide 106: Chapter 6: Summary
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
instantiation, implementation of various link layer technologies
  Ethernet
  switched LANS, VLANs
  virtualized networks as a link layer: MPLS
synthesis: a day in the life of a web request

## Slide 107: Chapter 6: let’s take a breath
journey down protocol stack complete (except PHY)
solid understanding of networking principles, practice!
….. could stop here …. but more interesting topics!
  wireless
  security

## Slide 108: Additional Chapter 6 slides

## Slide 109: Pure ALOHA efficiency
P(success by given node) = P(node transmits)
P(no other node transmits in [t0-1,t0]
P(no other node transmits in [t0-1,t0]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n
= 1/(2e) = .18
*
*
*
even worse than slotted Aloha!