## Slide 1: Internet Protocol (IP)
5강

## Slide 2: Overview – IP’s roles
IP is commissioned with two roles:
Overcome the incompatibility between the link layer technologies of the incoming interface and the outgoing interface (“internetworking”)
Determine the outgoing interface + next hop IP address, for an incoming IP datagram to reach the next hop (“forwarding”)

## Slide 3: Internetworking

## Slide 4: IP header

## Slide 5: Some history of IP versions
“TCP” version 1 was designed in 1973 (RFC 675)
“TCP” version 2 was documented in March 1977
In August 1977, Jon Postel realized it was violating the principle of layering
TCP and IP were split, with both being versioned number 3 in the spring of 1978
Stability was added in the fourth revision and that is how we got to IPv4
As the idea of streaming video and other new media become a reality, RFC 1190 was submitted for a formal implementation of IPv5. But IPv4 Internet took off!

## Slide 6: IP header
IHL : length in 4-byte units
  Should be aligned : may need padding bytes at the end of the header
Total length: in bytes
Max length = 65535

## Slide 7: DS & ECN
DS: for QoS
  No hope of this in the general Internet
ECN: Congestion control (more later …)
Rarely used today

## Slide 8: Fragmentation
Id increases by 1 for each datagram from the current host to a given destination IP
Flags: DF, MF
Fragment offset: in 8-byte units

## Slide 10: Path MTU discovery
DF bit set by transport layer (e.g. TCP: default)
  More on ICMP later on

## Slide 11: TTL
Time to live is time to death
Was originally “time” but …

## Slide 12: TTL
Initial value depends on OS, protocol, and kernel version
  Try “ping localhost”
Windows: 128
Linux: 64 or 255
Android: 64 (/proc/sys/net/ipv4/ip_default_ttl)

## Slide 13: Tracert/traceroute
Is exploiting TTL
When a router finds an incoming diagram with TTL=1
ICMP error message is sent back to the source of the killed IP datagram
See Wireshark with displayfilter “ICMP”

## Slide 14: IP header

## Slide 15: Protocol
Transport layer protocol that created this IP datagram
For demultiplexing
TCP=6, UDP=17, ICMP=1, IGMP=2, …

## Slide 16: Internet checksum
Check, sum
1’s complement of 1’s complement sum
  Almost all Internet protocols use it
1’s complement = sign change
S + (-S) = 0: check?

## Slide 17: 1’s vs. 2’s complement notations

## Slide 18: Internet checksum

## Slide 19: Internet checksum

## Slide 20: Checksum offload

## Slide 21: Wireshark and checksum
Checksum validation in Wireshark disabled by default
Due to NIC offloading

## Slide 22: Wireshark and checksum

## Slide 23: Options
TLV format: what’s good about this?
Only a couple remain useful
  Router Alert
Most are security threats
    Filtering rules recommendation: RFC7126
    Try “tracert –j xxx.xxx.xxx.xxx yyy.yyy.yyy.yyy”

## Slide 24: Tracert -j

## Slide 25: Tracert -j

## Slide 26: Routing table

## Slide 27: IP forwarding
Matching rule: longest-prefix matching
?
=172.30.1.2
m=255.255.255.0 (or /24)
match =172.30.1.0
Try other values of m

## Slide 28: Host processing rules
What if destination IP does not match my interface?
  “Be conservative in what you send, be liberal in what you accept” (Robustness Principle a.k.a. Postel’s Law)
Kill it silently or forward it?
Needs filtering anyway – consider multicast

## Slide 29: IP service characteristics
Connectionless
“Best-effort” service
Datagram: wherever you launch from, you will get to the destination

## Slide 30: IPv6: header

## Slide 31: IPv4 to IPv6
Remove useless fields from IPv4
  Checksum, Fragmentation
Add new fields
  Flow label for QoS – but still no hope
Rename some fields
  TTL  hop count
  Protocol  next header
  Total length  payload length (payload + extention header)
No “options”

## Slide 32: IPv6 header
Version = 6
Traffic class/flow label : QoS…forget it
Next header: demultiplexing

## Slide 33: IPv6 extension headers

## Slide 34: Extension headers

## Slide 35: Options

## Slide 36: Misc.
No ARP in IPv6 world
No IGMP in IPv6 world
They are done by ICMPv6
But the functionalities live!