## Slide 1: Satellite communication

## Slide 2: Now it’s even available to your phone
Without modifying your phone
  5G as such

## Slide 3: Some interesting vision from a novelist
With all due respect to engineers …
Arthur C. Clark (1917 – 2008)
  Postulated the entire concept of international satellite telecommunications from geostationary satellite orbit including coverage, power, services, solar eclipse
    “Extra-Terrestrial Relays”, Wireless World, 1945

## Slide 4: Satellite missions

## Slide 5: GEO, MEO, and LEO

## Slide 6: GEO
Satellites can relay signals over a long distance
Geostationary satellites
  Remain above the equator at a height of about 22300 miles (geosynchronous orbits)
  Travel around the earth in exactly the same time, the earth takes to rotate

## Slide 7: Kepler’s Law and GEO
  T: time for one complete orbit = 24 hours
  G: universal gravitational constant =
  : mass of Earth =
  R: orbital radius (from the center of Earth) = 36,000 km

## Slide 8: LEO
Circular or inclined orbit with < 1400 km altitude
  Satellite travels across sky from horizon to horizon in 5 - 15 minutes  needs handoff
  Earth stations must track satellite
    Phased array antenna
  Large constellation of satellites is needed for continuous communication
    66 satellites needed to cover earth
    42,000 planned by Starlink

## Slide 9: GEO, MEO, and LEO

## Slide 10: GEO, MEO, and LEO

## Slide 11: Types of orbits
Based on the inclination, i, over the equatorial plane:
  Equatorial Orbits above Earth’s equator (i=0°)
  Polar Orbits pass over both poles (i=90°)
  Other orbits called inclined orbits (0°<i<90°)
    E.g. Starlink
Based on eccentricity
  Circular with centre at the earth’s centre
  Elliptical with one foci at earth’s centre

## Slide 12: Inclination and elevation

## Slide 13: Satellite system elements

## Slide 14: Space segment
Satellite launch  Transfer orbit  Deployment  Operation  Retirement

## Slide 15: Communication satellite
A large microwave repeater
Contains several transponders
  Listens to some portion of spectrum
  Amplifies the incoming signal
  Broadcasts it in another frequency to avoid interference with incoming signals (e.g. TV)
Otherwise would require a surreally high tower for trans-atlantic wireless communication

## Slide 16: Use cases
Of communication satellites

## Slide 17: Satellite transmission bands
C band is the most frequently used
Ka and Ku bands are reserved exclusively for satellite communication but are subject to rain attenuation

## Slide 18: Attenuation
Different types of atmospheric losses can disturb radio wave transmission in satellite systems
  Atmospheric absorption
  Atmospheric attenuation
  Traveling ionospheric disturbances

## Slide 19: Atmospheric absorption
Energy absorption by atmospheric gases, which varies with the frequency of the radio waves
Two absorption peaks are observed (for 90º elevation angle):
  22.3 GHz from resonance absorption in water vapour (H2O)
  60 GHz from resonance absorption in oxygen (O2)

## Slide 20: Atmospheric attenuation
Rain is the main cause of atmospheric attenuation
  Hail, ice and snow have little effect on attenuation because of their low water content
  Total attenuation from rain can be determined by the effective path length of the signal through the rain

## Slide 21: Traveling ionospheric disturbances
Traveling ionospheric disturbances are clouds of electrons in the ionosphere that provoke radio signal fluctuations which can only be determined on a statistical basis

## Slide 22: Current developments
480 Starlink satellites testing direct connectivity to smartphones next week
  Texting in 2024  Audio, video, and Internet in 2025
  Threat to Internet and satellite TV industry for rural areas
Base stations (5G gNBs) on satellites planned

## Slide 23: Current developments
Apple + GlobalStar
Starlink, Starlink+T-Mobile

## Slide 24: Current developments
Starlink antennas on Royal Caribbean cruise ship
Ukraine

## Slide 25: Current developments
Starlink plans

## Slide 26: Current developments

## Slide 27: Current developments