## Slide 1: 8.7 Attacks involving ICMP
Three categories: floods, bombs, and information disclosure
  Floods cause a large amount of traffic to be generated, leading to an effective DoS attack on one or more computers
  Bomb (a.k.a. nuke) refers to sending specially constructed messages that cause IP or ICMP processing to crash or hang
  Information disclosure does not typically cause harm by themselves but can be used to inform the approaches used by other attack methods to avoid wasting time or avoid being detected

## Slide 2: 8.7 Attacks involving ICMP
Smurf attack uses ICMPv4 with a broadcast destination address to induce a large number of computers to respond
  Setting the source IP address to the intended victim’s address
  Responses go to the source address in the ICMP message (i.e., the victim’s)
  If this is done rapidly, it can result in a DoS attack
  This attack is easily handled by disallowing incoming directed broadcast traffic at the firewall perimeter

## Slide 3: 8.7 Attacks involving ICMP
Ping of death attack constructs packet fragments in such a way that when they are reassembled, they form an IPv4 datagram that is too large (>> 64KB)
  With ICMPv4 Echo Request/Reply (ping) messages
  This has been used to cause some systems to crash and represents another form of DoS attack
Teardrop attack changes Fragment Offset in IPv4 headers so as to induce errors in the IPv4 fragment reassembly routes

## Slide 4: 8.7 Attacks involving ICMP
Land attack exploits the assumption that an ICMP message would have distinct source and destination addresses
  ICMP message containing a source and destination IP address equal to the victim’s is sent to the victim
  Some implementations react in unfortunate ways when receiving such a message
The ICMP redirect fails to ensure that the message is authentic
  A man-in-the-middle can be inserted along the flow of traffic, which is then recorded and analyzed; similar to ARP poisoning attack
  In addition, it can cause a victim to believe that itself is the preferred gateway to a destination, causing an infinite loop and a consequential lockup of the victim computer

## Slide 5: 8.7 Attacks involving ICMP
ICMP Router Advertisement and Router Solicitation messages can be used to create an attack that somewhat resembles the redirect attack
  These messages can be used to induce victim systems to change their default routes to point to a compromised machine
  In addition, passively receiving these messages can enable an attacker to learn about the topology of the local network environment
ICMP can be used as a communication channel among invading programs that wish to coordinate
  In the TFN (Tribe Flood Network) attack, ICMP is used to coordinate among a group of collaborating viruses after they have compromised computers

## Slide 6: 8.7 Attacks involving ICMP
Smack or bloop attacks
  ICMP Destination Unreachable messages can be used to cause denial of service to currently existing connections (e.g., TCP connections)
  In some implementations, receiving a Host Unreachable, Port Unreachable, or Protocol Unreachable message from an IP address causes all transport-layer connections currently associated with that address to be closed
If an attacker modifies PTB message, it can force an endpoint TCP to run with very small packets (resulting in poor performance)
  This message contains a field indicating the recommended MTU
  This is used by transport protocols such as TCP to pick their packet size.

## Slide 7: 8.7 Attacks involving ICMP
The ICMP Timestamp Request/Reply message (which is not used anymore in normal operations) can be used to learn the time of day according to some host
Because many random numbers are based on the current time of day, revealing a host’s precise notion of the time could be a problem
  An external actor could predict the sequence of pseudo-random numbers used for creating cryptographic keys, possibly allowing a third party to guess otherwise secret values and hijack connections