## Slide 1: Ad hoc and Sensor Networks Chapter 3: Network architecture
Holger Karl

## Slide 2: Goals of this chapter
Having looked at the individual nodes in the previous chapter, we look at general principles and architectures how to put these nodes together to form a meaningful network
We will look at design approaches to both the more conventional ad hoc networks and the non-standard WSNs

## Slide 3: Outline
Network scenarios
Optimization goals
Design principles
Service interface
Gateway concepts

## Slide 4: Basic scenarios: Ad hoc networks
(Mobile) ad hoc scenarios
  Nodes talking to each other
  Nodes talking to “some” node in another network (Web server on the Internet, e.g.)
    Typically requires some connection to the fixed network
  Applications: Traditional data (http, ftp, collaborative apps, …) & multimedia (voice, video) ! humans in the loop
ad hoc
© J. Schiller

## Slide 5: Basic scenarios: sensor networks
Sensor network scenarios
  Sources: Any entity that provides data/measurements
  Sinks: Nodes where information is required
    Belongs to the sensor network as such
    Is an external entity, e.g., a PDA, but directly connected to the WSN
      Main difference: comes and goes, often moves around, …
    Is part of an external network (e.g., internet), somehow connected to the WSN
  Applications: Usually, machine to machine, often limited amounts of data, different notions of importance
Source
Sink
Internet
Sink
Source
Sink
Source

## Slide 6: Single-hop vs. multi-hop networks
One common problem: limited range of wireless communication
  Essentially due to limited transmission power, path loss, obstacles
Option: multi-hop networks
  Send packets to an intermediate node
  Intermediate node forwards packet to its destination
  Store-and-forward multi-hop network
Basic technique applies to both WSN and MANET
Note: Store&forward multi-hopping NOT the only possible solution
  E.g., collaborative networking, network coding
  Do not operate on a per-packet basis
Source
Sink
Obstacle

## Slide 7: Energy efficiency of multi-hopping?
Obvious idea: Multi-hopping is more energy-efficient than direct communication
  Because of path loss  > 2, energy for distance d is reduced from cd to 2c(d/2)
    c some constant
However: This is usually wrong, or at least very over-simplified
  Need to take constant offsets for powering transmitter, receiver into account
  Details see exercise, chapter 2
! Multi-hopping for energy savings needs careful choice

## Slide 8: WSN: Multiple sinks, multiple sources

## Slide 9: Different sources of mobility
Node mobility
  A node participating as source/sink (or destination) or a relay node might move around
  Deliberately, self-propelled or by external force; targeted or at random
  Happens in both WSN and MANET
Sink mobility
  In WSN, a sink that is not part of the WSN might move
  Mobile requester
Event mobility
  In WSN, event that is to be observed moves around (or extends, shrinks)
  Different WSN nodes become “responsible” for surveillance of such an event

## Slide 10: WSN sink mobility
Request
Movement
direction
Propagation
of answers

## Slide 11: WSN event mobility: Track the pink elephant
Here: Frisbee model as example

## Slide 12: Outline
Network scenarios
Optimization goals
Design principles
Service interface
Gateway concepts

## Slide 13: Optimization goal: Quality of Service
In MANET: Usual QoS interpretation
  Throughput/delay/jitter
  High perceived QoS for multimedia applications
In WSN, more complicated
  Event detection/reporting probability
  Event classification error, detection delay
  Probability of missing a periodic report
  Approximation accuracy (e.g, when WSN constructs a temperature map)
  Tracking accuracy (e.g., difference between true and conjectured position of the pink elephant)
Related goal: robustness
  Network should withstand failure of some nodes

## Slide 14: Optimization goal: Energy efficiency
Umbrella term!
Energy per correctly received bit
  Counting all the overheads, in intermediate nodes, etc.
Energy per reported (unique) event
  After all, information is important, not payload bits!
  Typical for WSN
Delay/energy tradeoffs
Network lifetime
  Time to first node failure
  Network half-life (how long until 50% of the nodes died?)
  Time to partition
  Time to loss of coverage
  Time to failure of first event notification

## Slide 15: Optimization goal: Scalability
Network should be operational regardless of number of nodes
  At high efficiency
Typical node numbers difficult to guess
  MANETs: 10s to 100s
  WSNs: 10s to 1000s, maybe more (although few people have seen such a network before…)
Requiring to scale to large node numbers has serious consequences for network architecture
  Might not result in the most efficient solutions for small networks!
  Carefully consider actual application needs before looking for n ! 1 solutions!

## Slide 16: Outline
Network scenarios
Optimization goals
Design principles
Service interface
Gateway concepts

## Slide 17: Distributed organization
Participants in a MANET/WSN should cooperate in organizing the network
  E.g., with respect to medium access, routing, …
  Centralistic approach as alternative usually not feasible – hinders scalability, robustness
Potential shortcomings
  Not clear whether distributed or centralistic organization achieves better energy efficiency (when taking all overheads into account)
Option: “limited centralized” solution
  Elect nodes for local coordination/control
  Perhaps rotate this function over time

## Slide 18: In-network processing
MANETs are supposed to deliver bits from one end to the other
WSNs, on the other end, are expected to provide information, not necessarily original bits
  Gives addition options
  E.g., manipulate or process the data in the network
Main example: aggregation
  Apply composable aggregation functions to a convergecast tree in a network
  Typical functions: minimum, maximum, average, sum, …
  Not amenable functions: median

## Slide 19: In-network processing: Aggregation example
Reduce number of transmitted bits/packets by applying an aggregation function in the network
1
1
3
1
1
6
1
1
1
1
1
1

## Slide 20: In-network processing: signal processing
Depending on application, more sophisticated processing of data can take place within the network
  Example edge detection: locally exchange raw data with neighboring nodes, compute edges, only communicate edge description to far away data sinks
  Example tracking/angle detection of signal source: Conceive of sensor nodes as a distributed microphone array, use it to compute the angle of a single source, only communicate this angle, not all the raw data
Exploit temporal and spatial correlation
  Observed signals might vary only slowly in time ! no need to transmit all data at full rate all the time
  Signals of neighboring nodes are often quite similar ! only try to transmit differences (details a bit complicated, see later)

## Slide 21: Adaptive fidelity
Adapt the effort with which data is exchanged to the currently required accuracy/fidelity
Example event detection
  When there is no event, only very rarely send short “all is well” messages
  When event occurs, increase rate of message exchanges
Example temperature
  When temperature is in acceptable range, only send temperature values at low resolution
  When temperature becomes high, increase resolution and thus message length

## Slide 22: Data centric networking
In typical networks (including ad hoc networks), network transactions are addressed to the identities of specific nodes
  A “node-centric” or “address-centric” networking paradigm
In a redundantly deployed sensor networks, specific source of an event, alarm, etc. might not be important
  Redundancy: e.g., several nodes can observe the same area
Thus: focus networking transactions on the data directly instead of their senders and transmitters ! data-centric networking
  Principal design change

## Slide 23: Implementation options for data-centric networking
Overlay networks & distributed hash tables (DHT)
  Hash table: content-addressable memory
  Retrieve data from an unknown source, like in peer-to-peer networking – with efficient implementation
  Some disparities remain
    Static key in DHT, dynamic changes in WSN
    DHTs typically ignore issues like hop count or distance between nodes when performing a lookup operation
Publish/subscribe
  Different interaction paradigm
  Nodes can publish data, can subscribe to any particular kind of data
  Once data of a certain type has been published, it is delivered to all subscribes
  Subscription and publication are decoupled in time; subscriber and published are agnostic of each other (decoupled in identity)
Databases

## Slide 24: Further design principles
Exploit location information
  Required anyways for many applications; can considerably increase performance
Exploit activity patterns
Exploit heterogeneity
  By construction: nodes of different types in the network
  By evolution: some nodes had to perform more tasks and have less energy left; some nodes received more solar energy than others; …
Cross-layer optimization of protocol stacks for WSN
  Goes against grain of standard networking; but promises big performance gains
  Also applicable to other networks like ad hoc; usually at least worthwhile to consider for most wireless networks

## Slide 25: Outline
Network scenarios
Optimization goals
Design principles
Service interface
Gateway concepts

## Slide 26: Interfaces to protocol stacks
The world’s all-purpose network interface: sockets
  Good for transmitting data from one sender to one receiver
  Not well matched to WSN needs (ok for ad hoc networks)
Expressibility requirements
  Support for simple request/response interactions
  Support for asynchronous event notification
  Different ways for identifying addressee of data
    By location, by observed values, implicitly by some other form of group membership
    By some semantically meaningful form – “room 123”
  Easy accessibility of in-network processing functions
    Formulate complex events – events defined only by several nodes
  Allow to specify accuracy & timeliness requirements
  Access node/network status information (e.g., battery level)
  Security, management functionality, …
No clear standard has emerged yet – many competing, unclear proposals

## Slide 27: Outline
Network scenarios
Optimization goals
Design principles
Service interface
Gateway concepts

## Slide 28: Gateway concepts for WSN/MANET
Gateways are necessary to the Internet for remote access to/from the WSN
  Same is true for ad hoc networks; additional complications due to mobility (change route to the gateway; use different gateways)
  WSN: Additionally bridge the gap between different interaction semantics (data vs. address-centric networking) in the gateway
Gateway needs support for different radios/protocols, …

## Slide 29: WSN to Internet communication
Gateway nodes
Alice‘s desktop
Alice‘s PDA
Alert Alice
Internet
Example: Deliver an alarm message to an Internet host
Issues
  Need to find a gateway (integrates routing & service discovery)
  Choose “best” gateway if several are available
  How to find Alice or Alice’s IP?

## Slide 30: Internet to WSN communication
How to find the right WSN to answer a need?
How to translate from IP protocols to WSN protocols, semantics?
Gateway nodes
Remote requester
Internet
Gateway

## Slide 31: WSN tunneling
Gateway nodes
Internet
Gateway
Use the Internet to “tunnel” WSN packets between two remote WSNs

## Slide 32: Summary
Network architectures for ad hoc networks are – in principle – relatively straightforward and similar to standard networks
  Mobility is compensated for by appropriate protocols, but interaction paradigms don’t change too much
WSNs, on the other hand, look quite different on many levels
  Data-centric paradigm, the need and the possibility to manipulate data as it travels through the network opens new possibilities for protocol design
The following chapters will look at how these ideas are realized by actual protocols