## Slide 1: MARS: A Muscle Activity Recognition System Enabling Self-conﬁguring Musculoskeletal Sensor Networks
IPSN 2013

## Slide 2: Motivation
Muscle injuries are a major problem for athletes
NEEDS: Correct motion & prevent injury
  Non-intrusive
  Scalable (autonomous setup)
  Accurate
Disadvantage of Related Works
  Vision-based: LOS, clothing & skin cover
  Needles: painful, low level activity
  Larger sensors with contact gels: low level activity

## Slide 3: Physiology of Skeletal Muscle
Activating skeletal muscle  resulting in mechanical vibrations
  Oscillations, tremors of the human motor system
  Muscle fibers sliding against each other
  Muscle belly’s circumference increase and decrease
Sensing of Muscles
  Using accelerometer
    Tremors & oscillations: 3.85 Hz ~ 8.8 Hz
    Internal vibration: 10 Hz ~ 40 Hz

## Slide 4: System Overview

## Slide 5: System Architecture
The Sensor Node Network
  Provide error detection checksum
    To preserve the integrity of the data In the MARS system
  Anti-alias filter for the accelerometer
  Wired to mobile data aggregator
    SPI interface, 1Mbps
    10 hours for 2200mAh battery
Notes: Anti-alias filter..나이키스트 샘플링 이론에 의거 샘플링 속도는 측정하고자 하는 신호의 최대 주파수보다 적어도 2배 이상이 되어야 함. 그러나 여타 다른 요소들 때문에 입력주파수보다 더 높은 주파수가 들어오는 경우가 생기고 이는 잘못된 결과를 야기시킬 수 있음. 따라서 low-pass filter등을 이용하여 높은 주파수 영역을 제거해줌

## Slide 6: System Architecture
The Mobile Data Aggregator
  On Yellow Jacket board
    Support 6 sensors & 2.5 meters
  Receive data from all nodes by TDMA
  Decode checksum
  Error control
    Damaged sensors
    Out of sync nodes
     Postpone data sampling until the next cycle
  Wi-Fi to backend server
Notes: 2.5m  to reduce line capacitance

## Slide 7: System Architecture
Backend Server – Muscle Activity Recognition
  How the vibration signatures are obtained?
    10Hz high pass filter:
    Feature extraction
  10Hz high pass filter:
    to isolate the lower freq. components
    avoid signal from tremors
     Tremors & oscillations: 3.85 Hz ~ 8.8 Hz

## Slide 8: System Architecture
Backend Server – Muscle Activity Recognition
  Feature extraction
    The FE calculates a selected set of 21 feature vectors
    6 time domain / 15 freq. domain features
  6 time domain features
    Root Mean Square: related to the intensity of an action
      *A consistent relationship between the standard deviation of accel. data and intensity of movement
      {RMS(x), RMS(y), RMS(z)}  3 features
    Cosine correlation: relation of vibrations at different axes
      {CC(x,y), CC(y,z), CC(x,z)}  3 features
* X. Long, B. Yin, and R. Aarts. Single-accelerometer-based daily physical activity classification. In Engineering in Medicine and Biology Society, 2009. EMBC 2009. Annual International Conference of the IEEE, volume 2009, pages 6107{6110. IEEE, Jan. 2009.
Notes: RMS  실제 실험/관측 결과가 평균적으로 얼마만큼 떨어져 있는지
Cosine correlation  주로 두 백터의 방향성의 일치를 보고자 할 때 사용됨 (문서 등의 비교)
주요 내용은 아니지만 50% overlap sliding window 사용  reference paper에 50%가 가장 좋다는 내용 있음

## Slide 9: System Architecture
Backend Server – Muscle Activity Recognition
  Feature extraction
  15 frequency domain features
    Apply Discrete Fourier Transform (DFT)
    Signal frequency domain entropy
      To help distinction of activities with a similar energy intensity by comparing their periodicities
       to distinguish cyclic and non-cyclic activities
      {entropy(x), entropy(y), entropy(z)}  3 features
    Power Spectral Density (PSD)
      The signal power per window
        Low, Medium, Medium high, High
        The similar freq. domain entropies at different freq. bands can be distinguished
        3 * 4 = 12 features
Notes: Entropy: describes the irregularity, complexity, or unpredictability characteristics of a signal
Frequency domain entropy was computed as the information entropy of the normalized PSD function of the input signal
PSD : 퓨리에(Fourier)변환을 통하여 구한 단위 주파수당 에너지의 분포이다

## Slide 10: System Architecture
Backend Server – Muscle Activity Recognition
  Training Classifiers and Classification
  J48 decision tree (DT) classifier
    C4.5 algorithm

## Slide 11: System Architecture
Backend Server – Motion Tracking & Visualization
  Complimentary filter fusion of sensor data
    Obtain accurate orientations of the sensors
    By quaternion-based complimentary filter
  Range of motion limitation
  Visualization and rendering
    Java & Unity Gaming Engine

## Slide 12: Experiments and Evaluation
Muscle Identity Experiment(Proof of Concept Experiments)
  Power Spectral Densities (PSD) of accelerometer
    Muscle activity can be quantified
    The vibration patterns are different  PSD is unique for different person

## Slide 13: Experiments and Evaluation
User Study Experiment
  4 females & 6 males from different background
  Isolated and compound muscles
  Compare three classifiers
    Naïve Bayes (NB) / Support Vector Machine (SVM) / J48 DT

## Slide 14: Precision & Recall
Precision: positive predictive value
Recall: as sensitivity
Notes: Precision은 컴퓨터의 예측 중, 결과가 나올 것이라 예측한 값 중에 실제 결과가 나온 비율이라고 할 수 있고, Recall은 컴퓨터가 맞다고 검색한 결과 중, 실제 정답의 비율이라고 할 수 있다.

## Slide 15: Experiments and Evaluation
User Study Experiment – Isolation type

## Slide 16: Experiments and Evaluation
User Study Experiment – Compound type

## Slide 17: Experiments and Evaluation
Motion Tracking Setup and Results

## Slide 18: Conclusion
Presenting MARS,
  a novel non-intrusive
  Autonomous setup capable
  Inertial sensor-based muscle identity recognition
  Motion tracking system
Pros,
  ONLY accelerometer
  Typical approach in recognition problem  chance to introduce useful tools!
Cons
  Not enough to explain motion tracking parts

## Slide 19: Backup Slide
Naïve Bayes classifier
  based on applying Bayes' theorem with strong (naive) independence assumptions.
  Using 
Support Vector Machine (SVM) classifier
Notes: X : new feature , Y : class , feature들이 독립이면

## Slide 20: Backup Slide