## Slide 1
DAISY Data Analysis and Information SecuritY Lab
Detecting Driver Phone Use Leveraging
Car Speakers
Presenter: Yingying Chen
Jie Yang†, Simon Sidhom†, Gayathri Chandrasekaran∗ , Tam Vu∗ , Hongbo Liu†,
Nicolae Cecan∗, Yingying Chen†, Marco Gruteser∗, Richard P. Martin∗
†Dept. of ECE, Stevens Institute of Technology
∗ WINLAB, Rutgers University
ACM MobiCom 2011

## Slide 2: Cell Phones Distract Drivers
  Cell phone as a distraction in 2009 on U.S. roadways
  18% of fatalities in distraction-related crashes involved reports of a cell phone
  995 fatalities
  24,000 injuries
Source: “Distracted Driving 2009” National Highway Traffic Safety Administration Traffic Safety Facts, 2009
Talking on Hand-held Cell
Visual — Eyes off road
Cognitive — Mind off driving
Texting on Hand-held Cell
Manu — Hands off wheel
Visual — Eyes off road
Cognitive — Mind off driving
81% of drivers admit to talking on phone while driving
18% of drivers admit to texting while driving

## Slide 3: Cell Phones Distract Drivers
  Do hands-free devices solve the problem?
  Minds off driving.
Real-world accidents indicated that hands-free and handheld users are as likely to be involved in accidents
Cognitive load distract driver!

## Slide 4: Cell Phone Distraction: What’s Being Done?
Law
  Several States ban handheld phone use
Technology
  Hard blocking: radio jammer, blocking phone calls, texting, chat …
  Soft interaction
    Routing incoming calls to voicemail,
    Delaying incoming text notifications
    Automatic reply to callers
Automatic Reply: “I’m driving right now; will get back with you!”

## Slide 5: What’s Being Done? - Is a Cell Phone in a Moving Vehicle ?
  Current Apps that actively prevent cell phone use in vehicle
    ONLY detect the phone is in vehicle or not!
GPS
Handover
Signal Strength
Car’s speedometer

## Slide 6: The Driver-Passenger Challenge
I am a passenger!
I want to make a phone call.
38% of automobile trips include passengers !
Source: National highway traffic safety administration: Fatality analysis reporting system

## Slide 7: Our Basic Idea
An Acoustic Ranging Approach
  No need of dedicated infrastructure
    Car speakers
    Bluetooth
  Classifying on which car seat a phone is being used
    No need for localization or fingerprinting
      Exploiting symmetric positioning of speakers
Symmetric positioning of speakers
Phone connecting with head unit

## Slide 8: How Does It work?
Audio
Head Unit
S1
Left
S2
Right
S3
S4
Time of Arrival - Absolute ranging:
clock synchronization
unknown processing delays
Travel Time: T1
Travel Time: T2
TDOA: T2 – T1
No clock synchronization
Need to distinguish signal from S1 and S2
S1, S2 emit signal simultaneously
Insert a fixed time interval ∆t
between two channels
S1 always come first
S2 always come second
No need of signal identifier!
No interference from different speakers!

## Slide 9: How Does It work?
Audio
Head Unit
∆t1 - ∆t > 0 => Closer to Left Speaker (S1 )
∆t1 - ∆t < 0 => Closer to Right Speaker (S2 )
∆t
∆t1
S1
Left
S2
Right
t1
t2
t’1
t’2
∆t2 - ∆t > 0 => Closer to Front Speaker (S1, S2)
∆t2 - ∆t < 0 => Closer to Back Speaker (S3, S4)
S3
Rear Right
S4
Rear Left
∆t2
- = ?
∆t
∆t1

## Slide 10: Walkthrough of the detection system
Emit beep signal
Record signal
Filtering
Signal Detection
Relative Ranging
∆t1 - ∆t
Location Classification
Driver
v.s.
non-Driver

## Slide 11: Walkthrough of the detection system
Channel 1
Channel 2
∆t
Beep signal: two channels
High frequency beep
  Robust to noise:
    engine, tire/road, conversation, music
  Unobtrusiveness
    Close to human’s hearing limit
Beep Length: 400 samples (i.e., 10 ms)
∆t: 10,000 samples
Emit beep signal
Record signal
Filtering
Signal Detection
Relative Ranging
∆t1 - ∆t
Location Classification
Driver
v.s.
non-Driver
Beep signal design
  Consider two challenges:
    Background noise and unobtrusiveness
Increasing frequency
22 kHz
0
engine, tire/road
1 kHz
300Hz
3.4kHz
conversation
50Hz
15kHz
Music
Beep Frequency Range

## Slide 12: Walkthrough of the detection system
Recorded signal
Signal distortion:
Heavy multipath in-car
Background noise
Reduced microphone sensitivity
Emit beep signal
Record signal
Filtering
Signal Detection
Relative Ranging
∆t1 - ∆t
Location Classification
Driver
v.s.
non-Driver
Where is the beep signal?

## Slide 13: Walkthrough of the detection system
Signal after Filtering
Emit beep signal
Filter out background noise
Noise mainly located below 15kHz
Beep signal frequency is above 15kHz
Emit beep signal
Record signal
Filtering
Relative Ranging
∆t1 - ∆t
Location Classification
Driver
v.s.
non-Driver
STFT Filter
Moving window size m: 32 samples
Beep signal
Signal Detection

## Slide 14: Walkthrough of the detection system
Signal Detection
Threshold td:
Based on noise: μ + 3σ
99.7% confidence level of noise
Robust window W:
Reduce false detection
40 samples
Emit beep signal
Record signal
Filtering
Signal Detection
Relative Ranging
∆t1 - ∆t
Location Classification
Driver
v.s.
non-Driver
Estimate Noise Mean and standard deviation: (μ , σ)
Threshold td
Signal Detected
Robust window
W
Change-point detection
Identifying the first arriving beep signal that deviates from the noise

## Slide 15: Walkthrough of the detection system
∆t: Predefined fixed time interval between two beep sounds
∆t1: Calculated time difference of arrival based on signal detection
∆t1 - ∆t: Relative ranging -> cell phone to two speakers
Time difference ∆t1:
Measured by sample counting
Emit beep signal
Record signal
Filtering
Signal Detection
Relative Ranging
∆t1 - ∆t
Location Classification
Driver
v.s.
non-Driver
∆t1 - ∆t
∆t1 - ∆t

## Slide 16: Walkthrough of the detection system
Emit beep signal
Record signal
Filtering
Signal Detection
Relative Ranging
∆t1 - ∆t
∆t1 - ∆t > 0 => Left Seats
∆t1 - ∆t < 0 => Right Seats
∆t2 - ∆t > 0 => Front Seats
∆t2 - ∆t < 0 => Rear Seats
With two-channel audio system:
With four-channel audio system: relative ranging from the 3rd or/and 4th channels: ∆t2
Location Classification
Driver
v.s.
non-Driver
Driver
v.s.
non-Driver
Driver v.s. Passenger

## Slide 17: Experimental Scenarios
Testing positions
Different number of occupants
Different noise conditions
  Highway Driving
    60MPH + music playing + w/o window opened
    Phones at front seats only
  Stationary
    Varying background noise: idling engine + conversation
Driver’s Control
Area

## Slide 18: Phones and Cars
Phones
Cars
ADP2
Bluetooth radio
16-bit 44.1kHz sampling rate
192 RAM
528MHz MSM7200 processor
Iphone 3G
Bluetooth radio
16-bit 44.1kHz sampling rate
256 RAM
600 MHz Cortex A8processor
Honda Civic Si Coupe
Bluetooth radio
Two channel audio system
two front and two rear speakers
Interior dimension
  Car I: 175 x 183 cm
  Car II: 185x 203cm
Acura sedan

## Slide 19: Results: Driver v.s. Passenger Phone use
Chart: Detection Accuracy
| ADP2,Civic | Iphone 3G, Acura | ADP2,Civic | Iphone 3G, Acura | Highway Driving
Un-calibrated | 95 | 84 | 95 | 87 | 97.5
Calibrated | 96 | 94 | 96 | 92 | 98
Results
4 channel, all seats
2 channel, front seats

## Slide 20: Results: Accuracy at Each Seat
Cup-holder v.s. co-driver left

## Slide 21: Conclusions
Limitations
  Phone is muffled by bag or winter coat
  Driver places the phone on an empty passenger seat
  Probabilistic nature of our approach – not intend for enforcement actions
Enabled a first generation system of detecting driver phone use through a smartphone app
  Practical today in all cars with built-in Bluetooth
  Leveraging car speakers – without additional hardware
  Computationally feasible on off-the-shelf smartphones
Validated the generality of our approach with two kinds of phones and in two different cars
  Classification accuracy of over 90%, and around 95% with some calibrations

## Slide 22
Thank You!
&
Questions
http://personal.stevens.edu/~ychen6/
yingying.chen@stevens.edu
DRIVE
SAFELY
TALK & TEXT LATER