## Slide 1: SNMP Term Project

## Slide 2: Environment Set Up
Set up SNMP on your Linux (virtual machine)
  Search on Google
    Use source code to install SNMP
    Depend on your Linux distribution (Fedora, Ubuntu, Mint, etc.)
    Do not use SNMP version 3
  Execute default SNMP command
    Command example: “snmpwalk –v 2c –c public localhost system”
Reference: http://www.net-snmp.org/wiki/index.php/Tutorials

## Slide 3: Create Custom SMI, MIB
Create your SMI at private branch
  .iso.org.dod.internet.private.’yourSMI’
  Start from .1.3.6.1.4.2 (.1.3.6.1.4.1 assigned to enterprises)
Create your MIB at your SMI branch
  .iso.org.dod.internet.private.’yourSMI’.’yourDeviceMIB’
  Start from .1.3.6.1.4.2.1
Name your SMI and MIB files
  ‘YourLastName’’StudentNumber’-SMI.txt
    ex)GILDONG2016001001-SMI.txt
  ‘YourLastName’’StudentNumber’-MIB.txt
    ex)GILDONG2016001001-MIB.txt

## Slide 4: MIB Requirement
Assume that you will manage your electronic device at your computer
Requirement of your private MIB
  MIB should include at least 5 electronic devices
    ex) refrigerator, air-conditioner, light controller, printer, washing machine, etc.
  Each device should have 5 properties or more
  Use proper data type (integer, string, etc.) to represent each property
You have to explain each item at ‘DESCRIPTION’ part
Reference: http://net-snmp.sourceforge.net/wiki/index.php/TUT:Writing_a_MIB_Module

## Slide 5: Create MIB Agent
Use mib2c command to generate C source code based on your MIB
  Function frame will be generated
Fill each function
Re-configure SNMP source code with your source code
Install SNMP with your agent
Test your MIB
Reference: http://net-snmp.sourceforge.net/wiki/index.php/TUT:Writing_a_Dynamically_Loadable_Object

## Slide 6: Report
Free format
Environment
  Linux distribution with version, SNMP source code version
Explain SNMP – definition, structure, etc.
Your SMI, MIB structure
Explain device and its property
  Each device explanation starts with “real” picture of it
Show results of snmpget, snmpset, snmptranslate, snmpwalk commands on your MIB
  Explain each command and capture of the results
Difficulty & Reference are mandatory

## Slide 7: Q & A
Blackboard discussion page – Term Project Q&A
  Write question related SNMP term project
  All of questions will be shared
  English only
Appropriate/good questions will be handle on April 18th
  OID, SMI, MIB
  Configuration or test(SNMP command) problem
  Virtual machine or Linux installation question is not allowed
  Basic programming question is not allowed (C, editor, sudo, etc.)

## Slide 8: Submission
Submission date: June 22nd
Submit at Blackboard (‘StudentIDNumber’.zip)
  SNMP source code (with SNMP agent)
  SMI, MIB txt file
  Report file – docx(doc) only