## Slide 1: SmartLight: Light-weight 3D Indoor Localization Using a Single LED Lamp
Song Liu, Tian He
University of Minnesota Twin Cities
Presented by Yongseok Jeon

## Slide 2: Motivation
Indoor localization
  Locate objects or people inside a building
  Used for a broad range of applications
    Ex. robot localization, object tracking, UAV indoor navigation
Fig 1. Example of indoor localization

## Slide 3: Motivation
Most of existing indoor localization systems are analog-based
  It can achieve high accuracy with careful calibration in a static environment
    Ex. Time of Fight (ToF), Angle of Arrival (AoA), Received Signal Strength (RSS), etc.
  They suffer performance degradation in dynamic environments
  Analog-based approaches rely on
    The accuracy of model parameters
    The measurements of analog metrics
    Careful system calibration in a controlled environment

## Slide 4: Motivation
Digital approaches
  Make binary decisions on the existence of a signal/observation
  Compared to analog approach,
    Robust to noise
    Requiring minimum calibration overhead
    More reliable

## Slide 5: SmartLight
SmartLight
  A digital 3D indoor localization approach based on LED light
  Exploiting light splitting properties of a convex lens to binary decision
  Asymmetry design
    Shift all the complexity into the transmitter (single LED lamp)
    Minimize the complexity of the receiver (light sensor)

## Slide 6: SmartLight
Digital localization
  Robustness against various factors
    Environmental noise
    Fluctuation of light source intensity
    Receiver orientation
    Disturbance along light propagation paths
Concurrent localization
  Single sender can locate multiple receivers simultaneously
Low-Cost localization
  Prototype system with a COTS projector and cheap light sensor

## Slide 7: Background
Converging(convex) lens
  Transparent material that refracts light rays to form an image
A indicator of how strongly the lens converges light
Fig 2. Convex lens

## Slide 8: Background
Converging(convex) lens (cont’d)
  Lens equation
  Magnification equation
Abbreviation | 
 | Focal length
 | Object distance
 | Image distance
Abbreviation | 
 | Focal length
 | Object distance
 | Image distance
Fig 3. Light ray diagram of image formation

## Slide 9: Background
Visible region
  A cone-shaped region formed by light rays refracting through the lens
  : visible region by pixel
Fig 4. 3D and 2D view of the visible region of a pixel on a light emitting object
Circular shape

## Slide 10: Basic Design
  SmartLight consists of
    SmartLight device
    Light sensors
System setup
Fig 5. Hardware setup of the system

## Slide 11: Basic Design
  SmartLight device consists of
    Square LEDs array panel
      Controlled by a Computer/MCU
    Circular convex lens on top of LEDs
  LED panel consists of pixel
    Each LED pixel can be modulated at different frequency
System setup
Fig 5. Hardware setup of the system

## Slide 12: Basic Design
  Small form factor light senor
    Receives light from a partial set of LED pixels
    Analyses the frequency spectrum of received light signals
    Makes binary decision on whether each frequency signal is received
    Sends back the received frequency components back to SmartLight device
System setup (cont’d)
Fig 5. Hardware setup of the system

## Slide 13: Basic Design
Coordinate system
Z-axis
Y-axis
X-axis
Light sensor
  3D Cartesian coordinate system with the origin at the center of the lens
    X-axis: the upward direction
    Y-axis: the horizontal right direction
    Z-axis: the perpendicular direction away from the lens
Fig 6. Coordinate system of SmartLight

## Slide 14: Basic Design
Key idea of localization
  Light sensor is within the visible region of a few LEDs
  Let be the set of pixels that receives
Fig 7. A light sensor is within the visible region of LED 8 but outside of LED 5

## Slide 15: Basic Design
Key idea of localization (cont’d)
  Since the lens is circular in shape, is also a continuous circular area of pixels on the LED panel
    The circle of grows bigger as moves closer to the lens
    moves upward n the panel as moves vertically downward
Fig 8. A 3D view showing that is a circle of pixels

## Slide 16: Basic Design
Key idea of localization (cont’d)
  The position of can be calculated using the circle of
    , : size and location on the panel
    : size
  The problem of localizing a light sensor at is equivalent to the problem of locating its observable circle of pixels on the LED panel
Fig 8. A 3D view showing that is a circle of pixels

## Slide 17: Basic Design
Key idea of localization (cont’d)
  Locating on the LED panel could be done easily by comparing the frequency signals received at
  In right bitmap, white pixels mean its blinking frequency matches one of the received light frequencies
Fig 9. 2D bitmap graph to visualize

## Slide 18: Basic Design
Calculation of 3D location
  The math formula to calculate the 3D location of light sensor based on the geometrical optical property of the convex lens
    Appendix
Table 1. Symbols used in Equ. 3, 4, 5
Variables

## Slide 19: Advanced Design
Limitation of the basic design
  Using SmartLight in a large workspace
    A number of pixels and unique frequencies are needed
Reduce the required number of frequency!!
  To guarantee the system scalability and efficiency
  At the same time, reliability should be maintained

## Slide 20: Advanced Design
Frequency reuse
  Reduce the total number of frequencies
    Reuse each frequency times (reuse ratio)
  Each pixel is allocated one of the frequencies with a uniform probability

## Slide 21: Advanced Design
Frequency reuse (cont’d)
  Light sensor receives light from only a circular area of pixels
  : the number of unique frequencies that receives
  Some pixels outside of also blink at one of the frequencies that receives
    The probability

## Slide 22: Advanced Design
2D bitmap representation
  To represent LED pixels on the panel, SmartLight uses 2D bitmap array
    Same dimension
    Value “1” (Yes) / “0” (No)
  “1” presents that the corresponding LED blinks at one of the received frequencies in
  “0” otherwise

## Slide 23
Fig 10. Projecting the 2D bitmap into the X and Y direction

## Slide 24: Advanced Design
Main task in frequency reuse
  Find out the circular area of pixels in “ocean” of sparse false positive dots
    Every frequency is randomly reused
    Some pixels could be allocated the same frequency at one of the LEDs in
  Light sensor actually do NOT physically receive the light from the false positive pixels

## Slide 25: Advanced Design
Multi-directional projection
  2D problem of locating a circle into 1D problem of finding a peak
Fig 11. Projection curve about the X direction

## Slide 26: Advanced Design
Multi-directional projection (cont’d)
  Project 2D bitmap onto the X-axis
  Counting the number of “1s” in each vertical column
  The shadow of the circle is apparently located at the peak of the curve
  Then, how to choose circle?
Fig 11. Projection curve about the X direction

## Slide 27: Advanced Design
Multi-directional projection (cont’d)
  To find the peak, use horizontal line is used to intercept the curve
  Consider the intervals bounded by every pair of adjacent intersection points
  The largest intersection interval is used as the peak interval
    Probabilistic mean value of any 1D vector element outside of the circle shadow region
Fig 11. Projection curve about the X direction

## Slide 28: Advanced Design
Multi-directional projection (cont’d)
  Repeat the previous steps once more in the y-axis
Fig 12. Projection curve about the Y direction

## Slide 29: Advanced Design
Multi-directional projection (cont’d)
  To further increase the accuracy,
    Take the average results of repeating the directional projection in different directions
    Repeat the procedures for times by using a different set of random blinking frequencies

## Slide 30: Advanced Design
False detection elimination
  Analyze the effectiveness of using a line to intercept the projection curve
  False positive rate of a single projection
    LED panel: pixels
    : center / radius
    Available frequencies:
      Save
Fig 13. Circle and projection curve

## Slide 31: Advanced Design
False detection elimination (cont’d)
  Each pixel outside of has the probability to be marked white
  Let be a projection curve value
  Then, is a random variable that follows the Gaussian distribution
    Each value on the curve outside of the circle shadow region has a probability to be above its mean value
Fig 13. Circle and projection curve

## Slide 32: Advanced Design
False detection elimination (cont’d)
  The probability of false positive situation where a diameter of is
    Having an intersection interval of length at a certain location outside of the circle shadow region
    Having consecutive Gaussian random variable larger than its mean value
      Ex.
Fig 13. Circle and projection curve

## Slide 33: Advanced Design
False detection elimination (cont’d)
  False positive rate with multiple projection
    By combining the projecting results in an enough number of directions, the probability of a false positive circle is negligible
      False positive intersection interval must be of the same length
      False positive intersection intervals in each direction must be the shadow of the same circle
    The probability of false positive situation where a diameter of is
      Having a continuous circle of false positive white pixels

## Slide 34: Advanced Design
False detection elimination (cont’d)
  False positive rate with multiple projection
    With times repeated procedures (different blinking frequency)
    Ex. /
Fig 14. The probability of having a false positive circle

## Slide 35: Advanced Design
False detection elimination (cont’d)
  Recover from marginal cases
    The case that the shadow region of the circle is separated into two intersections
    White pixels in the shadow region of the circle are not enough
    Strategy?
      Combine long adjacent intersection
        Long false positive intersection interval is rare
      Reduce the standard deviation of pixels outside of

## Slide 36
Fig 15. Example of marginal case, separation in projection curve

## Slide 37: Advanced Design
False detection elimination (cont’d)
  Recover from marginal cases
    The case that the shadow region of the circle is separated into two intersections
    White pixels in the shadow region of the circle are not enough
    Strategy?
      Combine long adjacent intersection
        Long false positive intersection interval is rare
      Reduce the standard deviation of pixels outside of

## Slide 38: Advanced Design
False detection elimination (cont’d)
  Recover from marginal cases
    Reduce the standard deviation of pixels outside of
      Let be the number of white pixels contributed by the circle in separated location
      Let random variable be the number of white dots pixels outside of in the same column
      The probability of the circle shadow divided
Fig 16. CDF of random variable

## Slide 40: Advanced Design
False detection elimination (cont’d)
  Recover from marginal cases
    Reduce the standard deviation of pixels outside of
      Repeat the experiments times and use the mean value
Fig 17. CDF of random variable
Fig 16. CDF of random variable

## Slide 41: Advanced Design
Parallel localization
  SmartLight can localize multiple light sensor simultaneously
    SmartLight treats the received light frequency components of each sensor separately
    Find its circle of pixels by comparing with the blinking frequencies of all LED pixels
Fig 18. Parallelly localize two sensors simultaneously

## Slide 42: System Implementation
Hardware design
  Light projecting device
    LCD computer projector Hitachi cpx1250
      Native resolution of 1024x768
      Refresh rate of 60
    Blinking pattern controller
      Desktop / Labtop
        Nvidia GTX1070, Intel i7-4790, 8GB RAM
        Nvidia GTX1060, Intel i7-7600HQ, 16GB RAM
    Light pattern
      60fps lossless avi video using FFMPEG

## Slide 43: System Implementation
Hardware design (cont’d)
  Receiver end prototype
    Light sensor
      Honeywell SD3410-001 with 1K resistor to the 5V DV of Atmega328 MCU
      Wide sensitivity range and wide acceptance angle (-90’ ~ 90')
    Second version prototype is portable
Fig 20. 2nd version of prototype
Fig 19. 1st version prototype

## Slide 44: System Implementation
Commercialization effort
  Button-sized wearable device “SmartButton” (2nd version of commercialization)
  It can be attached non-intrusively on the human body
Fig 21. 1st (left) and 2nd (right) version of commercial receiver-end design

## Slide 45: System Evaluation
Robustness against
  Environmental noise
  Fluctuation of the light source intensity
  Receiver orientation
  Disturbance along light propagation paths (reflection and attenuation)
Fine granularity and working distance
Impact of the reuse factor , the number of pixels

## Slide 46: System Evaluation
Testbed setup
4.4m x 4m
4m x 4m
10 feet sliding track (3m)
screen pixels
Grouping every nearby screen pixels into one square (grid)
Total number of 172 non-repeating frequency
Fig 22. (a) Testbed environment in the Lab
(b) Testbed environment in an apartment

## Slide 47: System Evaluation
Testbed setup (cont’d)
  Method for comparison
    Implementation of state-of-the-art
      Epsilon (NSDI’ 14)
      Spotlight
      Weighted average
      Coverage method (IPSN’ 14)
Fig 23. 3x3 LEDs Testbed (left) and testbed implementation of the state of the art (right) for comparison

## Slide 48: System Evaluation
Localization accuracy
  Among 5 methods, SmartLight is the only one that requires minimum device calibration
  SmartLight achieves performance with an average around and error of
    Algorithm problem
Fig 24. CDF of location error of different methods

## Slide 49: System Evaluation
Accuracy granularity at different distances
  Error increase with Z-axis distance
    It is not mainly due to the lower SNR at further distances from the projector
    It mainly because testbed setup has a low granularity with the slow hardware
    If is large enough, the degradation in localization granularity at longer distances becomes barely unnoticeable
Fig 25. Testbed with

## Slide 50: System Evaluation
Accuracy granularity at different distances (cont’d)
  The number of screen LCD pixels in the circle of at different distances from the projector
    Ex. A receiver at a distance of form the projector would see screen pixels
Fig 26. Ground truth of the number of pixels in diameter of at different distance

## Slide 51: System Evaluation
Accuracy granularity at different distances (cont’d)
  Ambiguity in Z-axis distance due to a low granularity of the grids
    From previous equations, the interval of increases as decreases
    The granularity of location would be further fine-grained as higher refresh rate and higher resolution projecting hardware are available
  X, Y-axis have similar problem
Fig 27. Granularity of error at different Z distances

## Slide 52: System Evaluation
Simulation on the impact of
  As increase, the projected grid have a finer granularity
  Location accuracy of SmartLight improves with increment of
  Location error interval in estimating Z-axis distance to the projector from to
Fig 28. Simulation: , increasing

## Slide 53: System Evaluation
Simulation on the impact of
  Advanced design uses less than () of unique frequencies to achieve comparable performance in the basic design
  As further increases, the required percentage of unique frequencies further decrease
Fig 29. Simulation:, increasing

## Slide 54: System Evaluation
Impact of ambient noise
  SmartLight is resistant to random ambient noises in real life
    By making binary decisions on the existence of frequencies
    Not their absolute amplitude
  Experiments in Lab with overhead lights and in apartment at different times (distance: )
    Ambient light has no noticeable impact on the performance of SmartLight
Fig 30. Impact of ambient light

## Slide 55: System Evaluation
Impact of signal strength
  Compare the performance of five methods after the signal strength are unexpectedly reduced without recalibrated
    SmartLight and Spotlight’s “ON”-state light illuminance level are halved by using gray scale
    Other methods are halved its emitted power brightness (  )
    SmartLight and Spotlight’s performance are relatively not impacted by the uncalibrated decrease on signal strength
Fig 31. Impact of uncalibrated signal strength change

## Slide 56: System Evaluation
Impact of receiver orientation
  Received light signal strength is directly related to the incidence angle of light
  SmartLight's algorithm localizes the light sensitive area by modeling the traveling paths of light rays instead of the absolute RSS
  The amplitude of the received frequency might be different at different angles, but the binary decision on the received frequency remain the same
Fig 32. Impact of receiver orientation

## Slide 57: System Evaluation
Impact of reflectors
  The reflectors are placed at a distance of near the receiver
    SmartLight and Spotlight performs stably with very little performance degradation
    Both approaches use convex lens to direct light rays so that there are less diffused light
    SmartLight’s algorithm can inherently tolerate some level of false positive pixels
Fig 33. Impact of common reflectors

## Slide 58: System Evaluation
Impact of propagation disturbance
  Localization system based on analog approach incur error from making oversimplified assumption of signal propagation
  Digital approach should be highly robust to disturbances in signal propagation
  Emulate the disturbance by inserting a polarized film on optical path
    Two digital methods perform well
Fig 34. Impact of uncalibrated propagation disturbance

## Slide 59: Conclusion
SmartLight
  A light-based 3D indoor localization design
  Highly robust and accurate model
    No in-situ signal strength attenuation & absolute signal strength
  Works well
    on low refresh rate projector implementation
    in various environments
    in various operational effects
  Indicates the potential of the digital localization can offer

## Slide 60: Critique
+ Probabilistic analysis of design and algorithm
  Calculate the probability of false positive
+ Digital-based approach
  Robust system in even noisy environments
- Low cost (??)
  Performances of SmartLight rely on N or K
  Increment of N or K means increment of cost!!
- Irritating system (??)
  Converging light can interfere people’s action

## Slide 61: Appendix
Converging(convex) lens
  Lens equation
  Magnification equation
Abbreviation | 
 | Focal length
 | Object distance
 | Image distance
Abbreviation | 
 | Focal length
 | Object distance
 | Image distance

## Slide 62: Appendix

## Slide 63: Appendix